### IUPAC Task Group on Atmospheric chemical kinetic Data Evaluation – Data Sheet V.A1.52 HI52

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: February 2008; last change in preferred values: February 2008.

BrONO2 + HBr  (ice surfaces)  Br2 + HNO3

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients:  |  |  |  |
| 6.6x10-3 exp[(700 180)/T] (ice type 1,2) | 180-210 | Aguzzi and Rossi, 2002 | Knudsen-MS (a) |  |

# Comments

- Ice surfaces formed by vapour deposition (type 1) freezing bulk solutions of distilled water either rapidly (type 2) or slowly (type 3), the latter with the intention of forming single-crystalline ice. The temperature dependenceof   listed in the table was obtained by weighted, least squares fitting to tabulated data of Aguzzi and Rossi, 2002.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  | 6.6x10-3exp(700/T) | 180 - 210 |

Reliability

| (E/R) / K | ± 250 | 180 - 210 |
| --- | --- | --- |

##### Comments on Preferred Values

There is only one study of the uptake of BrONO2 to ice in the presence of HBr. At the high initial levels of HBr on the surface used in this study (> 1016 cm-2), the major product was Br2. As surface HBr was depleted, HOBr was also observed in the gas-phase. Note that the uptake coefficients in the presence of HBr are essentially the same as on pure ice so that no dependence of the overall uptake coefficient on HBr concentrations is anticipated.

# References

Aguzzi, A. and Rossi, M. J.: J. Phys. Chem. A 106, 5891-5901, 2002.