### IUPAC Task Group on Atmospheric Chemical kinetic Data Evaluation – Data Sheet V.A1.50 HI50

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Subcommittee for Gas Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: February 2008; last change in preferred values: February 2008.

BrONO2 + H2O  (ice surfaces)  HOBr + HNO3

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients:  |  |  |  |
| > 0.3 | 200  10 | Hanson and Ravishankara, 1993 | CWFT-CIMS (a) |  |
| 0.25  0.07 | 190 | Allanic et al., 1997 | Knudsen-MS (b) |  |
| 0.33  0.10 | 200 |  |  |  |
| 1.08x10-3 exp[(1040 130)/T] (ice type 1) | 180-210 | Aguzzi and Rossi, 2002 | Knudsen-MS (c) |  |
| 5.32x10-4exp[(1125 130)/T] (ice type 2) |  |  |  |  |
| 1.16x10-9exp[(3540 130)/T] (ice type 3) |  |  |  |  |

# Comments

- Ice surface prepared by vapour deposition and the geometric surface area was used to calculate the uptake coefficient. The formation of HOBr was observed as gas-phase product of the surface hydrolysis of BrONO2. and displayed the same kinetics as BrONO2 loss.

- 20 m thick ice film made by vapour deposition and located in a Knudsen reactor operated in either continuous flow or pulsed mode. Uptake coefficients reported were from pulsed experiments which suffered less from an interference by Br2O (formed by the reaction of BrONO2 with HOBr). At the prevailing BrONO2 concentrations ( 11011 molecule cm-3) and reaction times, no passivation of the ice surface was observed and HOBr formation was prompt.

- Ice surfaces formed by vapour deposition (type 1) freezing bulk solutions of distilled water either rapidly (type 2) or slowly (type 3), the latter with the intention of forming single-crystalline ice. The temperature dependencies listed in the table were obtained by weighted, least squares fitting to tabulated data of Aguzzi and Rossi, 2002.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  | 5.3x10-4exp(1100/T) | 180 - 210 |

Reliability

| (E/R) / K | ± 250 | 210 - 250 |
| --- | --- | --- |

##### Comments on Preferred Values

There is good agreement between the various groups (and different methods) on the uptake coefficient at 190 and 200 K. All studies agree that the reaction of BrONO2 on an ice surface proceeds efficiently to form HOBr, which can be released into the gas-phase. The co-product, HNO3, was not detected in these studies.

The most comprehensive dataset of Aguzzi et al. (2002) shows that the uptake coefficient on morphologically different ice surfaces displayed a negative dependence on temperature, indicative of a precursor mechanism in which a H2OBr+·NO3- complex is formed (Gane et al., 2001; McNamara and Hillier, 2001) prior to dissociation to HOBr and HNO3. The preferred expression for the temperature dependent uptake coefficient is that obtained by Aguzzi and Rossi (2002) obtained using ice films of type 2 (presumably polycrystalline).  The assumption that the geometric surface area is equal to that available for reaction should be good for this surface and the temperature dependence is rounded down slightly. The considerably steeper temperature dependence obtained using “single crystal” ice leads to a much lower value of the uptake coefficient at higher temperatures (factor of  5), though the agreement with the type 1 and type 2 ices at 190 K is satisfactory.  The yield of HOBr released to the gas-phase was close to 100 % at 200 and 210 K, decreasing to 10-20 % at  lower temperatures. The “lost” HOBr was released to the gas phase when the ice film was subsequently warmed. The rate of HOBr release was reduced in the presence of nitric acid on the surface. This observation could be attributed to the reduction in surface H2O or enhanced stabilisation of the complex when high levels of surface nitrate are present. The uptake coefficient was however found to be independent of HNO3 adsorbed onto the ice, enabling a simple parameterisation .

# References

Aguzzi, A. and Rossi, M. J.: J. Phys. Chem. A 106, 5891-5901, 2002.

Allanic, A., Oppliger, R. and Rossi, M. J.: J. Geophys. Res. 102, 23529-23541, 1997.

Gane, M. P., Williams, N. A. and Sodeau, J. R.: J. Phys. Chem. A 105, 4002-4009, 2001.

Hanson, D. R. and Raivshankara, A. R. Reactions of halogen species on ice surfaces. In The tropospheric chemistry of ozone in the polar regions; Niki, H., Becker, K. H., Eds.; Springer-Verlag, Berlin-Heidelberg:, 1993.

McNamara, J. P. and Hillier, I. H.: J. Phys. Chem. A 105, 7011-7024, 2001.

# Text boxes

Uptake coefficients for BrONO2 + ice. Solid lines are Arrhenius-type fits to the three data sets of Aguzzi et al. (2002).