IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet CGI_15

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This datasheet last evaluated: May 2020; last change in preferred values: May 2020

CH3CHOO (Z- and E-) + SO2 ( products

## Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| k(Z-) = (2.4 ± 0.3)  10-11 | 298 | Taatjes et al., 2013 | PLP-PIMS (a) |
| k(E-) = (6.7 ± 1.0)  10-11 | 298 |  |  |
| k(Z-) = (2.9 ± 0.3)  10-11 | 293 | Sheps et al., 2014 | PLP-CEUVA (b) |
| k(E-) = (2.2 ± 0.2)  10-10 | 293 |  |  |
| (2.0 ± 0.3)  10-11 | 295 | Smith et al., 2014 | PLP-CEUVA (c) |
| (1.7 ± 0.3)  10-11 | 295 | Howes et al., 2018 | PLP-PIMS (d) |
| k(Z-) = (2.5 ± 0.2)  10-11 | 298 | Zhou et al., 2019 | PLP-LIF (HO product) (e) |

##### Comments

- CH3CHOO was produced by the reaction of CH3CHI + O2. CH3CHI was generated by 248-nm laser photolysis of 1,1-diiodoethane, CH3CH2I2, at 298 K and 4 Torr, in a large excess of O2.  The reacting mixture was monitored by PIMS. Both Z- and E- conformers of CH3CHOO are produced, which could be distinguished by the difference in their ionisation energies. It was demonstrated that E-CH3CHOO is substantially more reactive toward SO2 than is Z-CH3CHOO. SO3 production was observed, with a rise–time correlated with the decay-time of CH3CHOO, showing it to be a primary product of the reaction. The first order decay of Z- and E-CH3CHOO in the presence of excess SO2 was measured. Linear fits to the first order decay constants vs. [SO2] plots were used to determine k(Z-) and k(E-) for Z- and E-CH3CHOO, respectively.

- CH3CHOO prepared by PLP (266 nm) of CH3CHI2 in O2/Ar mixtures at 5 - 20 Torr pressure. CH3CHOO kinetics observed by recording the time-resolved UV absorption spectrum in the region 300 – 450 nm, corresponding to the B̃ (1A′) ← X̃(1A′) electronic transition.  IO (formed from secondary chemistry) was also detected. Absorption features due to Z- and E- conformers of CH3CHOO could be distinguished by their differing reactivities, reflected in their characteristic time dependencies, allowing conformer-specific rate coefficients to be determined. The pseudo-first order decay plots in presence of varying excess [SO2] gave the cited values of k(Z-) and k(E-) for Z- and E-CH3CHOO.

- CH3CHOO prepared by PLP (266 nm) of CH3CHI2 in O2/Ar mixtures and measured by wavelength-resolved transient absorption in a flow cell at 295 K and 15–100 Torr pressure (N2). k was determined from plots of first order decay constant vs. [SO2]. The absorption data quality did not allow distinction between the reactivity of Z- and E-conformers, but earlier work of Taatjes et al. (Z-:E- = 9:1) and Sheps et al. (Z-:E- = 3:1) suggests that the Z- conformer is dominant.

- CH3CHOO generated by 248 nm laser photolysis of CH3CHI2 in the presence of O2. The PIMS system used in this study was unable to differentiate between the reactivity of Z- and E-conformers of CH3CHOO, but earlier work of Taatjes et al. (Z-:E- = 9:1) and Sheps et al. (Z-:E- = 3:1) suggests that the Z- conformer is dominant.

- CH3CHOO produced from 248 nm laser photolysis of CH3CHI2 in the presence of O2, at 298 K at pressures in the range 10-100 Torr (Ar). The decay kinetics of Z-CH3CHOO (k(Z-)) were monitored using HO as a marker species (LIF), making the assumption that the observed formation of HO is due to the thermal decomposition of Z-CH3CHOO, with [HO] controlled by its rapid removal in the system (e.g. via reaction with CH3CHI2). Experiments were carried out under pseudo-first order conditions in the presence of excess [SO2]. The tabulated value of k(Z-) was determined from the dependence of the first-order decay constant on [SO2].

##### Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| k(Z-)/cm3 molecule-1 s-1 | 2.6  10-11 | 298 |
| k(E-)/cm3 molecule-1 s-1 | 1.4  10-10 | 298 |

Reliability

|  log k(Z-) | ± 0.1 | 298 |
| --- | --- | --- |
|  log k(E-) | ± 0.3 | 298 |

- Comments on Preferred Values

- CH3CHOO has two possible conformers: E- and Z-CH3CHOO, which differ in the orientation of the C-O-O group. This leads to conformer-dependent reactivity. Computational studies indicate that Z-CH3CHOO is significantly less reactive than E-CH3CHOO towards, e.g. H2O (Anglada et al., 2011). Calculations place the Z- conformer ~15 kJ mol−1 lower in energy than E- CH3CHOO (Kuwata et al., 2010), reflecting the zwitterionic character of the C–O bond. The barrier to interconversion of these conformers is substantial, ~160 kJ mol−1, and consequently Z- and E-CH3CHOO act as distinct chemical species at atmospheric temperatures.

- The five studies of the reaction with SO2 used the same source of acetaldehyde oxide, i.e. reaction of CH3CHI with O2, which produces both conformers of CH3CHOO together with iodine atoms. The signal:noise characteristics of the spectra needed to define conformer differences is marginal so the parameter distinction is not well defined in the case of acetaldehyde oxide. Moreover, there is uncertainty in the relative amounts of the two conformers formed in the source chemistry. Nevertheless, the results for the rate coefficient for reaction of predominantly Z-CH3CHOO with SO2 are in good agreement, considering the uncertainties (quoted error limits were 1). The result of Sheps et al. (2014) for k(E-) is a factor of ~3 higher than that obtained by Taatjes et al. (2013), and both determinations are significantly larger than their determinations of k(Z-), and that of Zhou et al. (2019). The difference between these rate coefficients probably reflects the sensitivity and selectivity of the detection techniques; the decay data for E-CH3CHOO using the UV spectroscopy method appears superior in quality to the PIMS but there is some uncertainty in the relative UV cross sections and initial yields of the two conformers, both of which are required to extract conformer-specific rate coefficients. The observed higher reactivity of the E-CH3CHOO is consistent with theoretical predictions for the reactivity of the two conformers referred to above, and the preferred value of k(E-) is the mean of the two reported values, which carries an uncertainty of a factor of 2. The preferred value of k(Z-) is based on an unweighted mean of the determinations of Taatjes et al. (2013), Sheps et al. (2014) and Zhou et al. (2019), which are in good agreement.

- Quantum chemical studies predict that the reactions of the CH3CHOO conformers with SO2 proceed via initial barrierless formation of chemically-activated cyclic secondary ozonides (Vereecken et al. 2012). As discussed for the CH2OO + SO2 reaction (data sheet CGI_1), the chemically-activated C2 secondary ozonides are expected to isomerise and decompose mainly to form CH3CHO + SO3, and this is consistent with the results of direct kinetics studies at low pressures (Taatjes et al., 2013; Howes et al., 2018). At higher pressures, collisional stabilization of the secondary ozonides may be important (Vereecken et al. 2012), and further studies are required to characterize their onward reactions. Until additional theoretical and quantitative experimental product channel data become available, we recommend that the reaction predominantly forms CH3CHO and SO3.

References

Anglada, J. M., González, J. and Torrent-Sucarrat, M.: Phys., Chem. Chem. Phys. 13, 13034, 2011.

Kuwata, K. T., Hermes, M. R., Carlson, M. J. and Zogg, C. K.: J. Phys. Chem. A, 114, 9192, 2010.

Sheps, L., Scully, A. M., and Au, K.: Phys. Chem. Chem. Phys., 16, 19941, 2014.

Smith, M. C., Ting, W. L., Chang, C. H., Takahashi, K., Boering, K. A. and Lin, J. J. M.: J. Chem. Phys., 141, 074302, 2014.

Howes, N. U. M., Mir, Z. S., Blitz, M. A., Hardman, S., Lewis, T. R., Stone, D., and Seakins, P. W., Phys. Chem. Chem. Phys., 20, 22218, 2018.

Taatjes, C. A., Welz, O.; Eskola, A. J., Savee, J. D., Scheer, A. M., Shallcross, D. E., Rotavera, B., Lee, E. P. F., Dyke, J. M., Mok, D. K. W., Osborn, D. L., and Percival, C. J.: Science, 340, 177, 2013.

Vereecken, L., Harder, H. and Novelli, A.: Phys. Chem. Chem. Phys., 14, 14682, 2012.

Zhou, X., Liu, Y., Dong, W. and Yang, X.: J. Phys. Chem. Lett., 10(17), 4817, 2019.