# IUPAC Task Group on Atmospheric chemical Kinetic Data Evaluation – Data Sheet VI.A4.15 HET_SL_15

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: July 2012; last change in preferred values: July 2012.

ClO + H2SO4 (l) → products

Experimental data

| Parameter | [H2SO4] /wt % | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- |
| Uptake coefficients:  |  |  |  |  |
| (2.01) × 10-5 | 90 | 295 | Martin et al., 1980 | CWFT-EPR (a) |
| (1.51) × 10-4 | 85 | 260 |  |  |
| (2.21) × 10-4 | 80 | 240 |  |  |
| <1.0 × 10-4 | 60-70 | 213 | Abbatt, 1996 | CWFT-RF (b) |

Comments

(a)	Measurement of the uptake kinetics in a fast flow tube with EPR detection of ClO. Pure Cl2 at 0.67 mbar was discharged in a -wave cavity and combined downstream with an excess of O3 in order to generate ClO.  The quartz flow tube was coated with halocarbon wax and the discharge tube with solid B2O3 in order to minimize wall losses of ClO. The inside of the flow tube was coated with H2SO4 and the H2O vapor pressure was held constant throughout the temperature range at 6.7x10-4 mbar leading to a changing composition of the H2SO4/H2O mixture as the temperature was changed (96% at 300K, 80% at 240K).

(b)	Uptake rates measured in a coated wall flow tube at 1.3 mbar total pressure of He coupled to a resonance fluorescence (RF) detector after chemical conversion. ClO was generated from the reaction Cl + O3 → ClO + O2 by discharging Cl2/He in a microwave cavity and adding O3 downstream at typical [O3] in the range from 1 to 3 x 1013 molecule cm-3. After ClO interacted with the active surface it was converted to Cl in the reaction ClO + NO → Cl + NO2 which was detected using a RF-excited Cl2/He lamp emitting in the VUV at 119 nm in conjunction with a flowing O2 filter. The sensitivit of the RF lamp was measured using the reaction H + Cl2 → HCl + Cl. The ClO concentrations used in this work were on the order of 1 to 2 x 1011 molecule cm-3.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  | No recommendation |  |

Comments on Preferred Values

In the work of Martin et al. (1980) no separation between the effects of changing composition of the cryogenic phase (considered to be negligible) and the temperature dependence of  was performed.  All kinetic results were obtained from the full numerical integration of the parabolic flow system including axial diffusion and resulted in a pronounced negative temperature dependence of the uptake coefficient ss.  The unexpected product of the heterogeneous reaction was HCl and no effect of irradiation by simulated sunlight on  was found within a ± 20% variation of . Martin et al. (1980) report a higher sensitivity for ClO-detection compared to Abbatt (1996). In the light of the disagreement between the two datasets we make no recommendations, but note that uptake of ClO to H2SO4 at stratospheric temperatures and composition is inefficient.

References

Martin, L.R., Judeikis, H.S., Wun, M.: J. Geophys. Res. 85, 5511-5518, 1980.

Abbatt, J.P.D.: Geophys. Res. Lett. 23, 1681-1684, 1996.