IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A2.10 HET_SALTS_10

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet evaluated: 15th January 2009; last change in preferred values: 15th January 2009.

ClONO2 + Cl-/Br-  Cl2/ClBr + HNO3

# Experimental data

| Parameter | [X]/ M | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- |
| Uptake coefficients: ,ss,0 |  |  |  |  |
|  = 0.0244±0.0023 | 0.1M NaCl | 274.6 | Dieber et al, 2004 | DFT-MS (a) |
|  = 0.041±0.0067  = 0.046±0.0019  = 0.047±0.0011 | 0.01M NaBr | 274.1 277 280.8 |  |  |
|  = 0.044±0.0027  = 0.041±0.0043 | 0.025M NaBr | 274.3 276.2 |  |  |
|  = 0.055±0.0060  = 0.054±0.0039  = 0.053±0.0028 | 0.05M NaBr | 274 277 281 |  |  |
|  = 0.057±0.0048  = 0.049±0.0024  = 0.056±0.0008 | 0.10M NaBr | 274.9 276.2 279.9 |  |  |
|  = 0.0655±0.0015  = 0.0663±0.0011 | 0.5M NaBr | 274.4 276.5 |  |  |
|  = 0.073±0.0106 | 1.0M NaBr |  |  |  |

# Comments

- Uptake rates measured onto 200mm droplets following loss of reactant in conventional droplet train apparatus. Droplet temperature controlled by evaporative cooling with adjustment of p(H2O). Uptake coefficient determined with a simple correction for diffusion effects.  g measured as function of [NaCl] and [NaBr].  On NaCl g was not significantly larger than on pure water, but Cl2 was observed as a unique gas-phase product.  On  NaBr droplets  increased with increasing [Br-] and was essentially independent of temperature over the small range investigated for all [Br-]. Both BrCl and Br2 were detected as gas phase products.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| αb | 0.108 | 273-290 |
| HkII (M1/2 atm-1s-1/2) (Br-) | 1.0 x 106 | 273-290 |

Reliability

|  log (α) | ± 0.2 | 273-290 |
| --- | --- | --- |
|  log (HkII) | ±0.15 | 273-290 |

Comments on Preferred Values

The cited work is the only study of reactive uptake of ClONO2 on aqueous halide substrates NaCl and NaBr; all the other reported studies used either solid substrates (ice) or sulphuric acid solutions. These studies showed that uptake led to XCl (X= Cl or Br) and HNO3 formation.  The dihalogens can partition to the gas phase, depending on their solubilty.  No gas phase products were observed from uptake on water droplets due to the high solubilty of the products.

The measured uptake coefficient on NaCl was not significantly greater than on pure water droplets (see data sheet for ClONO2 + H2O, VI.A2.16). However it is expected that Cl2 rather than HOCl will be formed as products.  When Br- was present in solution,  increased with increasing [Br-] and was independent of temperature over the small range investigated for all [Br-].  This was interpreted in terms of the resistance model with increasing liquid phase reaction rate of ClONO2(aq) due to reaction with Br- allowing accommodatopn controlled uptake at high [Br-];

where kI (s-1) =  kII  x [Br-]aq (M)

This allowed evaluation of the reactive uptake parameters for uptake on Br- containing solutions at 274.5 K: ab = (0.108 ± 0.011) and the product HkII = 1.0x 106 M1/2 atm-1s-1/2  from a plot of uptake coefficients corrected for gas phase diffusion effects (1/ - (1/ diff), vs 1/[NaBr]1/2, according to the resistance model with Dl assumed to be 5 x 10-6 cm2s-1.. The recommended uptake parameters are based on this analysis. There are no reported values of H or Dl for ClONO2.

# References

Deiber, G.; George, Ch.; le Calve, S.; Schweitzer, F.; Mirabel, Ph., Atm. Chem.Phys., 4(5),  1291-1299 , (2004).