# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A4.7 HSTD7

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: August 2009; last change in preferred values: August 2009.

ClONO2 + H2O (SAT) → HNO3 + HOCl

Uptake coefficient data

| Parameter | Temp/K | Reference | Comment |
| --- | --- | --- | --- |
| Uptake Coefficients( ClONO2) |  |  |  |
| 2.0 x 10-3 (RH = 90%) 2.0 x 10-3 (RH = 30%) 5.0 x 10-4 (RH = 16%) 1.0 x 10-4 (RH = 7%) | 191.5 196 200 205 | Hanson and Ravishankara, 1993 | CWFT-CIMS(a) |
| 0.016±0.4 (RH = 100%) 5.6 x 10-3 (RH = 72%)* 2 x 103 (RH = 36%)* 9 x 10-4 (RH = 18%)* (5.0±1.3) x 10-4 8% RH 0.02 (RH = 100%)* 4 x 10-3 (RH = 52%)* 1.5 x 10-3 (RH = 28%)* 0.85 x 10-3 (RH = 13%)* | 195 195 195 195 195 192 196 200 205 | Zhang, Jayne and Molina, 1994 | CWFT-EIMS(b) |
| <1.0 x 10-4 | 200-220 | Zhang, Leu and Keyser, 1995 | CWFT-CIMS(c) |

Comments

(a)	Solid film of sulphuric acid ≥ 0.1 mm thickness made from freezing a liquid solution of composition corresponding to SAT (57.5% H2SO4/H2O) on the inside of the flow tube wall to 195K. The cryogenic deposits were characterized by their vapour pressure of H2O monitored by an ion-molecule reaction with F2-. The results were obtained as a function of relative humidity in the range 10 to 90%, obtained by using a fixed p(H2O) ~3.3 x104 mbar and varying the temperature  from 192 - 205 K. p(ClONO2) = (1.3 to 7 x10-7) mbar.  Uptake slower than onto liquid sulphuric acid surfaces.

(b)	Solid film of sulphuric acid ≥ 0.1 mm thickness made from freezing a liquid solution of composition corresponding to SAT (57.5% H2SO4/H2O) on the inside of the flow tube wall to <200 K.  The thermodynamic state of the SAT sample was controlled by setting the vapour pressure of H2O, either H2O-rich (approaching 100% rh) or H2SO4-rich at constant temperature or selecting the temperature at constant p(H2O). The p(H2O) for the cited data are given in terms of relative humidity expressed relative to p(H2O) for pure ice at the experimental temperature. Data marked* were extracted from graphs. The dependence of  on PH2O (Torr) and on temperature (K) was expressed in parametric form: log =10.12 + 5.75logP + 0.62log2P for T=195K, [P= p(H2O)]]; p(ClONO2) = 3 to 5x108 Torr, p(H2O) = 4x10-5 to 5.6x10-4 Torr; log  = 318.67 - 3.13logT + 0.0076log2T for T in the range 192-206K, p(ClONO2) = 2 to 4x10-8 Torr and p(H2O)=3.4x10-4 Torr.

(c)	Uptake experiment on solid sulphuric acid monohydrate (H2SO4•H2O, SAM) using a fast flow tube reactor coupled either to MS (most data) or CIMS.  The thickness of the crystalline SAM films was approximately 0.1 mm, p(H2O) = (1.3 - 5.2)  10-4 mbar at 220-240 K.  ClONO2 uptake was much slower than onto liquid sulphuric acid surfaces.

Preferred values

| parameter | value | Temp/K |
| --- | --- | --- |
|  | 1 x 10-4 + 4 x 10-5 RH + 4.7 x 10-7 RH2 | 195 – 205 |

RH = p(H2O)/p(ice)

Reliability

| (log ) | 0.3 | 195 - 205 |
| --- | --- | --- |

Comments on Preferred Values

Uptake of ClONO2 on solid sulphuric acid films is followed by rapid reaction with H2O to form HOCl and HNO3 in a surface reaction. HOCl partitions into the gas phase, but HNO3 can remain on the surface. The two studies on SAT show that uptake is slower than on liquid sulphuric acid and is a strong function of relative humidity. Thus the uptake coefficient depends on the thermodynamic state of the surface.  The  values of Hanson and Ravishankara are significantly lower than the more extensive data of Zhang et al (1994), especially at low RH.  The  value of Zhang et al. (1993) for H2O-rich SAT (>90% RH) is intermediate between that observed for ice (0.08±0.02) and H2O-rich NAT (~0.002). At lower p(H2O) and higher temperatures the reaction becomes very slow, although there is some indication that  on H2O-rich SAT increases with decreasing temperature.  The origin of the apparent discrepancy in the two studies at low RH is unclear.  Hanson and Ravishankara reported time-dependent  characteristic of inhibition of uptake by surface HNO3, whilst Zhang et al. (1994) report  constant with exposure time.

The IUPAC recommended parameterisation for hydrolysis of ClONO2 on ice surfaces used a Langmuir-Hinshelwood model. Application of this model to solid sulphuric acid films requires the surface concentration of water molecules [H2O]s to be defined.  If [H2O]s is related directly to p(H2O) (i.e low coverage of available H2O molecules) LH should be linearly dependent on RH ( or p(H2O) at a fixed temperature). The experimental  values of Zhang et al. at 195 K show higher order dependence on RH, indicating a more complex model is needed. Note that if surface saturation at high RH occurs the opposite trend would result.

The recommended expression for ClONO2 is a second order polynomial fit as a function of relative humidity to results of Zhang et al. (1994) over the temperature range 191.5 to 205 K. An alternate parameterisation based on the Langmuir-Hinshelwood model fit to the data for 195K :

where  s = 1 and A = (1.68±0.22) x 104. This gives a reasonable representation of the uptake coefficient at RH < 60% but underestimates the uptake coefficient 100% RH.  The factor A in theLH part of the expression contains usual c, ks and KLinC terms for ClONO2, as well as the conversion between [H2O]s (molecule cm-2) and relative humidity (i.e. p(H2O)/p(ice) [= 7.4 x 10-4 mbar at 195K). The temperature dependence of these terms is needed if the expression is applied to other temperatures.

References

Hanson, D.R. and Ravishankara, A.R.: J. Geophys. Res. 98, 22931 (1993).

Leu, M.-T., Moore, S.B. and Keyser, L.F.: J. Phys. Chem. 95, 7763 (1991).

Zhang, R., J. T. Jayne and Molina, M.J.: J.Phys. Chem. 98, 867 (1994).