### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.45 HI45

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet updated: 17th October 2007.

ClONO2 + HBr (ice) → HONO2 + BrCl

Uptake coefficient data

| Parameter | Temp/K | Reference | Comment |
| --- | --- | --- | --- |
| Uptake coefficients for ClONO2 |  |  |  |
| ss ≥ 0.3 | 201 | Hanson and Ravishankara, 1992 | CWFT-CIMS(a) |
| ss = 0.56±.0.11 | 180-200 | Allanic et al, 2000 | Knud-MS(b) |

Comments

(a) Ice layers 2-10 m thick were condensed from the vapor phase. An efficient reaction with ss ≥ 0.3 was observed on pure ice, HNO3-treated ice and on cold Pyrex at 50% r.h., where  scales with the amount of adsorbed HBr..  No difference in reactivity was found between pure ice and HNO3-treated ice.  Significant diffusion  corrections had to be made using calculated diffusion coefficients for ClONO2 in He.

(b) The ice samples were generated from vapor phase deposition. Fast secondary interfacial reactions prevent the observation of the expected primary product BrCl.

Preferred values

| Parameter | Value | T/K |
| --- | --- | --- |
| ERClONO2) | 0.56 | 180 – 200 |
| sClONO2) | gER (ClONO2) x qHBr | 180 – 200 |
| qHBr | 4.14 x 10-10[HBr]0.88 at 188 K | 180 - 200 |

[HBr] in molecule cm-3.

Reliability

| ER | ±0.2 | 185 – 210 K. |
| --- | --- | --- |

Comments on Preferred Values

Heterogeneous reaction of ClONO2 with HBr occurs rapidly on ice surfaces at temperatures relevant for the UTLS. BrCl is a likely product of this reaction, but has not been observed in the gas phase due to secondary reactions (Allanic et al, 1997).  Both cited studies were at temperatures and HBr concentrations corresponding to stability regions of the phase diagram for HBr hydrate (Chu and Chu, 1998). Under these conditions with pHBr > pClNO3 , the reactive uptake coefficient was practically independent of  temperature and pHBr, except on pyrex when g increased with [HBr]. The Knudsen cell results (Oppliger et al, 1997) which do not require correction for gas phase diffusion form the basis of our recommendation for g0.

Carslaw and Peter (1997) described the reaction rate for ClONO2 + HX and related stratospheric reactions on ice particles in terms of surface coverage of HX, using a modified Langmuir-Hinshelwood model. As for the ClONO2 + HCl reaction the reactive uptake coefficient of ClONO2 as a function of [HBr]g is given by the product of 0 and the dimensionless surface coverage of HBr. i.e assuming an Ely-Rideal type mechanism.  HBr adsorption doesn’t follow a Langmuir model under the laboratory experimental conditions used (see data sheet for HBr + ice). The recommended expression for the reactive uptake coefficient at 188 K uses the current IUPAC recommended parameterisation for qHBr = 4.14 x10-10 [HBr]0.88at this temperature. This is only valid for surface coverages up to qHBr  =  1, calculated with this isotherm.

Values given by this parameterisation for pHBr < 10-7 Torr at 188 K are shown on Fig 1.

References

Allanic, A., Oppliger, R., van den Bergh, H. and Rossi, M.J.: Zeitschr. f. Phys. Chem. 214, 1479 (2000).

Chu, L.T. and Chu, L.: J. Phys. Chem. A 103, 384 (1999).

Carslaw, K. S., and Peter, Th., Geophys.Res.Lett., 24, 1743, (1997).

Hanson, D.R. and Ravishankara, A.R.: J. Phys. Chem. 96, 9441 (1992).

Figure 1. The recommended parameterization for P(HBr) dependence of the uptake coefficient of ClONO2 on ice in the presence of HBr.

Fig 1