IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A4.8 HSTD8

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: August 2008; last change in preferred values: August 2008.

ClONO2 + HCl (SAT) → HNO3 + Cl2

Uptake coefficient data

| Parameter | Temp/K | Reference | Comment |
| --- | --- | --- | --- |
| Uptake Coefficients( ClONO2) |  |  |  |
| 0.125 100% RH 2.4 x 10-4 8% RH | 192 205 | Hanson and Ravishankara, 1993 | CWFT-CIMS(a) |
| 0.12±0.03 100% RH 0.06±0.03 72% RH* 0.04±0.03 61% RH* 0.01±0.03 36% RH* 0.0035±0.03 18% RH* (7.0±2.0) x 10-4 7% RH | 195 | Zhang, Jayne and Molina, 1994 | CWFT-EIMS(b) |
| >0.2* | 190 |  |  |
| 0.02* | 208 |  |  |
| <1.0 x 10-4 | 200-220 | Zhang, Leu and Keyser, 1995 | CWFT-CIMS(c) |

Comments

(a)	Solid film of sulphuric acid ≥ 0.1 mm thickness made from freezing a liquid solution of composition corresponding to SAT (57.5% H2SO4/H2O) on the inside of the flow tube wall to 195K.  The cryogenic deposits were characterized by their vapour pressure of H2O monitored by an ion-molecule reaction with F2-. The results were obtained as a function of relative humidity in the range 10 to 90%, obtained by using a fixed p(H2O and varying the temperature  from 192 - 205 K. p(ClONO2) = (1.3 to 7 x10-7) mbar.  PHCl was approximately held at 2 x 10-7 mbar (2-3 ppbv at 17 km) and pH2O for the displayed  values was 6.7 x 10-4 mbar.  The uptake coefficients could be expressed as ln = -0.636-0.4802T, where T = T-189.  T can be approximated by T-Tice where Tice is the temperature of the ice point at a given partial pressure of water vapor and where pH2O < pice.

(b)	Solid film of sulphuric acid ≥ 0.1 mm thickness made from freezing a liquid solution of composition corresponding to SAT (57.5% H2SO4/H2O) on the inside of the flow tube wall to <200 K.  The thermodynamic state of the SAT sample was controlled by setting the vapour pressure of H2O, either H2O -rich (approaching 100% rh) or H2SO4-rich at constant temperature or selecting the temperature at constant p(H2O).  The HCl was always in excess of ClONO2 and no HOCl product was detected.   strongly depends on the relative humidity over the SAT surface, a trend that reflects the partitioning of HCl to the surface;  its value decreases by more than two orders of magnitude at 195K, from 0.12 at 100% rh to 7x10-4 at low rh.   The following expressions are provided for the uptake coefficient at typical stratospheric [HCl]: log  = 5.25 + 1.91logPH2O for T=195K, PClONO2 = 4 to 5.3 x10-8 mbar, PHCl = 5.3 to 10.5 x 10-7 mbar,  PH2O= 5.3 x10-5 to 7.4 x10-5 mbar;  log  = 175.74- 1.59logT + 0.0035log2T for T in the range 195-206K, PClONO2 = 4 to 6.7x10-8 mbar, PHCl = 5.3 to 10.6 x 10-7 mbar and PH2O= 7.4x10-4 mbar.

(c)	Solid film of sulphuric acid ≥ 0.1 mm thickness made from freezing a liquid solution of composition corresponding to SAM (75-85% H2SO4/H2O) on the inside of the flow tube wall at 220-230 K.  PHCl and PClONO2 were in the range 2.7 to10.6 x10-7 mbar.  The experiment was performed by first exposing SAM to HCl and subsequently measuring the uptake of ClONO2 which was identical to hydrolysis on SAM with HCl absent.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| ER | 0.12 | 190 – 199 |
| HCl | [HCl]* 6800 * F | 190 – 199 |
| F | (-2.47x1011+3.28x1011RH+3.27x109 RH2+2.43x109 RH3)/1.7x1014 | 190 – 199 |

[HCl] in molecule cm-3.

Reliability

| rxn | ±0.2 | 185 – 210 K. |
| --- | --- | --- |

Comments on Preferred Values

As with ice films the uptake of ClONO2 on SAT films is followed by reaction with  HCl to form Cl2 and HNO3 in a surface reaction.  At stratospheric temperatures HOCl partitions into the gas phase. The two studies of Hanson and Ravishankara (1993) and Zhang et al. (1994) on SAT show that reactive uptake of ClONO2 on HCl-doped SAT is a strong function of relative humidity, declining as RH reduced, as was also found for NAT surfaces. In the case of SAT, Zhang et al. (1994) showed that surface coverage resulting from a given p(HCl) also declined rapidly with decreasing RH, which accounts for the effect on the surface reaction rate and hence the reactive uptake coefficient of ClONO2. The  values of Hanson and Ravishankara(1993) are in good agreement with the more extensive data Zhang et al.(1994). For H2O-rich SAT (>90% RH) at 195 K,  = 0.12 which is approximately a factor of 2 lower than observed for HCl doped ice (0.27±0.02) for  similar p(HCl) of 7 x 10-7 mbar. At lower p(H2O) and higher temperatures  reduces to ~10-3, although there is some indication that  on H2O-rich SAT increases with decreasing temperature. Reactive uptake of ClONO2 on HCl-doped SAM is very slow,  ~ 1 x 10-4.

The IUPAC recommended upateke coefficient parameterisation for reaction of ClONO2 + HCl on ice surfaces used an Ely-Rideal model. Application of this model to solid sulphuric acid films requires the surface concentration [HCl]s to be defined as a function of temperature and p(H2O).   The partitioning of HCl to SAT studied by Zhang et al.(1994) forms the basis of our recommendation for KLinC for HCl as a function of RH in the temperature range 190 - 199 K (IUPAC, 2009). The recommended reactive uptake coefficients for ClONO2 + HCl use the IUPAC KLinC to evaluate HCl in the following expression for ClONO2

s = ERClONO2)x HCl

The uptake coefficients from this expression give a reasonable fit to results of Zhang et al. (1994) as a function of relative humidity and temperature over the temperature range 191.5 to 205 K.

References

Hanson, D.R. and Ravishankara, A.R.: J. Geophys. Res. 98, 22931 (1993).

Leu, M.-T., Moore, S.B. and Keyser, L.F.: J. Phys. Chem. 95, 7763 (1991).

Zhang, R., J. T. Jayne and Molina, M.J.: J.Phys. Chem. 98, 867 (1994).