IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A2.13 MD13

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: June 2010; last change in preferred values: June 2010

H2O2  + mineral oxide (dust) surfaces

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients:  |  |  |  |
| 1.5 × 10-3 (TiO2, 15% RH) | 298 | Pradhan et al., 2010a | AFT-CIMS (a) |  |
| 5.0 × 10-4 (TiO2, 70% RH) |  |  |  |  |
| (3.33  0.26)  10-4 (Gobi sand, 15% RH) |  | Pradhan et al., 2010b | AFT-CIMS (b) |  |
| (6.03  0.42)  10-4 (Gobi sand, 70% RH) |  |  |  |  |
| (6.20  0.22)  10-4 (Saharan dust, 15% RH) |  |  |  |  |
| (9.42  0.41)  10-4 (Saharan dust, 70% RH) |  |  |  |  |

# Comments

- H2O2 (initial concentration ≈ 4.1 × 1012 molecule cm-3) was detected by CIMS using CF3O- (m/z = 85) as a reagent ion. A sub-micron aerosol was generated by nebulising an aqueous dispersion of TiO2 particles followed by diffusion drying. Particle number and size distribution was analysed using a DMA, giving typically surface area of Sa = 6 × 10-3 cm2 cm-3 and Dmax of 0.45 m at 40% RH. The uptake coefficient was calculated using the time- and aerosol area dependent loss rate of H2O2, which was first order in all cases. Uptake coefficients () were measured at relative humidities of 15, 35 and 70 %.

- Experimental method as in comment (a). For Gobi sand  the available surface area was mainly from particles of diameter ~0.4 m, for Saharan dust ~0.2 m. The relative humidity was varied between 15 and 70 % (not all uptake coefficients obtained are listed in the table above).

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  (15-70 % RH) | 6.24  10-4 – 1.87  10-6 RH + 9.37  10-8 (RH)2 | 298 |

Reliability

|  log () | 0.5 |  |
| --- | --- | --- |

##### Comments on Preferred Values

The uptake kinetics of H2O2 on mineral dust material has been reported in two publications from the same group (Pradhan et al, (2010a, 2010b). Pradhan et al., found irreversible uptake of H2O2 to sub micron Saharan dust, Gobi sand and TiO2 aerosol substrates, but no gas phase products were detected. For TiO2, an increase of  was observed as RH decreased below ~ 40%, but  remained approximately constant above 50% RH. This was attributed to competition between water molecules and H2O2 for surface sites. In contrast, the uptake of H2O2 to both Gobi sand and Saharan dust became more efficient with increasing RH. No dependence of  on [H2O2] was observed. In this case, the authors argue that the increasing uptake with RH is due to dissolution of H2O2 in surface adsorbed water.

Our preferred values are based on the data for Saharan dust, which is most likely to best represent atmospheric mineral aerosol. The parameters were derived by fitting a polynomial to data read from a graph and should not be extrapolated beyond the range given. The error limits are expanded to reflect this and the fact that (to date) the data are only reported in a discussion paper.

# References

Pradhan, M., Kalberer, M., Griffiths, P. T., Braban, C. F., Pope, F. D., Cox, R. A. and Lambert, R. M.,  Environ. Sci. Technol., 44, 1360-1365, 2010a.

Pradhan, M., Kyriakou, G., Archibald, T., Papageorgiou, A. C., Kalberer, M., and Lambert, R. M.: Atmos. Chem. Phys. Disc. 10, 11081-11107, 2010b.