### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.5 HI5

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: June 2010. Last change in preferred values June 2010.

H2O2  + ice

# Experimental data

| Parameter | Temp./K | Reference | Technique/Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients:  |  |  |  |
| 0.02 | 228-270 | Conklin et al., 2002 | PC (a) |  |
| Partition coefficients: K |  |  |  |  |
| KlinC = 1.56 | 228 | Clegg and Abbatt, 2001 | CWFT-MS (b) |  |
| Kv = 8.3 x 104 | 270 | Conklin et al., 2002 | PC (a) |  |
| Kv = 1.24 x 105 | 262 |  |  |  |
| Kv = 5.78 x 105 | 243 |  |  |  |
| Kv = 1.07 x 107 | 228 |  |  |  |
| KlinC = 2.1  10-5 exp (3800 / T) | 203-233 | Marécal et al., 2010 | (c) |  |

# Comments

(a)	Column packed with  200 m ice spheres. H2O2 ( 1010-1012 molecule cm-3) detected using liquid phase enzymatic fluorometry. Due to the long duration of the experiments (up to 20 hours), some of the uptake observed (exceeding 1 monolayer at the lowest temperatures) is due to bulk dissolution of H2O2. Equilibrium gas-to-ice volume partitioning coefficients were extracted from experimental data when the net uptake was zero, or by using an advection-dispersion model of H2O2 transport in the column (at 228 K). The coefficient Kv includes both surface and bulk H2O2.

(b)	Ice films were  made by freezing water. The uptake of H2O2 was observed to be totally reversible. The geometric surface area was used to calculate the coverage. The value of KlinC presented in the Table was determined from data presented in a plot and uses the observed linear relationship between N (surface coverage in molecule cm-2 of ice) and [H2O2]. No significant dependence of KlinC on temperature was observed.

(c)	The parameters for KlinC were reported in an modelling study of the effect of H2O2 uptake to cirrus clouds. Though no experimental details are given by Marécal et al., the method used was CWFT with CIMS and MS detection of H2O2 (MPI-Mainz group, Pouvesle et al.).

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| KlinC / cm | 2.1  10-5 exp (3800 / T) | 200 - 240 |
| Nmax / molecule cm-2 | 4.5  1014 | 200 - 240 |

Reliability

| log KlinC | 0.5 | 200 - 240 |
| --- | --- | --- |
| log Nmax | 0.3 | 200 - 240 |

Comments on Preferred Values

The experimental data show that the interaction of H2O2 ice is reversible, and that, at long exposure times, both surface and volume uptake are observed. The solubility in ice appears to be a factor of  200 smaller than in liquid water, extrapolated to the same temperature (Conklin and Bales, 1993).

Partitioning to the ice surface is surprisingly weak, and no temperature dependence was detected in the one published study of this parameter (Clegg and Abbatt, 2001). A further value of  KlinC  = 2.1  10-5 exp (3800 / T) has been reported by Marécal et al. (2010) in a modelling study. This value is based on unpublished experimental work (Pouvesle et al., from the MPI-Mainz group) using a coated wall flow tube, though no experimental details are given. This parameterisation results in values of KlinC which are orders of magnitude larger than reported by Clegg and Abbatt (2001).

The larger partition coeffcient measured by Pouvesle et al. is more consistent with the emerging picture of the interaction of hydrogen bonding trace gases with ice surfaces in which a distinct inverse relationship between the vapour pressure of the trace gas and the partition coefficient is observed (Sokolov and Abbatt, 2002). For this reason we prefer the value reported by Marécal et al. (2010) but with expanded error limits to refect the divergence in the available studies and the fact that it has not yet been published. We also adopt the value of Nmax reported by Pouvesle et al.)

# References

Clegg, S. M., and Abbatt, J. P. D.: J. Phys. Chem. A  105,  6630-6636, 2001.

Conklin, M. H., Sigg, A., Neftel, A., and Bales, R. C.: J. Geophys. Res. 98, 18367-18376, 1993.

Marécal, V., Pirre, M., Riviere, E. D., Pouvesle, N., Crowley, J. N., Freitas, S. R. and Longo, K. M.: Atmos. Chem. Phys. 10, 4977-5000, 2010.

Sokolov, O and Abbatt, J. P. D.: J. Phys. Chem. A, 106, 775-782, 2002.