# IUPAC Task Group on Atmospheric chemical Kinetic Data Evaluation – Data Sheet VI.A1.12 HET_H2OL_12

Data sheets can be downloaded for personal use only and must not be re-transmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

Data sheet last evaluated: December 2011; last change in preferred values: December 2011

HBr + H2O(liq) → products

Experimental data

| Parameter | Temp./K | Reference | Technique/Comments |
| --- | --- | --- | --- |
| Accommodation coefficients: b |  |  |  |
| 0.16 6.8 × 10-2 | 263 281 | Schweitzer et al., 2000 | DT-MS (a) |
| 0.26±0.02 0.14±0.02 | 273 283 | Li et al., 2002 | DT-MS (b) |

Comments

(a)	80-150 m diameter droplets with a gas-liquid interaction time of 0-20 ms. The HBr concentrations were in the range 1012 – 1014 molecule cm-3, with most experiments performed at 1013 molecule cm-3. Rate of uptake was time-independent as well as independent on pH in the range 7-14. Diffusion-corrected uptake coefficient is interpreted as a bulk accommodation coefficient b having a significant negative temperature dependence.

(b)	Droplet train experiment with ethylene glycol/water mixtures. Droplet size was in the range 70 to 300 m, 2.6-25 mbar of (mostly) He in flow tube with trace gas species concentrations in the range 2 x 1013 to 3 x 1014 molecule cm-3.  The value of b was found to be independent of the interaction time in the range 2.5 to 17 ms, and temperature. b varied continuously with increasing mole fraction of H2O from a high (pure glycol) to a low (pure H2O) value which has been successfully modelled using surface tension data for glycol/H2O solutions of variable composition.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| b | 2.3 x 10-2 | 298 |
| b | 1.3 x 10-8 exp (4290/T) | 263-281 |

Reliability

|  log (b) | ± 0.3 | 298 |
| --- | --- | --- |
|  (E/R) | ± 600 K | 263-281 |

Comments on Preferred Values

Although both Schweitzer et al. (2000) and Li et al. (2002) present bulk accommodation coefficients with a strong negative temperature dependence, there is disagreement of a factor of between 3 and 5 in the absolute values of b.  We have taken the data of Schweitzer et al. (2000) as the basis of our recommended values owing in part to the larger number of data taken within a larger temperature range.

References

Li, Y.Q.; Zhang, H.Z.; Davidovits, P.; Jayne, J.T.; Kolb, C.E. and Worsnop, D.R.: J. Phys. Chem. A, 106, 1220-1227, 2002.

Schweitzer, F., Mirabel, Ph. and George, C.: J. Phys. Chem. A, 104, 72-76, 2000.