### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A1.7 HET_H2OL_7

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: June 2011; last change in preferred values: June 2011.

HONO (g) + H2O (l) → NO (aqueous) + NO2 (aqueous) + H2O (l)

Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Bulk accommodation coefficients: b |  |  |  |  |
| > 5 × 10-3 | 299 | Kirchner et al., 1990 | LJ-IC (a) |  |
| 4.3 × 10-3 (wet Na2CO3) | 298 | Msibi et al., 1993 | CWFT (b) |  |
| (5+2-1) × 10-2 | 297 | Bongartz et al., 1994 | LJ-IC (c) |  |
| (5+4-1) × 10-2 | 245 |  | DT-IC (c) |  |
| 4 × 10-3 < b < 4 × 10-2 | 278 | Mertes and Wahner, 1995 | LJ (d) |  |
| Solubility: H |  |  |  |  |
| 223 ± 11 | 273 | Park and Lee, 1988 | Bubbler-CLD (e) |  |
| 121 ± 6 |  |  |  |  |
| 60 ± 3 |  |  |  |  |
| 38 ± 2 |  |  |  |  |
| H * = 194 ± 25 (8.7 wt% H2SO4) | 269 | Becker et al., 1996 | Static-TDLAS/IC (f) |  |
| H * = 117 ± 20 (8.7 wt% H2SO4) | 278 |  |  |  |
| H * = 73 ± 10 (8.7 wt% H2SO4) | 285 |  |  |  |
| H * = 50 ± 8 (8.7 wt% H2SO4) | 291 |  |  |  |
| H * = 34 ± 5 (8.7 wt% H2SO4) | 298 |  |  |  |
| Rate constants, k1 [M-1 s-1] |  |  |  |  |
| 3.46 | 283 | Park and Lee, 1988 | Bubbler-CLD (e) |  |
| 13.4 | 295 |  |  |  |
| 28.6 | 303 |  |  |  |
| Rate constants, k-1 [M-1 s-1] |  |  |  |  |
| 1.98 × 108 | 283 | Park and Lee, 1988 | Bubbler-CLD (e) |  |
| 1.58 × 108 | 295 |  |  |  |
| 1.67 × 108 | 303 |  |  |  |

Comments

(a)	Interaction of HNO2 (60 ppm) with a liquid jet of pure water. The kinetics were studied by ion chromatographic analysis of the liquid jet nitrite content.  The gas phase diffusion coefficient value used was 0.13 cm2 s-1, the value used for the solubility of HNO2 in water was 60 M atm-1. A kinetic model taking into account diffusion in the gas phase as well as the radially resolved flow velocity within the jet was used to simulate the data of appearance of nitrite in the aqueous phase. Agreement with the data was not very good likely due to uncertainties in the velocity distribution of the liquid jet. Taking into account dissociation of HONO in the aqueous phase did not improve the fits. Thus, the bulk accommodation coefficient is regarded as a lower limit.

(b)	A flow of 6 l per min of air at 97 % relative humidity containing about 0.5 ppm NO2 at atmospheric pressure passed an annular glass reactor, coated with a mixture of Na2CO3 and glycerol. Uptake of nitrous acid detected by wet extraction of reactor segments.

(c)	Two experimental flow techniques, an improved version of the liquid jet and the droplet train technique, were used. Both techniques involve the measurement of the concentration of NO2- in the collected liquid droplets of 10 µm to 100 µm diameter at residence times of 3.7 ms to 16 ms at total pressures of 40 mbar to 80 mbar. Temperature refers to droplet surface temperature of (245 ± 5) K. A 20% uncertainty in Dg leads to the stated error intervals.

(d)	Liquid jet at 298 K. Experiments were done with pure water, with 0.01 M NaOH, 33.4 g/l triethanolamine and 1g/l NaAsO2 to vary the liquid phase sink. HONO was measured by DOAS in a White cell. HONO was produced indirectly by reaction of NO2 with the glass walls upstream of the jet leading to concentrations of 1013 to 1014 cm-3 in presence of a factor of 50 more NO2. Nitrite and nitrate were measured spectrophotometrically. HONO uptake was independent of pH or added sink. Within the short residence time of the jet, the liquid phase remained far from equilibrium. A kinetic model was used to obtain the likely range for b based on the observed loss of HONO from the gas phase (lower limit) and the appearance of nitrite in the aqueous phase (upper limit), respectively.

(e)	A thermostated pyrex reactor with a fritted gas inlet. The solubility of HONO was measured by using low concentration HONO solutions (10-6 M) and observing the purge behavior with a chemiluminescence detector. HONO decomposition experiments were performed at higher solution concentrations > 10-5 M to allow observation of NO and NO2 purging from the bubbler apparatus. The rate constants listed in the table for the forward (decomposition) (k1) and backward reaction (k-1) were obtained by fitting a kinetic model to the purge data. The mass transfer properties of the bubbler were calibrated using CO2.

(f)	Solubility of HONO was measured in a 11-L Pyrex glass reactor directly by monitoring both gas phase composition by tunable diode laser spectrometry and liquid phase by ion chromatography. Formation of NO2 due to 2 HONO = NO + NO2 + H2O was observed. Since the NO2 concentration equilibrated with time, this reaction was included into calculating the effective solubility.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| αb | 0.05 | 273 - 300 |
| H* | 4.2 × 10-6 exp(4873/T) (1 + 5.9 × 10-4 exp(-1760 (1/T-1/298))/[H+]) | 273 - 300 |
| k1 (M-1 s-1) | 3.1 × 1014 exp(-9090/T) | 273 - 300 |
| k-1 (M-1 s-1) | 1.7 × 108 | 273 - 300 |
| Reliability |  |  |
|  log (αb) | 0.7 | 273 - 300 |
|  log (k) | 0.3 | 273 - 300 |
|  E/R [K] | 50 | 273 - 300 |

Comments on Preferred Values

Most of the attempts to measure the bulk accommodation coefficient of HONO into water or dilute aqueous solutions were done with a liquid jet experiment at relatively high pressure. Uncertainties arise from not understanding precisely the radial flow velocity distribution within the jet, which critically determines whether or not uptake runs into solubility equilibrium. The other significant issue is that especially at atmospheric pressure, transfer of the gas into the liquid is strongly affected by gas phase diffusion. We therefore adopt the value from the Bongartz et al. (1994) study performed at lower pressure than the others.

The solubility of HONO in water has been directly measured by Park and Lee (1988). Their data are also in line with the extrapolated solubility from those by Becker et al. (1996), who measured the solubility as a function of sulphuric acid composition (0.3 wt% and above). The preferred expression is consistent with that presented in data sheet VI.A4.7 for 0 wt% H2SO4 and agrees well with the temperature dependence measured by Park and Lee. The acid dissociation constant used in this expression is that determined by Park and Lee, which is identical to that calculated from the standard free energies of formation of HONO(g) and HONO(aq) (Schwartz and White, 1981). We note that the acid dissociation constant determined by Riordan et al. was somewhat lower (1.6 × 10-3 (pK=2.8) at 298 K).

The rate constants for the decomposition reaction of HONO (k1) and the reverse process (k-1) has been adopted from Park and Lee (1988); for k-1 the average of the available rate constants at three temperatures have been taken as preferred value. They are somewhat above those of earlier studies (Schwartz and White, 1981, and references therein), but better represent the low concentrations expected under atmospheric conditions. The preferred value for k1 is much lower than that in H2SO4 at about 50 wt% (320 M-1 s-1, see data sheet VI.A4.7). Given that the back reaction is significant, an expression for gamma based on the resistance model is not appropriate.

References

Becker, K. H., Kleffmann, J., Kurtenbach, R., and Wiesen, P.: J. Phys. Chem., 100, 14984-14990, 1996.

Bongartz, A., Kames, J., Schurath, U., George, C., Mirabel, P., and Ponche, J. L.: J. Atmos. Chem., 18, 149-169, 1994.

Kirchner, W., Welter, F., Bongartz, A., Kames, J., Schweighofer, S., and Schurath, U.: J. Atmos. Chem., 10, 427-449, 1990.

Mertes, S., and Wahner, A.: J. Phys. Chem., 99, 14000-14006, 1995.

Msibi, I. M., Shi, J. P., and Harrison, R. M.: J. Atmos. Chem., 17, 339-351, 1993.

Park, J.-Y., and Lee, Y.-N.: J. Phys. Chem., 92, 6294-6302, 1988.

Ponche, J. L., George, C., and Mirabel, P.: J. Atmos. Chem., 16, 1-21, 1993.

Schwartz, S.E., and  White, W.H.: in: Advances in Environmental Science and Engineering, J. R. Pfafflin and E. N. Ziegler, ed(s)., Gordon and Breach Science Publishers, NY, 1981, 1-45.