IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A4.09 HSTD9

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: May 2008; last change in preferred values: May 2008.

HNO3 + SAT

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients: , 0 |  |  |  |
| 0 > 0.3 0 > 0.2 | 191.5 200 | Hanson, 1992 | CWFT-CIMS a) |  |
| 0 = 0.20 10% H2SO4 0 = 0.05 98% H2SO4 0 = 0.10 10% H2SO4 0 = 0.03 98% H2SO4 | 180 180 200 200 | Aguzzi and Rossi, 1991 | Knud (b) |  |
| Partition coefficients: K(cm) |  |  |  |  |
| No reversible adsorption observed |  |  |  |  |

# Comments

(a)	HNO3 uptake on SAT film made by freezing aqueous sulphuric acid solutions of composition 57.5 or 59.6 wt.% on the flow tube wall at <200 K.   corrected for gas diffusion using estimated diffusion coefficients. Pressure = 0.6 mbar He.  Rapid uptake observed, but with increasing surface coverage of HNO3 the rate of uptake decreased.  The steady-state partial pressure of HNO3 over SAT surface at 191 K with a coverage of approximately 1 monolayer of HNO3 was about a factor of ~3 higher than the vapor pressure over NAT, showing that new hydrate was not formed.  At 200 K p(HNO3) was ~3x lower than over pure NAT.  This is attributed to the formation of metastable NAM at this temperature.

(b)	SAT film made by freezing aqueous sulphuric acid solutions of composition indicated in wt.%. Uptake was continuous and g was time independent except at the highest [H2SO4], when some decline with exposure time was noticed. The initial uptake coefficient decreased linearly with increasing [H2SO4] in the range given at both temperatures.  If H2O vapour was added to the flow into the Knudsen cell, the uptake coefficient was indpendent of [H2SO4] up to ~ 60-70%, depending on temperature.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| as | >0.2 | 190 – 240 |

##### Reliability

| log as | 0.3 | 190 – 240 |
| --- | --- | --- |

Comments on Preferred Values

The results of the two experimental studies of nitric acid interaction with specifically prepared solid H2SO4-hydrate surfaces at temperatures and concentrations relevant for the lower stratosphere are in good agreement. Under these conditions uptake is rapid, continuous and irreversible, but declined with increasing coverage of surface HNO3. Evidence from measurements of the p(HNO3) over the surfaces indicated that the NAT-type solids formed on the surfaces were not in complete vapour-solid equilibrium.  The data do not allow determination of the partition coefficient for adsorption, but the agreement between the results from different techniques allows us to recommended accommodation coefficient .

# References

Aguzzi, A. and Rossi, M.J.: Phys. Chem. Chem. Phys. 3, 3707 (2001).

Hanson, D. R.: J. Geophys. Res. Lett. 19, 2063 (1992).