### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.12 HI12

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

Data sheet last evaluated: December 2007: ; last change in preferred values: December 2008.

HNO3 + ice

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients: , 0 |  |  |  |
| 0 > 0.2 | 197 | Leu, 1988 | CWFT-MS (a) |  |
| 0 > 0.3 | 191-200 | Hanson, 1992 | CWFT-MS (b) |  |
| 0 > 0.2 | 208-248 | Abbatt, 1997 | CWFT-MS (c) |  |
| 0 >5 x 10-3 ss = (2 ± 1) x 10-4 | 220-223 | Zondlo, Barone and Tolbert, 1997 | Knud (d) |  |
|  = 0.3 | 200 | Seisel, Flückiger and Rossi, 1998 | Knud (e) |  |
|  = 0.27±0.08 0.25±0.10 0.17±0.05 0.09±0.03 | 180 190 200 210 | Aguzzi and Rossi, 2001 | Knud (f) |  |
|  = (3.3±0.6)x10-2 1.2x10-2 6.0x10-3 | 214 218 235 | Hynes, Fernandez and Cox, 2002 | CWFT-MS (g) |  |
| 0 = 7x10-3 0 = 3x10-3 | 209 220 | Hudson et al., 2002 | Knud (h) |  |
| Partition coefficients: K(cm) |  | * calculated in this evaluation (see comments) |  |  |
| 4.64  104 * 2.00  104* 0.83  104 * 0.32  104 * | 218 228 238 248 | Abbatt, 1997 | CWFT-MS (c) |  |
| (1.06 ± 0.1.6)  103 (2 site model) (0.48 ± 0.072)  103 (2 site model) | 218 228 | Hynes, Fernandez and Cox, 2002 | CWFT-MS (g) |  |
| (10.05 ± 3.22)  104 (5.53 ± 1.93)  104 (1.74 ± 0.51)  104 | 214 229 239 | Ullerstam et al, 2005 | CWFT_MS (i) |  |
| 10.26  104 3.91  104 1.75  104 | 214 229 239 | Cox et. al. 2005 | CWFT-MS (j) |  |

# Comments

(a)	Fast flow tube reactor with MS detection.  Ice condensed from the vapor phase onto the cold flow tube.   corrected for gas diffusion using estimated diffusion coefficients.

(b)	Fast flow tube reactor with CIMS detection of HNO3 at pHNO3 = (1 - 4) x 10-7 mbar.  Ice condensed from the vapor phase onto the cold flow tube.   corrected for gas diffusion using estimated diffusion coefficients. Evidence for time-dependent uptake due to surface saturation.

(c)	Coated-wall flow tube with MS detection.  Pressure = 1.3 mbar of He.  The ice surfaces were prepared by wetting the inner wall of a tube which was inserted into the cooled flow tube resulting in a smooth ice film. Initially, HNO3 is taken up rapidly independent of the HNO3 partial pressure with  as cited.  Uptake then saturates at a surface coverage of Nmax ~0.2 to 0.3 monolayers. Subsequently, small rates of uptake following a T-0.5 rate law were observed corresponding to diffusional loss processes on the ice.  The heterogeneous interaction is nearly irreversible as only about 25% of the quantity of HNO3 was recovered after the HNO3 flow was halted.  The formation of an amorphous albeit stable surface layer of HNO3-H2O is postulated as the HNO3 partial pressures are well below those for formation of stable hydrates.  The intregrated amount of HNO3 adsorbed was weakly dependent on pHNO3 in the range (1.7 - 41) x 10-7 mbar at 218 K, and increased with decreasing temperature at approximately constant pHNO3 (6.5 to 9.0 x 10-7 mbar).  The cited Langmuir equilbrium constants were calculated from the reported equilibrium surface coverages using a single site model with Nmax assumed = 2.7 x 1014 molecule cm-2

(d)	Two-chamber flow reactor equipped with FTIR reflection-absorption as well as MS detection.  The flow reactor configuration only allowed uptake coefficients lower than 5 x 10-3 to be measured.  At low pHNO3, uptake partially saturates after deposition of approximately one monolayer and reaches steady state.  Above ~2.7 x 10-5 mbar of HNO3 uptake occurs continually at 0 without signs of saturation.   The former uptake regime is interpreted as leading to an amorphous mixture of HNO3-H2O, whereas the continuous uptake leads to a supercooled liquid mixture of a typical composition of 3:1 to 4:1 H2O-HNO3.

(e)	Uptake experiment in a Knudsen flow reactor equipped with a residual gas MS and simultaneous grazing-incidence FTIR reflection-absorption spectrometry.

(f)	Uptake experiment in a Knudsen flow reactor on ice films condensed from the vapor phase and on frozen bulk H2O.  Pulsed valve and steady state uptake experiments resulted in identical values for  after correction for the interaction of HNO3 with the Teflon coating.   shows a strong negative temperature dependence for T≥195K with Ea=-28±4 kJ mol-1 and a constant value of 0.3 below that temperature.

(g) Coated wall flow tube study at 2.3 mbar He using MS detection of HNO3. PHNO3 was in the range (0.4-2.7) x10-6 mbar and led to time-dependent uptake converging to steady-state conditions after typically 200s of uptake.   for HNO3 uptake was unaffected by the presence of HCl in comparable quantities at 218K.  Surface coverages were determined from integrated uptake prior to saturation. They showed little variation with PHNO3 in the range and maximum surface coverage was 3 x 1014 molecule cm-2 at 218 K and 228 K.  Partition coefficient was determined using 2-site Langmuir isotherm fit to experimental data at 218 and 228 K, with Nmax = 1015 molecule cm-2 . The enthalpy of HNO3 adsorption onto ice was –(54.0±2.6) kJ/mol, evaluated using the Van’t Hoff equation and the values of Keq cited.

(h)	Uptake experiment in a Knudsen flow reactor equipped with simultaneous reflection-I.R.absorption spectroscopy and MS.  Surface area of vapour deposited ice, measured by BET method using butane adsorbent gas, was a factor of 2.27 larger than the geometric area of the base surface.  values were time dependent in the ice stability region at low P(HNO3).  Initial values cited for pHNO3 ~ 1 x10-6 mbar. Surface coverages were determined from integrated uptake prior to saturation, and showed a strong T dependence below 214 K.

(i)	Coated wall flow tube with pHNO3 in range 10-8 hPa - 10-6 hPa detected using CIMS. Ice films formed by freezing liquid water. At T > 214 K surface coverages measured in both unsaturated regime at low partial pressure and close to saturation. Maximum surface coverage was (2.1 - 2.7) x 1014 molecule cm-2 independent of temperature. The uptake is nearly irreversible as only 10- 40% of the quantity of HNO3 desorbed after the HNO3 exposure was halted. At 200 K continuous uptakes were obsereved without saturation and little desorption.  Partition coefficients were determined using single-site Langmuir isotherm fit to experimental data at 214, 229 and 239 K, giving the expression: KLangP(hPa-1) = -(5.1± 0.4) x 105 T  +  (12.3± 0.9) x 107.  The enthalpy of HNO3 adsorption onto ice was –(30.3±6) kJ/mol, evaluated using the Van’t Hoff equation, and similar values were obtained from T-dependence of integrated desorption.

(j) Model of gas flow and surface exchange in CWFT with a single site Langmuir mechanism The model was used to reanalyse experimental results from Ullerstam et al (see note (i)). The experimental time-dependent uptake profiles were best fitted with an additional process involving diffusion of the adsorbed molecules into the ice film.  The model allowed true surface coverages to be distinguished from total uptake including transfer to the bulk, leading to more accurate estimates of the Langmuir constant, Keq, for surface adsorption. At T ≥ 229 K, Keq decreased by up to 30% as pHNO3 decreased from the saturated region; the cited values are midrange.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| αs | 0.1 | 190 - 240 |
| Nmax / molecule cm-2 | 2.7  1014 | 214 - 240 |
| KlinC / cm | 7.5 x 10-5 exp(4585/T) | 214 - 240 |

Reliability

|  log (αs) | ± 0.3 | 190 - 240 |
| --- | --- | --- |
|  (KlinC) / cm | ± 0.1 | 228 |
|  (E/R) /K | ± 700 |  |

Comments on Preferred Values

There have been many experimental studies of nitric acid – ice interaction but mostly at temperatures and concentrations corresponding to stability regions for either hydrate or supercooled HNO3/H2O solutions. Under these conditions at T< 210 K uptake is continuous and irreversible. At higher temperatures in the ‘ice stability’ region, uptake rate is time dependent, declining from an initial rapid uptake ( > 0.2) to very slow uptake when the surface is saturated at q ~3.0  1014 molecules cm-2.  Surface coverages at low pHNO3 on ice films in the temperature range 210-240 K have been quoted in a number of studies (Abbatt, 1997, Hudson et al., 2002, Hynes et al., 2002, Ullerstam et al., 2005 and Cox et al., 2005, and also Arora et al., 1999 (who measured HNO3 uptake on ice particles). There is good agreement in the measured uptakes near saturation in the CWFT studies. For example, for a temperature of 228 K, a gas-phase concentration of 3  1010 molecule cm-3 of HNO3 results in equilibrium surface coverages (Nmax) of 1.9  1014 molecules cm-2 (Abbatt, 1997), 1.6  1014 molecules cm-2 (Hynes et al., 2002), 2.4  1014 molecules cm-2 (Ullerstam et al. 2005). The Knudsen cell study of Hudson et al (2002) shows much lower saturated coverages at 220 K and a huge increase with decreasing temperature.

Values of the maximum surface coverage, Nmax, vary between 1.2±0.2  1014  molecules cm-2 (230 K, Arora et al, 1999), (2.1 - 2.7) x 1014 molecule cm-2 (214 -239 K, Ullerstam et al., 2005), and 3  1014 molecule cm-2 (Hynes et al, 2002). These values are consistent with values for other traces gases on similar ice surfaces, and with molecular dynamics calculations (Abbatt, 2003).

Partitioning coefficents in the table were derived using a single site Langmuir model for the data reported by the Abbatt group and a 2-site model for the Hynes data, who also used a high value of Nmax = 1015 cm-2 in their fit.  Ullerstam et al showed that the 2-site model failed when tested against data at low pHNO3.  Variable values of the derived equilibrium partition coefficients and adsorption enthalpy, Hads , result from different models used to interpret the results. Bartels-Rausch et al reported  Hads = -44 kJ mol-1 from chromatographic measurements of HNO3 retention in a packed ice column, which lies midway between the other reported values.

The preferred partitioning coefficient  is based on the data of Ullerstam et al., 2005, using the refined analysis given in the study of Cox et al., 2005. This may be used in the full form of the single site Langmuir isotherm :

together with the recommended Nmax value, based on the values given by Ullerstam, 2005,  to provide a simple parameterisation appropriate for equilibrium surface coverages at concentrations up to ~5 x 10-7 mbar in the given temperature range. At lower temperatures and higher pHNO3, near the phase boundary for thermodynamic stability of hydrates or supercooled HNO3/H2O solutions,  uptake is continuous with no saturation and the Langmuir model cannot be used. Note however that all flow tube studies report that the adsorption of HNO3 to ice is not completely reversible, even in the HNO3/ice stability regime.  Surface spectroscopic investigations (Zondlo et al., 1997; Hudson et al, 2002) suggest that adsorbed HNO3 is solvated to form nitrate ions, suggesting that adsorbed molecules enter the surface layer of the ice film.

Measurements of the uptake coefficient are problematic in CWFT experiments, due to the difficulty in separating adsorption and desorption kinetics and to diffusion limitations, which will result in determination of a lower limit. Knudsen cell measurements of o indicate a surface accomodation coefficient of ~0.3 at T < 200 K. The uptake coefficent decreases with time as increasing amounts of HNO3 are adsorbed in the ice film, and most measurements are affected by this.  The recommended value for go is based on the measurements of Abbatt (1997) Hanson (1992) and Agussi and Rossi (2001).

Ullerstam and Abbatt (2005) showed that on growing ice the long term uptake of nitric acid  is significantly enhanced compared to an experiment performed at equilibrium, i.e. at 100% relative humidity  (RH) with respect to ice.  The fraction of HNO3 that is deposited onto the growing ice surface is independent of the growth rate and may be driven by the solubility of the nitric acid in the growing ice film rather than by condensation kinetics alone.

# References

Abbatt, J. P. D.: Geophys. Res. Lett. 24, 1479 1997.

Abbatt, J. P. D.: Chem. Rev., 103, 4783, 2003.

Aguzzi, A. and Rossi, M.J.: Phys. Chem. Chem. Phys. 3, 3707 2001.

Bartels-Rausch,T., Eichler, B., Zimmermann, P., Gaggeler, H. W., and Ammann, M., Atm.Chem.Phys., 2, 235, 2002.

Cox, R. A., Fernandez, M.A., Symington, A., Ullerstam, M. and Abbatt, J.P.D.: Phys.Chem.Chem.Phys, 7, 3434, 2005.

Hanson, D. R.: J. Geophys. Res. Lett. 19, 2063 1992.

Hudson, P. K. ,J. E. Shilling, M. A. Tolbert and O. B. Toon: J. Phys. Chem. A, 2002, 106, 9874-9882

Hynes, R. G., Fernandez, M. A. and Cox, R. A.: J. Geophys. Res. 107, 4797 2002, doi:10.1029/2001JD001557.

Leu, M.-T.: Geophys. Res. Lett. 15, 17, 1988

Picaud, S., Toubin, C. and Girardet, C.: Surface Science 454, 178-182, 2000.

Seisel, S., Flückiger, B. and Rossi, M. J.: Ber. Bunsenges. Phys. Chem. A 102, 811, 1998.

Ullerstam, M., Thornberry, T. and Abbatt , J. P. D.: Faraday Discuss., 130, 211,  2005.

Ullerstam, M. and Abbatt , J. P. D.: Phys. Chem. Chem. Phys. 7, 3596 2005.

Zondlo, M. A., Barone, S. B. and Tolbert, M. A.: Geophys. Res. Lett. 24, 1391 1997.