### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A1.8 HET_H2OL_8

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: April 2009; last change in preferred values: June 2009.

HNO3 (g) +  H2O (l)   HNO3 (aqueous)

Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Uptake coefficients:  |  |  |  |  |
| 0.190.02 | 268 | Van Doren et al., 1990 | DT-IR (a) |  |
| 0.0710.02 | 293 |  |  |  |
| > 0.01 | 298 | Kirchner et al., 1990 | LJ-IC (b) |  |
| 0.110.01 | 298 | Ponche et al., 1993 | DT-IC (c) |  |
| 0.03 | 298 | Schütze and Herrmann, 2002 | (d) |  |

Comments

(a)	Experiments performed at room temperature flow with the water vapor pressure adjusted to the vapour pressure of water at the experimental temperature. HNO3 was detected downstream of the flow tube using IR absorption. The uptake coefficients were corrected for gas phase diffusion. The data show significant negative temperature dependence within the range indicated in the table. Given that under the experimental conditions the near surface region of the droplet does not saturate, it is argued that the uptake coefficients derived are actually bulk accommodation coefficients equivalent to the rate limiting step being solvation.

(b)	Interaction of HNO3 (60 ppm) in 1 bar of synthetic air with a liquid jet of pure water. The kinetics were studied by ion chromatographic analysis of the liquid jet nitrate content. The uptake coefficient was attributed to a bulk accommodation coefficient and is regarded as a lower limit due to uncertainties in the velocity distribution of the liquid jet. The gas phase diffusion coefficient value used was 0.132 cm2 s-1, the value used for the effective solubility of HNO3 in water was 2.45 × 106 M2 atm-1.

(c)	Gas uptake into a monodisperse (70 µm to 110 µm diameter) droplet train. The pH of water was adjusted to 9.5 and 11.0. Uptake determined by chemical analysis (ion chromatography) of collected aqueous phase. The uptake coefficient corrected for gas phase diffusion was independent of pH, of the contact time and of the HNO3 concentration in the range 10 to 100 ppm. The value for the diffusion coefficient used was 0.160 cm2 s-1 in the gas phase and 2.6 × 10-5 cm2 s-1 in the liquid phase. The solubility was assumed to be 2.1x105 M atm-1. The measured average uptake coefficient obs was (5.0 ± 0.9) × 10-2 at 67 mbar N2 and 298 K.

(d)	A drop of water (2-3mm diameter) was exposed to HNO3 (3-5 × 1013 cm-3) in a flow tube. The drop was probed by UV spectroscopy to monitor the appearance of nitrate in the aqueous phase. A model was used to determine the effect of gas phase diffusion on the measured uptake coefficient.  The value for the gas phase diffusion coefficient was 0.124 cm2 s-1 in H2O at 298 K and 0.534 atm cm2 s-1 in He at 298. The value used for the effective solubility of HNO3 in water was 2.1 × 105 M atm-1. The measurements indicate that the uptake coefficient given in the table is a lower limit.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| αb | 7.5 × 10-5 exp(2100/T) | 268 - 300 |
| Reliability |  |  |
|  log (αb) | 0.7 |  |
|  E/R [K] | 1000 |  |

Comments on Preferred Values

The experiments on HNO3 uptake to pure water all resulted in large uptake coefficients, and all studies concluded that bulk accommodation rather than solubility or reaction in the liquid phase (dissociation) was rate limiting. They all carry a significant uncertainty due to gas phase diffusion, depending on geometry and pressure. The high pressure liquid jet experiment by Kirchner et al. (1990) was most sensitively affected by the magnitude of the diffusion coefficient and in addition contained an uncertainty with respect to the liquid flow regime. Schütze and Herrmann (2002) also used several simplifications and suggest that their uptake coefficient represents a lower limit to the bulk accommodation coefficient. Also, the diffusion correction commonly applied for high uptake coefficients to the droplet train experiments as reported by Van Doren et al. (1990) has recently been challenged (Morita et al. 2003; Hanson et al., 2004; Garrett et al., 2006; Davidovits et al., 2006). Van Doren’s experiments at high temperature were measured at higher total pressure than those at lower temperature. The two droplet train studies, in spite of determining uptake via loss of gas phase HNO3 in one case (Van Doren et al., 1990) and the appearance of nitrate in the aqueous phase in the other (Ponche et al., 1993), but both using the same method to correct for diffusion, agree fairly well with each other. The recommended expression for αb is a least square fit to the data by Ponche et al. and Van Doren et al. in Arrhenius form, with large error limits to account for potential systematic errors.

References

Davidovits, P., Kolb, C. E., Williams, L. R., Jayne, J. T., and Worsnop, D. R.: Chem. Rev., 106, 1323-1354, 2006.

Garrett, B. C., Schenter, G. K., and Morita, A.: Chem. Rev., 106, 1355-1374, 2006.

Hanson, D. R., Sugiyama, M., and Morita, A.: J. Phys. Chem. A, 108, 3739-3744, 2004.

Kirchner, W., Welter, F., Bongartz, A., Kames, J., Schweighofer, S., and Schurath, U.: J. Atmos. Chem., 10, 427-449, 1990.

Morita, A., Sugiyama, M., and Koda, S.: J. Phys. Chem. A, 107, 1749-1759, 2003.

Ponche, J. L., George, C., and Mirabel, P.: J. Atmos. Chem., 16, 1-21, 1993.

Schütze, M., and Herrmann, H.: Phys. Chem. Chem. Phys., 4, 60-67, 2002.

Van Doren, J. M., Watson, L. R., Davidovits, P., Worsnop, D. R., Zahniser, M. S., and Kolb, C. E.: J. Phys. Chem., 94, 3265-3269, 1990.

Figure 1: Uptake coefficients of HNO3 into water as a function of temperature. Symbols denote data, the solid lines represents the recommended parameterisation for the bulk accommodation coefficient.