### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.49 HI49

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet updated: 17th October 2007.

HOBr + HBr(ice)  Br2+ H2O

Uptake coefficient data

| Parameter | Temp./K | Reference | Technique/Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients for HOBr: , 0 |  |  |  |
| 0.12±0.03 | 228 | Abbatt, 1994 | CWFT-MS(a) |
| ≥ 1.5 | 230-240 | Kirchner, Benter and Schindler, 1997 | CWFT-MS(b) |
| 0.44 0.39 0.37 0.305 0.205 0.16 | 180 185 190 195 200 205 | Chaix, Allanic and Rossi, 2000 | Knudsen –MS (c) |

Comments

(a)	Frozen film ice surface; [HOBr] ~ 1012 molecule cm-3, generated in situ by reaction of Br2 with OH. [HBr]o = (1-2) x 1012 molecule cm-3 which corresponded to a surface coverage of  at least 10 formal ML at 188 K, based on the recommended KLinC(data sheet V.A1.27).  Gas phase Br2 formation kinetics matched the HOBr decay.  Continuous steady state uptake rate  observed.

(b)	Reflectron Time-of-Flight mass spectrometer used.  The total pressure was in the range 5 to 20 mbar He.  Ice films were produced by spraying water or aqueous solutions of HBr onto the interior walls of the cold flow tube. [HOBr] was in the range 0.7 to 1.2x1013 molecules cm-3.

(c)	Ice surfaces formed by vapour deposition (type C) freezing bulk solutions of distilled water either rapidly (type B) or slowly (type SC), the latter with the intention of forming single-crystalline ice.  Water vapour was continuously added to maintain the ice films during experiments. Both pulsed-valve and continuous flow experiments were performed on the different types of HBr-doped ice samples, using two sources of HOBr. Typical flow rates of HBr used to dope the surface of ice ranged from 1014 to 1016 molecule s-1 leading to the deposition of 0.5 to 10 formal monolayers onto ice depending on the deposition time.  In all cases the uptke of HOBr led to production of Br2. The cited uptake coefficients are the mean  of values reported for type C and type B ice surfaces at each temperature, which were very similar.

Preferred values

| Parameter | Value | T/K |
| --- | --- | --- |
| sHOBr) | 4.8 x 10-4exp(1240/T) | 180 – 230 |

Reliability

| log(ER | ±0.15 | 185 – 210 |
| --- | --- | --- |

Comments on preferred values

All studies report rapid and continuous uptake of HOBr onto ice films doped with gaseous HBr. Under the conditions of these experiments both HBr and HOBr form stable hydrates on ice surfaces and no dependence of g(HOBr) on [HBr] wasfound.  Br2 is the sole product observed. The reported g  values in the temperature range 180 – 228 K are in reasonably consistent and show a negative temperature dependence.  The recommended expression for gmax, is an Arrhenius fit to the data of Abbatt at 229 K and the mean of  the values reported by Chaix et al. on vapour-deposited and frozen film ice at each temperature in the range 180 – 205 K. These values can be assumed to be independent of [HBr] provided [HBr]o > [HOBr] o.

References

Abbatt, J.P.D.: Geophys. Res. Lett. 21, 665 (1994).

Chaix, L., Allanic, A. and Rossi, M.J.: J. Phys. Chem. A 104, 7268 (2000).

Kirchner, U., Benter, Th. and Schindler, R.N.: Ber. Bunsenges. Phys. Chem. 101, 975 (1997).

Figure 1 Arrehius plot of uptake coefficient for HOBr on ice doped with HBr