### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.48 HI48

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: 17th October 2007; last change in preferred values: 17th October 2007.

HOBr + HCl(ice)  BrCl + H2O

Uptake coefficient data

| Parameter | Temp./K | Reference | Technique/Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients: , 0 |  |  |  |
| 0.25 (+0.10/-0.05) | 228 | Abbatt, 1994 | CWFT-MS(a) |
| (3.3±0.5)x10-1 (2.3±0.2)x10-1 | 190 200 | Allanic, Oppliger and Rossi, 1997 | Knudsen –MS (b) |
| 5x10-2 – pHCl =1.8x10-7 mbar 0.23 – pHCl =1.2x10-5 mbar 4x10-3 – pHCl = 5.6 x10-7 mbar 0.19 – pHCl = 2x10-5 mbar | 190 222 | Chu and Chu, 1999 | CWFT-MS (c) |
| 0.3±0.05 | 180-195 | Chaix, Allanic and Rossi, 2000 | Knudsen –MS (b) |
| >0.1 ; [HCl] = 8 x 1011 ss= 0.005±0.002 ; [HCl]o = 5.8 x 1011 | 205-227 227 | Mössinger, Hynes and Cox, 2002 | CWFT-MS (e) |

Comments

(a)	Frozen film ice surface; [HOBr] ~ 1012 molecule cm-3, generated in situ by reaction of Br2 with OH. [HCl]o = (1-2) x 1012 molecule cm-3 which corresponded to a fractional surface coverage of  >0.95 at 228 K, based on the recommended KLinC(data sheet V.A1.27). Gas phase BrCl formation kinetics matched the HOBr decay.

(b)	20 m thick ice film made by vapour deposition and located in a Knudsen reactor operated in either continuous flow or pulsed mode. Uptake coefficients cited obtained at short (0.3 s) residence time avoiding saturation effects.  PHCl used was sufficient to give at least 1 ML coverage and all HOBr taken up was converted to BrCl, demonstrating effective competition of HCl surface reaction with uptake of HOBr into the ice film.

(c)	The ice film of typical thickness of 28 m was grown from H2O vapor condensation in the temperature range 190 to 240 K.  Uptake coefficients were determined from HOBr loss and BrCl formation, giving comparable values. Both  HOBr  amd BrCl  decreased substantially with decreasing PHCl from 2x10-5 mbar down to 2x10-7.

(d)	Ice surfaces formed by vapour deposition (type C) freezing bulk solutions of distilled water either rapidly (type B) or slowly (type SC), the latter with the intention of forming single-crystalline ice.  Water vapour was continuously add to maintain the ice films during experiments. Both pulsed-valve and continuous flow experiments were performed on the different types of HX-doped ice samples, using two sources of HOBr. Typical flow rates of HX used to dope the surface of ice ranged from 1014 to 1016 molecule s-1 leading to the deposition of 0.5 to 10 formal monolayers of HX onto ice depending on the deposition time.  In all cases the uptke of HOBr led to rapid and quantitative production of BrCl with the cited uptake coefficient.

(e)	The ice coating was produced by freezing a liquid H2O film and HOBr was stored as an aqueous solution at 273K.  [HOBr] and [HCl] varied between (2–22)x1011 and (4-8)x1011 molecule cm-3, respectively.  The lower limit of >0.1 reflects diffusion limited uptake.  For [HCl]< [HOBr] the HOBr uptake was time- and concentration dependent owing to the changing HCl surface coverage.  BrCl was observed as product. Evidence for an Ely Rideal mechanism was presented.

Preferred values

| Parameter | Value | T/K |
| --- | --- | --- |
| ERHOBr) | 0.25 | 185 – 210 |

Reliability

| ER | ±0.05 | 185 – 210 K. |
| --- | --- | --- |

Comments on preferred values

All studies report rapid uptake of HOBr onto ice films doped with HCl.  BrCl is the sole product with a yield of 100%.  The conditions of these experiments mostly corresponded to near maximum coverage of HCl in the ice or HCl hydrate stability region.  The reported maximum values of g at high [HCl] in the temperature range 180 – 228 K are in reasonably good agreement, with a slight tendency to increase with decreasing temperature. We recommend a temperature independent value of gmax, which is a mean of the values obtained from all studies cited and the T range is extended to 220 K.

The study of Chu and Chu (1999) observed a dependence of the uptake coefficient on initial [HCl] and Mossinger et al. (2002) found evidence for surface coverage dependence of the uptake coefficient when initial [HOBr] was in excess of [HCl], leading significant HCl consumption.  The kinetic dependence in both studies appears to be complex and the data are not well fitted by either an Ely-Rideal and Langmuir Hinshelwood mechanism. Fig 1 & 2 show fits to the data for HCl dependence reported by Chu and Chu (1999). In particular neither model captures the observed fall-off in g with initial p(HCl) assuming that surface coverage of HCl is given by the recommended IUPAC value of the [HCl] partition coefficient with Nmax = 3 x 1014 molecule cm-3. This probably results from reagent depletion due to the surface reaction.  Therefore we cannot recommend a reactive uptake coefficient for HOCl as a function of [HCl]g

References

Abbatt, J.P.D.: Geophys. Res. Lett. 21, 665 (1994).

Allanic, A., Oppliger, R. and Rossi, M.J.: J. Geophys. Res. 102D, 23529 (1997).

Chaix, L., Allanic, A. and Rossi, M.J.: J. Phys. Chem. A 104, 7268 (2000).

Chu, L. and Chu, L.T.: J. Phys. Chem. A 103, 8640 (1999).

Mössinger, J.C., Hynes, R.G. and Cox, R.A.; J. Geophys. Res. 107, art. No. 4740 (2002), doi:10.1029/2002JD002151.