### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.41 HI41

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: September 2007; last change in preferred values: September 2007.

HOCl + HCl(ice)  Cl2 + H2O

Uptake coefficient data

| Parameter | Temp/K | Reference | Comments |
| --- | --- | --- | --- |
| Uptake coefficients: ss (HOCl) |  |  |  |
| ≥ 0.3 (+0.7, -0.1) | 191 | Hanson and Ravishankara, 1992 | CWFT-CIMS (a) |
| 0.16±0.1 | 202 | Abbatt and Molina, 1992 | CWFT-MS(b) |
| 0.24 (+0.5, -0.15) | 195 |  |  |
| 0.34±0.20 | 188 | Chu, Leu and Keyser, 1993 | CWFT-MS(c) |
| 0.15 | 160 200 | Oppliger, Allanic and Rossi, 1997 | Knud(d) |
| 0.15 | 188 200 | Chu and Chu, 1999 | CWFT-MS(e) |

Comments

(a)	Kinetics study on vapour deposited ice film. The initial [HOCl] was 2 x 109 molecule cm-3. The decay rate of HOCl was identical for [HCl] = 2 x109 or 2 x1010  molecule cm3, indicating surface saturation of HCl. Cl2 product was rapidly released from ice surface.

(b)	The uptake of HOCl in the presence of excess HCl is time-independent. Uptake rate shows a negative temperature dependence:   increases from 0.16 to 0.24 when the temperature drops from 202 to 195K.

(c)	The ice film was deposited from water vapor saturated He and consisted of m-sized granules. The thickness ranged from 3.7 to 34.7 m which were calculated and calibrated gravimetrically. The internal surface was measured using BET gas adsorption measurments.  PHOCl ranged from (1.7 to 24) x 10-7 mbar and PHCl from (1.2 to 10.6) x 10-6 mbar.  Taking into account a structural model for the ice substrate a lower limit value of ss =0.13±0.08 was obtained.

(d)	Uptake experiment performed in a Knudsen flow reactor with MS detection using both steady-state and real-time pulsed valve admission of HOCl and HCl with a balancing H2O flow.  The ice samples were generated from vapor phase deposition of approximately 2x105 monolayers of H2O (20 m thick).  Mass balance studies indicate that HOCl reacts with all HCl taken up by the ice sample even though the rate of formation of Cl2 decreases towards the end of the reaction.  The rate of Cl2 formation upon HOCl exposure to HCl-doped ice slows down in the presence of HNO3 hydrates.

(l)	The ice was condensed from the vapor phase at 188.5 K and flow tube pressure was 0.37 mbar. Cited values for g are not corrected for pore diffusion.  Uptake of HOCl mbar  (PHOCl = 9.7 x 10-7 mbar) was continuous and HOClss was independent of [HCl] over range (1.9 – 11.0) x 10-6 mbar; at lower [HCl] (PHOCl≈PHCl g decreased, presumably due to depletion of the surface HCl.  An Ely-Rideal mechanism was proposed for the surface reaction, but no supporting evidence was presented.

Preferred values

| Parameter | Value | T/K |
| --- | --- | --- |
| ER (HOCl) | 0.1 | 180 - 220 |
|  (HOCl) | ER (HOCl) x [HCl]s | 180 - 220 |
| [HCl]s / molecule cm-2 | KlinC(HCl) x [HCl]g |  |

Reliability

|  log (ER) | ± 0.1 | 298 |
| --- | --- | --- |

Comments on preferred values

All studies report rapid uptake of HOCl onto ice films doped with HCl.  Cl2 is the sole product with a yield of 100%.  The conditions of these experiments all corresponded to near maximum coverage of HCl in the ice or HCl hydrate stability region.   Surface melting was also a likely occurance under these conditions (McNeill et al, 2006).  The reported g  values are in reasonably good agreement and there is a suggestion of a negative temperature dependence (see Fig.2).  However, considering the small temperature range and the cited experimental errors, which arise substantially from the large corrections necessary to account for the effect of gas phase diffusion on the measured rate constants in the CWFT studies, we recommend a temperature independent value of gmax. The preferred value is a mean of the values obtained from all studies cited and the T range is extended to 220 K.

Only the study of Chu and Chu (1999) observed an [HCl] dependence of the uptake coefficient on pure ice surfaces, although Abbatt and Molina (1992) noted that uptake of HOCl on HNO3-doped ice was much slower and exhibited [HCl] dependence. Fig 1 shows a plot of the uptake coefficient calculated as a function of p(HCl) at 188 K, assuming both Ely-Rideal and Langmuir Hinshelwood mechanisms, together with the results of Chu & Chu. Neither model captures the observed fall-off in g at low p(HCl), which almost certainly results from reagent depletion as (p(HCl) ≤ p(HOCl)). The recommend a reactive uptake coefficient for HOCl as a function of [HCl]g is given by 0 x q(HCl) calculated using the recommended value of KlinC for HCl on ice (see data sheet V.A1.27) with Nmax = 3 x 1014 molecule cm-3.  In the presence of HNO3 a competitive Langmuir isotherm can be used to obtain qHCl.

References

Abbatt, J.P.D. and Molina, M.J.: Geophys. Res. Lett. 19, 461 (1992).

Chu, L. and Chu, L.T.: J. Phys. Chem. 103 A, 691 (1999).

Chu, L.T., Leu, M.-T. and Keyser, L.F.: J. Phys. Chem. 97, 12798 (1993).

Hanson, D.R. and Ravishankara, A.R.: J. Phys. Chem. 96, 2682 (1992).

Hanson, D.R. and Ravishankara, A.R.: J. Phys. Chem. 97, 12309 (1993).

McNeill, V. F., Loerting, Th., Geiger, F.M., Trout, B.L., and Mario Molina, M. J., Proc.Nat.Acad.Sci.(US), 103, 9422, (2006).

Oppliger, R., Allanic, A. and Rossi, M.J.: J. Phys. Chem. A 101, 1903 (1997).

Zhang, R., Leu, M.-T. and Keyser, L.F.: J. Phys. Chem. 98, 13563 (1994).

Figure 1. The recommended parameterization for P(HCl) dependence of the uptake coefficient of HOCl on ice in the presence of HCl at 188 K.

Figure 2. The temperature dependence of the observed uptake coefficients of HOCl on ice in the presence of excess HCl.

# Text boxes

Fig 1