IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A3.6 HET_O_6

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet evaluated: 15th January 2009; last change in preferred values: 15th January 2009.

N2O5 + H2O (ammonium bisulphate aerosols)

# Experimental data

| Parameter | RH/ % | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- |
| Uptake coefficients: ,ss,0 |  |  |  |  |
| 0.020  0.0036 | 13 | 293 | Mozurkewitch and Calvert, 1988 | AFT-CL (a) |
| 0.0218  0.0055 | 35 |  |  |  |
| 0.050  0.0055 | 45 |  |  |  |
| 0.0482  0.0055 | 62.5 |  |  |  |
| 0.0382  0.0055 | 77.5 |  |  |  |
| 0.0015  0.00042 | 13 | 295±1 | Kane et al., 2001 | AFT- |
| 0.0031  0.0023 | 32 |  |  | CIMS/SMPS |
| 0.012  0.0032 | 38 |  |  | (b) |
| 0.018  0.0027 | 48 |  |  |  |
| 0.022  0.0019 | 63 |  |  |  |
| 0.035 0.011 | 74 |  |  |  |
| 0.046  0.012 | 89 |  |  |  |
| 0.069  0.0095 | 99 |  |  |  |
| 0.020  0.0020 | 60 | 295±2 | Folkers et al, 2003 | FTIR/SMPS/APC (c) |
| 0.0190  0.0040 | 67 |  |  |  |
| 0.0187  0.0043 | 79.7 |  |  |  |
| 0.0025 - 0.0063 (+natural organic) | 55 - 83 |  |  |  |
| 0.0031  0.0017 | 20 | 298 | Hallquist et al., 2003 | AFT-CL/SMPS (d) |
| 0.0041  0.0020 | 35 |  |  |  |
| 0.018  0.008 | 50 |  |  |  |
| 0.023 0.0013 | 70 |  |  |  |
| 0.015  0.006 | 80 |  |  |  |
| 0.030  0.0022 | 50 | 263 |  |  |
| 0.0140  0.0062 | 50 | 268 |  |  |
| 0.0129  0.0045 | 50 | 273 |  |  |
| 0.036 0.0018 | 50 | 283 |  |  |
| 0.0037  0.008 | 50 | 308 |  |  |
| 0.0133  0.0009 | 30 | 298 | Badger, 2006 | AFT-CL/SMPS (e) |
| 0.015  0.002 | 50 |  |  |  |
| 0.0196  0.0009 | 60 |  |  |  |
| 0.024  0.001 | 70 |  |  |  |
| 0.036±0.009 | 50 | 263 | Griffiths and Cox, 2009 | AFT-CL/SMPS (f) |
| 0.005±0.002 | 50 | 268 |  |  |
| 0.014±0.006 | 50 | 278 |  |  |
| 0.012±0.001 | 50 | 283 |  |  |
| 0.011±0.001 | 50 | 288 |  |  |
| 0.016±0.003 | 50 | 293 |  |  |
| 0.003±0.001 | 50 | 303 |  |  |

# Comments

- Atmospheric pressure aerosol flow tube with N2O5 ( 1013 molecule cm-3)measured by a modified chemiluminescence method, via thermal dissociation to NO3 and titration with NO, which was detected. Aerosols generated in a constant output atomiser, dried, and size selected with a differential mobility analyser (DMA) coupled to a condensation particle counter (CPC), to count the particles. The monodisperse aerosol was then equilibrated at controlled humidity before entry into the flow tube.  The size and surface area of the aerosol in the flow tube was calculated from the deliquescence properties of the aerosol, determined in separate tandem DMA experiments. The typical diameter, dmean was 0.08-0.2 mm, with surface area density of 1 – 5 x 10-5 cm2/cm3. Uptake coefficients were determined from the first order rate constants for N2O5 decay, corrected for wall loss, which were linearly dependent on surface area. Diffusion limitation was negligible for the size range used..

- Atmospheric pressure aerosol flow tube with detection of N2O5 [(5 to 200) x 1012 molecule cm-3] by CIMS using I- reagent ion. Aerosols generated in a constant output atomiser and were dried and equilibrated at controlled humidity before entry into the flow tube.  The size distribution was measured with a scanning mobility particle sizer (SMPS) coupled to a condensation particle counter (CPC). The surface area of the aerosol in the flow tube was calculated from the observed size distribution assuming the particles are spherical. The mean diameter, dmean was 0.12 mm, with surface area density of 0.0016 cm2/cm3. Uptake coefficients were determined from the first order rate constants for N2O5 decay, corrected for wall loss, and for diffusion limitation to the particle surface using the size resolved Knudsen number for the non-monodisperse aerosol.  Although the values of g showed some scatter (ony selected values from the 17 data points reported are cited), a large increase with RH throughout the range 13-99% was observed, which was fitted by the expression:  = 2.79 x 10-4 + 1.3 x 10-4  x (RH) – 3.43 x 10-6  x (RH)2 + 7.52 x 10-8  x (RH)3. No dependence on the uptake coefficient on [N2O5] was observed.

- Static aerosol chamber with inert teflon walls at ambient pressure and temperature. N2O5 ( 1013 molecule cm-3) produced in situ by reaction of NO2 with ozone. Gas phase species measured by FTIR and UV spectroscopy. Polydisperse aerosol (dia.=20nm – 5 mm) generated by spraying dilute ammonium bisulphate solutions, with size distribution measured by SMPS for particle diameters <700nm and for larger diameters by aerodynamic particle sizer.  Uptake coefficients determined by fitting experimental time dependence of species with a numerical model of chemistry and integrated aerosol surface area. To investigate effect of organic film on uptake, NH4HSO4 coated by organic oxidation products of ambient VOC with added ozone.  A noticeable reduction in g was observed in this case.

- Atmospheric pressure aerosol flow tube with N2O5 (7.5 - 125 x 1013 molecule cm-3) measured by via thermal dissociation to NO3 and titration with NO, which was detected by O3-chemiluminescence. Deliquesced aerosols were generated in a constant output atomiser, and conditioned by equilibration with an additional excess flow of controlled RH. Size distribution determined with a differential mobility analyser (DMA) coupled to Faraday cup electrometer to count the particles. The typical peak diameter, dmax was 200 nm, with surface area density of (7-37) x 10-5 cm2/cm3. Uptake coefficients were determined from the first order rate constants for N2O5 decay, after correction for wall loss and diffusion effects. The measured uptake coefficients were independent of [N2O5] or on RH  above 50%, but g declined with decreasing RH below 50%. This falloff was attributed to decreased liquid water amounts in the deliquesced aerosol at low RH.

- Same experimental details as (d); the aerosol surface area in range 0.06 – 0.27 m2m-3 with an area weighted particle diameter of 260 nm.

- Same experimental method as in (d), except that the halocarbon-wax-coated flow tube and the DMA were contained in a modified low temperature chamber so that aerosol Sa could be measured at the same temeperature as the gas uptake region, leading to improved accuracy of uptake measurements. N2O5 mixing ratios were around 300 ppbv and aerosol surface area density varied in the range 0.02 to 0.5 cm2 cm-3.  The aerosol volume to surface ratio varied  between 3 and 4  10-9 m.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| α | 0.035 | 298 |
|  (50% RH) | 94.9 - T + 3.53 x 10-3T2 - 4.14 x 10-6T3 | 260 - 305 |
| kI (s-1) | kII x [H2O]aq (M) |  |
| kII (M-1 s-1) | 1.0 x 105 | 298 |

Reliability

|  log (α) | ± 0.3 | 298 |
| --- | --- | --- |
| log () at 50% RH | ± 0.5 | 260 - 305 |

Comments on Preferred Values

All studies used deliquesced or supersaturated aqueous NH4HSO4 aerosols, with uptake coefficients measured as a function of RH. g was generally seen to increase with RH over the range 20 – 90% but there is poor agreement between the different studies. The early study of Mozurkewitch and Calvert reported much larger uptake coefficients than from more recent work even after the 15% downward revision of their reported g values suggested by Freid et al.(1995).  The results of Kane et al are very scattered at RH < 50% and show a large increase in g above 70% RH which has not been reproduced in any of the other studies, which g show little dependence on RH above ~50% RH, with a value of ~0.02 , similar to that for uptake on ammonium sulphate.  We suggest some source of systematic error in measurement of the surface area of the particles is responsible for the high uptakes reported by Mozurkewitch and Calvert and Kane et al. (at high RH). The former authors suggest that evaporation of NH3 could lead to acidification of the particles, forming H2SO4 which is more reactive.   Kane et al. give insufficient experimental detail of the sizing method using SMPS to evaluate the reliability of SA measurements at high RH. We therefore recommend an expression giving an approximately constant value of g above 70% RH at 298 K.

The g value is similar to that on pure water drops (~0.015 at 298 K), and only slightly lower than that on H2SO4 droplets ( = 0.036 ± 0.008, Hallquist et al, 2000). The uptake leads to hydrolysis of N2O5 and formation of HNO3 which mostly transfers to the gas phase. The lack of a dependence on the water content of deliquesced droplets at RH >50%, suggests that uptake is controlled by a surface process, either mass accommodation or surface reaction. At lower RH, gdeclines.  Since NH4HSO4 aerosols do not effloresce easily this result suggests that uptake at lower RH is limited by the rate of hydrolysis of N2O5 in the bulk liquid phase, and hence on [H2O]aq . For very small particles at low RH uptake rate can become dependent on particle volume.

The recommended expression for RH dependence uses a size dependent resistance-model formulation:

g =

The recommended value of ab = 0.035 is based on observed for uptake on malonic acid (Thornton et al (2004)) and H2SO4 droplets (Hallquist et al, 2003). kI is calculated using the recommended liquid phase rate constant for N2O5 + [H2O]aq : kII = 1 x 105 M-1s-1, which is intermediate between the values derived by Thornton et al. (2003) from hydrolysis of on malonic acid aerosol (2.5 x 104 M-1s-1 ) and by Mentel et al. (1999) from uptake on NaNO3 aerosols (1.5 x 105 M-1s-1). Figure 1 shows the RH dependence of g using water mass fractions taken from the AIM database and using Dl = 1 x 10-5 cm2s-1 and 2 M atm-1. The expression fits the >50% RH data well but overestimates uptake rates at low RH.  The reacto-diffusive parameter ({Dl/ kII[H2O]}0.5) predicts a significant size dependence of gfor r < 100 nm.

Hallquist et al (2003) reported a temperature dependence of N2O5 uptake on NH4HSO4 aerosols at constant RH of 50%. Their data showed considerable scatter but generally g increased as T decreased in the range 263 -308 K, but with a region of apparantly zero temperature dependence between 270 - 290 K. The recent results of Griffiths and Cox (2009), which had reduced uncertainties in determination of the actual Sa of the aerosol,  confirm this  complex trend. In view of this agreement, we tentatively recommend an empiracle cubic fit to the data, to provide a temperature dependence of g in the range 260 -305 K, with large error limits.

# References

Badger, C. L.; PhD Thesis, University of Cambridge, (2006).

Hallquist, M., Stewart, D.J., Baker, J. and Cox, R.A.: J. Phys. Chem. 104A, 3984 (2000).

Hallquist, M., Stewart, D.J., Stephenson, S.K. and Cox, R.A.: Phys. Chem. Chem. Phys. 5, 3453 (2003).

Fried, A., B. E. Henry, J. G. Calvert and Mozurkewich, M.: J. Geophys. Res. 99, 3517 (1994).

Folkers, M., Mentel, Th F.Mentel and Wahner, A.: Geophys.Res.Lett., 30, No12, 1644, doi:10.1029/2003GL017168, 2003

Griffiths, P.T and Cox, R.A., Atm. Science Lett., submitted January (2009)

Kane, S.M., Caloz, F. and Leu, M.-T.: J. Phys. Chem. 105A, 6465 (2001).

Mentel, T.F, Sohn,M. and Wahner, A.: Phys. Chem. Chem. Phys. 1, 5451 (1999).

Mozurkewich, M. and Calvert, J.G.: J. Geophys. Res. 93, 15889 (1988).

Thornton, J.A., Braban, C.F. and Abbatt, J.P.D.: Phys. Chem. Chem. Phys 5, 4593-4603 (2003).

Figure 3: Uptake coefficients for heterogeneous uptake of N2O5 by ammonium bisulfate aerosol at 50% RH.  Filled circles: Griffiths et al., 2008; open squares: Hallquist et al.,2003;

Line shows cubic fit to data of Griffiths et al.