### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A4.2 HSTD2

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: January 2009; last change in preferred values: January 2009.

N2O5 + H2O  (SAT)   →  products

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Uptake coefficients:  |  |  |  |  |
| 0.6  10-3 (60 wt. % H2SO4, RH 40 %) | 192 | Hanson and Ravishankara, 1993 | CWFT-CIMS (a) |  |
| 2.4  10-3 (60 wt. % H2SO4, RH 80 %) | 192 |  |  |  |
| 5  10-3 (57.5 wt. % H2SO4, RH 44-100 %) | 195 |  |  |  |
| 8  10-3 (57.5 wt. % H2SO4, RH 22-85 %) | 205 |  |  |  |
| 5  10-3 (60 wt. % H2SO4, RH 24-87 %) | 205 |  |  |  |

# Comments

(a)	Sulphuric acid tetrahydrate was generated by freezing H2SO4 solutions (57.5 or 60 wt. %). The relative humidity above the film was varied by adjusting the temperature at fixed H2O partial pressure or by adjusting the H2O partial pressure at fixed  temperature. The geometric surface area was used to calculate the uptake coefficient. Experiments were conducted with [N2O5] at  10-7 Torr.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| (RH 22 –100 %) | 6.5  10-3 | 195 - 205 K |

##### Reliability

|  log net | 0.4 | 195 - 205 K |
| --- | --- | --- |

Comments on Preferred Value

The hydrolysis of N2O5 on sulphuric acid tetrahydrate films is much less efficient ( factor 20) than on liquid H2SO4. For SAT formed from an acid of concentration 57.5 wt. %, no dependence on RH was observed, whereas at 60 wt. % larger RH resulted in larger , possibly due to the presence of other hydrates. At 205 K values of  were larger than at 192 K and the authors speculated that this may have been due to formation of a liquid ternary mixture. Our preferred value uses the data obtained  at 57.5 wt. % H2SO4, which corresponds to the composition of SAT. It takes a simple average value of the results at the two temperatures covered and is independent of RH from 22 to 100 %.

# References

Hanson, D. R. and Ravishankara, A. R.: J. Geophys. Res. 98, 22931-22936, 1993.