### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A1.3 HET_H2OL_3

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: April 2011; last change in preferred values: April 2011.

2 NO2 (g) + H2O (l) → HNO2 (aq) + HNO3 (aq)

Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Uptake coefficients:  |  |  |  |  |
| 10-7 (pure water and 0.05 M NaOH) | 273 | Lee and Tang, 1988 | (a) |  |
| (1.50.6)  10-3 (9  1014 cm-3 NO2) | 298 | Ponche et al., 1993 | DT-IC (b) |  |
| (8.70.6)  10-5 | 298 | Msibi et al., 1993 | CWFT(c) |  |
| (2.41.4)  10-4 (9  1014 cm-3 NO2) | 298 | Mertes and Wahner, 1995 | LJ(d) |  |
| (1.20.4)  10-3 (5  1015 cm-3 NO2) | 298 |  |  |  |
| (9.51.5)  10-7 (3 – 6  1014 cm-3 NO2) | 298 | Kleffmann et al., 1998 | Bubbler-IR/IC (e) |  |
| < 5  10-4 | 273 | Cheung et al., 2000 | DT-MS (f) |  |
| ≤ 10-7 (pH 2 – 12) | 298 | Gutzwiller et al., 2002 Ammann et al., 2005 | WWFT-CLD (g) |  |
| ≈ 10-6 (6  1014 cm-3 NO2, 0.01 M NaOH) | 288 | Komiyama and Inoue, 1980 | Bubbler-UV (h) |  |
| Accommodation coefficient: αb |  |  |  |  |
| (6.3±0.7)  10-4 (> 10-2 M hydrochinone) | 273 | Lee and Tang, 1988 | (a) |  |
| (4.2±0.9)  10-4 (5  10-2 M ascorbate) | 298 | Msibi et al., 1993 | CWFT (c) |  |
| (2.4±1.8)  10-2 (deliquesced dihydroxyphenolates) | 296 | Sosedova et al., 2009 | AFT-RC (i) |  |
| Hk21/2 |  |  |  |  |
| 70 M-1/2 atm-1 s-1/2 | 295 | Lee and Schwartz, 1981 | (j) |  |
| 134 M-1/2 atm-1 s-1/2 | 284 | Cape et al., 1993 | (k) |  |
| 7110 M-1/2 atm-1 s-1/2 | 293 | Cheung et al., 2000 | (f) |  |
| 92 M-1/2 atm-1 s-1/2 | 295 | Park and Lee, 1988 | (l) |  |
| Solublity |  |  |  |  |
| 2.0x10-2 M atm-1 | 298 | Andrew and Hanson, 1960 | (m) |  |
| 2.2x10-2 M atm-1 | 288 | Komiyama and Inoue, 1980 | (h) |  |
| (7.00.5)  10-3 M atm-1 | 295 | Lee and Schwartz, 1981 | (i) |  |
| (5.50.6)  10-2 M atm-1 | 284 | Cape et al., 1993 | (k) |  |
| (1.40.2)  10-2 M atm-1 | 293 | Cheung et al., 2000 | (f) |  |
| (2.3+0.3-0.9)  10-2 M atm-1 | 276 |  |  |  |
| Liquid phase rate constant |  |  |  |  |
| (1.00.1)  108 M-1 s-1 | 295 | Lee and Schwartz, 1981 | (j) |  |
| (8.41.5)  107 M-1 s-1 | 295 | Park and Lee, 1988 | (m) |  |
| (6.02.0)  106 M-1 s-1 | 284 | Cape et al., 1993 | (k) |  |
| (3.00.9)  107 M-1 s-1 (2.20.6)  107 M-1 s-1 | 293 276 | Cheung et al., 2000 | (f) |  |

# Comments

(a)	Uptake experiment involving a stopped flow of NO2 (initial concentration 1015 cm-3) in humidified He carrier gas exposed to a circulating fluid sample of either pure water, water with 0.05 M NaOH, or water containing (1-7) x 10-2 M hydroquinone sodium salt.  The uptake coefficients were corrected for gas phase diffusion.

(b)	Gas uptake into a monodisperse (70 µm to 110 µm diameter) droplet train.  The pH of water was adjusted to 4, 5.6 and 11.0. Uptake was determined by detecting nitrate by ion chromatography in the collected aqueous phase after addition of 0.16 M H2O2 to convert all nitrite to nitrate.  The uptake coefficient corrected for gas phase diffusion was independent of pH. The value for the diffusion coefficient used was 0.192 cm2 s-1 in the gas phase and 1 × 10-5 cm2 s-1 in the liquid phase. The solubility was assumed to be 1.2x10-2 M atm-1. The observed uptake coefficient obs was larger than expected from solubility limited uptake, independent of pH. Impurities might have been present as a liquid phase sink for NO2 to drive reaction limited uptake.

(c)	A flow of 6 l per min of air at 97 % relative humidity containing about 0.5 ppm NO2 at atmospheric pressure passed an annular glass reactor, coated with either deionised water or a mixture of 0.05 M ascorbic acid and 0.05 M NaOH (pH 9.3). NO2 was measured using a luminol based NO2 analyzer.

(d)	Liquid jet (50 µm diameter) in a reactor at 298 K. Experiments were done with pure water, with 0.01 M NaOH, 33.4 g/l triethanolamine and 1g/l NaAsO2 to vary the liquid phase sink for NO2. Nitrite and nitrate were measured spectrophotometrically. NO2 uptake was independent of pH or added sink, but was was much larger than solubility limited uptake. The authors therefore proposed a surface reaction proceeding with the uptake coefficients listed in the table.

(e)	NO2 was circulated through a thermostated bubbler containing 125 to 500 ml of water. NO2 and HONO were measured using tunable diode laser absorption spectrometry. Nitrate and nitrite in the liquid were measured using ion chromatography, showing that they were initially formed at equimolar amounts. The first order rate constant for NO2 decay was not depending on the NO2 concentration, indicating overall first-order behaviour.

(f)	Experiments were performed with both a droplet train and a bubble train apparatus. The droplet train was operated with 1013 – 1016 NO2 molecules cm-3,. Uptake of NO2 was not detectable in the droplet train experiment, leading to an upper limit of  < 5 × 10-4 at 273 K. In the bubble train flow reactor,  the NO2(g) concentration was monitored by QMS. Loss of NO2 from the gas phase was fitted with a model of NO2 uptake considering both solubility limitation and reaction in the bulk. This led to both, independent values for H and

(g)	The wetted wall flow tube was operated at room temperature and with 80 ppb of NO2 in N2. The uptake coefficient listed in the table was obtained as blank values for pure water and water with pH adjusted to between 2 and 12 as part of a study to explore the reactivity of NO2 with hydroxysubstituted aromatics.

(h)	NO2 (10 to 2000 ppm) was passed either over a flat liquid surface (both gas and liquid stirred) or through a bubbler. NO2 concentration in the gas phase and nitrate and nitrite were measured using UV absorption. The mass transfer characteristics were determined with CO2. Nitrate and nitrite concentrations were equal over the whole NO2 pressure range. The NO2 absorption rate reported over the full range was proportional to the square of the NO2 pressure at high and proportional to NO2 at low NO2 pressures as expected for mass transport limitation. The absorption rate reported for about 6 × 1014 cm-3 is converted to an uptake coefficient and listed in the table.

(i)	Aerosol particles were produced from nebulizing aqueous solutions of dihydroxybenzoic acid and hydrochinone sodium salts. 13N labeled NO2 was used as reactant, and uptake to particles was monitored by counting radioactive decays of 13N associated with particles after the flow reactor with residence times between 1 and 60 s at ambient pressure and 40 % relative humidity. The observed uptake coefficients in the range of a few 10-3 could be well explained by bulk reaction limited uptake, which allowed deriving an estimate for b listed in the table.

(j)	NO2 at partial pressures of 100 ppb to 800 ppm was passed through 10 to 70 ml of water in a fritted bubbler in a thermostated vessel. NO2 was measured with a chemiluminescence detector. The ionic products in water were determined with a conductivity detector online. Nitrate and nitrite were measured offline with a colorimetric method. The mass transport characteristics were calibrated using CO2, leading to mass transfer times between 1.7 and 5.3 s.

(k)	NO2 at partial pressures of 10 to 100 ppb was passed through 1.0 l of water or aqueous solution in a fritted bubbler in a thermostated vessel. The loss of NO2 was measured with a chemiluminescence detector. The mixing time in the reactor was 60 s based on experiments with CO2. The authors caution that the distribution of NO2 in the reactor may have not been uniform, leading to an overestimate of the rate constants.

(l)	Investigation of HNO2 decomposition kinetics in water in a bubbler type apparatus. The kinetics of the hydrolysis reaction was indirectly derived from the evolution of NO and NO2 measured with a chemiluminescence detector.

(m)	NO2 (200 ppm to 10%) was passed through water in a bubbler type reactor. The solubility listed in the table was derived from observations of HNO2 formation as a function of NO2 pressure.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| αb | 2 x 10-2 | 273 - 298 |
| k / M-1 s-1 | 8.1 ×109 exp (-1630/T) | 276 - 293 |
| H / M atm-1 | 4.4 ×10-6 exp (-2350/T) | 273 – 298 |
| Reliability |  |  |
|  log (αb) | ± 0.7 | 273-298 |
|  log (k) | ± 0.08 | 273-298 |
|  log (H) | ± 0.06 | 273-298 |
|  log (E/R) | 50 | 273-298 |

Comments on Preferred Values

Uptake of NO2 to pure water is driven by the low solubility and slow second order hydrolysis in bulk water. The study by Cheung et al. (2000) has covered the NO2 concentration range down to atmospherically relevant levels and most carefully elaborated the associated mass transfer issues, allowing them to obtain an independent estimate for the solubility at 293 K. They also estimate a value at 276 K using arguments about the expected solubility dependence presented by Schwartz and White (1981). The recommended expression for the temperature dependence is based on these two values.

Cheung et al. also show that their value for Hk1/2 is consistent with most earlier studies covering the lower concentration range, especially the one by Lee and Schwartz (1981). The disagreement with Cape et al. (1993) is likely due to inhomogeneous distribution of NO2 in their reactor, as cautioned by the authors. Due to strong coupling between the liquid phase rate constant and the solubility, we calculate an average value of Hk1/2 extracted from the Cheung et al. (2000), Lee and Schwartz (1981) and Park and Lee (1988) and use the solubility as recommended to arrive at the expression for the rate constant.

Bambauer et al. (1994) report an experiment in a cloud chamber, in which the cloud droplet seeds were NaCl, which seemed to be inconsistent with the second-order reaction of NO2 in water. This and other evidence for apparent first order uptake with surprisingly high uptake coefficient can be discussed as due to reactions with impurities (Ponche et al. 1993; Msibi et al., 1993; Mertes and Wahner, 1995) rather than being representative of bulk accommodation limitation. Yabushita et al. (2009) suggest the formation of a surface complex with chloride ions to explain enhanced NO2 hydrolysis in mM chloride solutions (see also data sheet VI.A2.4). Due to the low solubility of NO2, a strong aqueous phase scavenger is required to get into a bulk accommodation limited kinetic regime. While the CWFT study by Msibi et al. (1993) was likely affected by evaporation, Lee and Tang (1988) show evidence for the transition from reaction limited to bulk accommodation limited kinetics. Sosedova et al. (2009) used an aerosol flow tube approach, which is practically free of gas phase diffusion effects, to obtain a bulk accommodation coefficient of 0.02 for deliquesced sodium salts of hydrochinone and dihydroxybenzoate, which is used as a basis for the recommendation for αb.

The recommended values can be used to calculate uptake coefficients for the reaction of NO2 with dilute aqueous solutions in absence of significant aqueous phase scavengers. In this case, 1/αb is not rate limiting, and the uptake coefficients can be calculated using

,

This leads to uptake coefficients of e.g. 6 ×10-9 at 10 ppb NO2 due to hydrolysis. Under many conditions, the reacto-diffusive length may be large compared to the diameter of the droplet, so that the geometry correction needs to be applied to this expression. On shorter time scales, it needs to be carefully evaluated whether or not 1/Γsol is rate limiting.

References

Ammann, M., Rossler, E., Strekowski, R., and George, C.: Phys. Chem. Chem. Phys., 7, 2513-2518, 2005.

Andrew, S. P. S., and Hanson, D.: Chem. Eng. Sci., 14, 105-114, 1961.

Bambauer, A., Brantner, B., Paige, M., and Novakov, T.: Atmos. Environ., 28, 3225-3232, 1994.

Cape, J. N.; Storeton-West, R. L.; Devine, S. F.; Beatty, R. N.; Murdoch, A. Atmos. Environ. 1993, 27A, 2613-2621.

Cheung, J. L., Li, Y. Q., Boniface, J., Shi, Q., Davidovits, P., Worsnop, D. R., Jayne, J. T., and Kolb, C. E.: J. Phys. Chem. A, 104, 2655-2662, 2000.

Gutzwiller, L., George, C., Rössler, E., and Ammann, M.: J. Phys. Chem. A, 106, 12045-12050, 2002.

Kleffmann, J., Becker, K. H., and Wiesen, P.: Atmos. Environ., 32, 2721-2729, 1998.

Kleffmann, J., Becker, K. H., and Wiesen, P.: J. Chem. Soc. Faraday Trans., 94, 3289-3292, 1998.

Komiyama, H., and Inoue, H.: Chem. Eng. Sci., 35, 154-161, 1980.

Lee, Y.-N., and Schwartz, S. E.: J. Phys. Chem., 85, 840-848, 1981.

Lee, J. H., and Tang, I. N.: Atmos. Environ., 22, 1147-1151, 1988.

Mertes, S., and Wahner, A.: J. Phys. Chem., 99, 14000-14006, 1995.

Park, J.-Y., and Lee, Y.-N.: J. Phys. Chem., 92, 6294-6302, 1988.

Ponche, J. L., George, C., and Mirabel, P.: J. Atmos. Chem., 16, 1-21, 1993.

Kleffmann, J., Kurtenbach, R., Becker, K. H., and Wiesen, P.: Faraday Discuss., 100, 121-127, 1995.

Kleffmann, J., Becker, K. H., and Wiesen, P.: Atmos. Environ., 32, 2721-2729, 1998.

Shen, C. H., and Rochelle, G. T.: Environ. Sci. Technol., 32, 1994-2003, 1998.

Shen, C. H., and Rochelle, G. T.: J. Air Waste Man. Assoc., 49, 332-338, 1999.

Sosedova, Y., Rouvière, A. l., Gäggeler, H. W., and Ammann, M.: J. Phys. Chem. A, 113, 10979-10987, 2009.

Yabushita, A., Enami, S., Sakamoto, Y., Kawasaki, M., Hoffmann, M. R., and Colussi, A. J.: J. Phys. Chem. A, 113, 4844-4848, 2009.