### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation  – Data Sheet I.A3.45 NOx15

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

The citation for this data sheet is: Atkinson, R., Baulch, D. L., Cox, R. A., Crowley, J. N., Hampson, R. F., Hynes, R. G., Jenkin, M. E., Rossi, M. J., and Troe, J.: Atmos. Chem. Phys., 4, 1461, 2004; IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This datasheet last evaluated: November 2017; last change in preferred values: May 2008.

| HO2 + NO  NO2 + HO | (1) |
| --- | --- |
| HO2 + NO + M  HNO3 + M | (2) |

H(1) = -34.5 kJ mol-1

H(2) = -59.4 kJ mol-1

Rate coefficient data (k = k1 + k2)

| k / cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (8.1  1.5) x 10-12 | 296 | Howard and Evenson, 1977 | DF-LMR (a) |
| 3.3 x 10-12 exp[(254  50)/T] | 230-400 | Howard, 1979 | DF-LMR |
| 8.01 x 10-12 | 299 |  |  |
| 5.7 x 10-12 exp[(130  270)T] | 270-425 | Leu, 1979 | DF-RF (b) |
| (9.8  1.6) x 10-12 | 298 |  |  |
| (1.1  0.3) x 10-11 | 297 | Glaschick-Schimpf et al., 1979 | DF (c) |
| (7.6  1.7) x 10-12 | 293 | Hack et al., 1980 | DF-LMR/EPR (d) |
| 3.57 x 10-12 exp[(226  41)/T] | 423-1271 | Howard, 1980 | DF-LMR (e) |
| 7.6 x 10-12 | 298* |  |  |
| (8.5  1.3) x 10-12 | 297 | Jemi-Alade and Thrush, 1990 | DF-LMR (f) |
| 3.0 x 10-12 exp[(290  30)/T] | 206-295 | Seeley et al., 1996 | DF-CIMS (g) |
| (8.0  0.5) x 10-12 | 294 |  |  |
| (9.6  1.5) x 10-12 | 298 | Bohn and Zetzsch, 1997 | PLP-A (h) |
| 3.98 x 10-12 exp [(223  16.5)/T] | 183-300 | Bardwell et al., 2003 | DF-CIMS (i) |
| (8.43  0.20) x 10-12 | 298 |  |  |
| Relative Rate Coefficients |  |  |  |
| (7.3  0.7) x 10-12 | 298 | Thrush and Wilkinson, 1981 | DF-LMR (j) |
| Branching ratios |  |  |  |
| k1/k > 0.95 | 298 | Bohn and Zetzsch, 1997 | PLP-A (h) |
| k1/k = (1  0.05) | 183-300 | Bardwell et al., 2003 | DF-CIMS (i) |
| k2/k= 0.18% (at 267 mbar N2) | 298 | Butkovskaya et al., 2005 | DF-CIMS (k) |
| k2/k= 1.78x10-5 exp[(1374  63) /T] (at 267 mbar N2) | 223-298 K |  |  |
| k2/k= {[(530  10)/T] + 8.53x10-4 x P –(1.73  0.07)}/100 (P in mbar) | 223-298 | Butkovskaya et al., 2007 | DF-CIMS (l) |

##### Comments

(a)	[HO2] was monitored by LMR. An upper limit of 4.5 x 10-30 cm6 molecule-2 s-1 was established for the rate coefficient of the potentially pressure dependent third-order channel.

(b)	[HO] was monitored.

(c)	[HO2] was monitored in excess NO by the light emitted at 1.43 m after energy transfer from O2(1) produced by a microwave discharge in NO.

(d)	[HO2] was monitored by both LMR and EPR. The rate coefficient was observed to be pressure independent over the range 2.1-16.7 mbar (1.6-12.5 Torr).

(e)	The same technique was used as in similar earlier studies (Howard and Evenson, 1977; Howard 1979) from the same laboratory. The author combined the data from the present study with that at lower temperatures from the earlier studies to derive the expression k = 3.51 x 10-12 exp[(24030)/T) cm3 molecule-1 s-1 for the temperature range 232-1271 K. The rate coefficient for the reverse reaction was also measured over the range 425-1115 K and from the two studies a value of H(HO2) = (102.5) kJ mol-1 at 298 K was derived. The value of k at 298 K tabulated is obtained by extrapolation of the high temperature expression.

(f)	[HO2] was monitored by LMR and HO radicals were scavenged by C2F3Cl. k was observed to be independent of pressure over the range 1.1-17 mbar (0.8-13 Torr).

(g)	Turbulent flow technique was used. [HO2], [HO], and [NO2] were monitored by high pressure chemical ionisation mass-spectrometry. k was found to independent of pressure over the range 93-253 mbar N2 (70-190 Torr) at 294 K.

(h)	Pulsed laser photolysis at 248 nm of H2O2/NO/O2 mixtures at total pressures of 0.1, 0.5, and 1 bar. [OH] was monitored by time resolved CW UV laser absorption in the 308 nm region.  The value of k was found to be independent of pressure. The rate of HO formation and HO2 removal were found to be identical within experimental error indicating an HO yield > 95%.

(i)	Detection of HO, HO2 and NO2 using chemical ionisation with SF6-. No pressure dependence of k between 75 and 220 Torr within the range of temperatures covered. Measurement of HO and NO2 allowed derivation of the  unity branching ratio for channel (1).

(j)	[HO] and [HO2] were monitored by LMR. The steady-state values of [HO] and [HO2] were measured in a system where their relative concentrations are related by [HO]/[HO2] = k/k(HO+H2O2). k was calculated using a rate coefficient of k(HO+H2O2) = 1.7 x 10-12 cm3 molecule-1s-1  (IUPAC, 2008).

(k)	High pressure, turbulent flow tube study of HNO3 formation. HNO3 was detected by chemical ionisation using SF6- ions and calibrated relative to its formation in the HO + NO2 reaction. Unwanted formation of HNO3 via the Reaction of HO with NO2 (both from 1) was avoided by using excess NO or C6H12 as HO scavenger. The yield of HNO3 was found to increase in the presence of water vapour and with pressure between 133 and 533 Torr N2.

(l)	P in mbar. Same set-up as described in comment k, but with chemical amplification of the NO2 and HNO3 products via addition of CO and an extended study of the pressure dependence of the branching to HNO3. Also, HNO3 and NO2 signals were calibrated using reference standards rather than in-situ production.

## Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| k /cm3 molecule-1 s-1 | 8.5 x 10-12 | 298 |
| k /cm3 molecule-1 s-1 | 3.45 x 10-12 exp(270/T) | 200-400 |
| k2/k | {[(530  10)/T] + 4.8x10-4 x P –(1.73  0.07)}/100 (P in mbar) |  |
| Reliability |  |  |
| ( log k | ± 0.1 | 298 |
| ( (E/R) /K | ( 100 | 200-400 |
| log(k2/k) | 0.3 |  |

#### Comments on Preferred Values

The preferred value of k at 298 K is the mean of the values of Howard and Evenson (1977), Howard (1979), Leu (1979), Hack et al. (1980), Jemi-Alade and Thrush (1990), Seeley et al. (1996), Bohn and Zetzsch (1997) and Bardwell et al. (2003).  The temperature dependence was obtained by unweighted, least-squares fitting to the data reported by Howard (1979), Seeley et al. (1996) and Bardwell et al. (2003). The pre-exponential factor has been adjusted to fit the preferred value of k at 298 K.

Measurements of the branching ratios for HO formation (Bohn and Zetzsch, 1997), NO2 formation (Bardwell et al. 2003) and HNO3 formation (Butkovskaya et al., 2005, 2007) show that the reaction proceeds almost entirely via channel (1) with less than 1% via a termolecular process to form HNO3 under all atmospheric conditions. Although the possibility for HNO3 formation via rearrangement of an initially formed HOONO adduct has been confirmed in the theoretical study of Zhang and Donanhue (2006), further studies of the formation of HNO3 in the title reaction are urgently required to reduce uncertainties. The yield of HNO3 increases by added water, according to a factor (1+ 2 x 10-17 [H2O]( at 298 K where [H2O] is in molecule cm-3 (Butkovskaya et al., 2009). This effect could be attributed to a chaperone mechanism involving HO2-H2O complexes or to large energy transfer efficiency of water as a collision partner of vibrationally excited HNO3 (see Guide to the Gas Phase Data Sheets).

##### References

Bardwell, M.W., Bacak, A., Raventos, M.T., Percival, C.J., Sanchez-Reyna, G., and Shallcross, D.E.: Phys. Chem. Chem. Phys., 5, 2381, 2003.

Bohn, B., and Zetzsch, C.: J. Phys. Chem. A 101, 1488, 1997.

Butkovskaya, N.I., Kukui, A., Pouvesle, N., and Le Bras, G.: J. Phys. Chem. A, 109, 6509, 2005.

Butkovskaya, N., Kukui, A., and Le Bras, G.: J. Phys. Chem. A, 111, 9047, 2007.

Butkovskaya, N., Rayez, M.-T., Rayez, J.-C., Kukui, A., and Le Bras, G.: J. Phys. Chem. A, 113, 11327, 2009.

Gershenzon, Yu. M., Il’in, S. D., Politenkova, G. G., and Remorov, R. G.:  Chem. Phys. Rep. 18, 91, 1999.

Glaschick-Schimpf, Leiss, A., Monkhouse, P. B., Schurath, U., Becker, K. H., and Fink, E. H.:  Chem. Phys. Lett. 67, 318, 1979.Howard, C. J., and Evenson, K. M.: Geophys. Res. Lett. 4, 437, 1977.

Hack, W., Preuss, A. W., Temps, F., Wagner, H. Gg., and Hoyermann, K.: Int. J. Chem. Kinet. 12, 851, 1980.

Howard, C. J.: J. Chem. Phys. 71, 2352, 1979.

Howard, C. J.:  J. Am. Chem. Soc. 102, 851, 1980.

Jemi-Alade, A. A., and Thrush, B. A.:  J. Chem. Soc. Faraday Trans. 86, 3355, 1990.

Leu, M.-T.; J. Chem. Phys. 70, 1662, 1979.

Seeley, J. V., Meads, R. F., Elrod, M. J., and Molina, M. J.:  J. Phys. Chem. 100, 4026, 1996.

Thrush, B. A., and Wilkinson, J. P. T.:  Chem. Phys. Lett. 81, 1, 1981.

Zhang, J., and Donanhue, N. M.: J. Phys. Chem. A, 110, 6898, 2006.