IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet I.A3.47 NOx17

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this datasheet is: Atkinson, R., Baulch, D. L., Cox, R. A., Crowley, J. N., Hampson, R. F., Hynes, R. G., Jenkin, M. E., Rossi, M. J., and Troe, J.: Atmos. Chem. Phys. 4, 1461, 2004; IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This data sheet last evaluated: November 2017; last change in preferred values: June 2012.

HO2NO2 + M HO2 + NO2 + M

H = 100.5 kJ·mol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 1.5 x 10-20 [N2] | 298 | Cox and Patrick, 1979 | (a) |
| 5.2x10-6 exp[-(10014±250)/T] [N2] | 261-295 | Graham et al., 1978 | (b) |
| 1.3 x 10-20 [N2] | 298 |  |  |
| 4.1x10-5 exp[-(10645±260)/T] [N2] | 261-307 | Zabel, 1995 | (c) |
| 1.2 x 10-20 [N2] | 298 |  |  |
| 2.1 x 10-18 [N2] | 348 | Gierczak et al., 2005 | (d) |

# Comments

(a)	Derived from measurements of the reverse reaction.  Conversion of the data to the dissociation reaction of HO2NO2 using the equilibrium constant Kc = 1.68 x 1028 exp(-11977/T) cm3 molecule-1 from Uselman et al. (1978) and comparison with earlier dissociation data.

(b)	FTIR study in a 5800 L chamber.  Measurements were made at 1-7 Torr of N2.  At higher pressures , deviations from low pressure behavior were observed.

(c)	FTIR study in a 420 L chamber.  The pressure range was 10-772 Torr.  The falloff curve was evaluated with Fc = 0.5.

(d)	Pulsed LIF experiments. NO was added to HO2NO2 in equilibrium with HO2 and NO2, and OH was detected. Temperatures between 330 and 350 K and pressures of N2 between 33 and 66 mbar were applied. The resulting rate coefficients agree well with the extrapolated results from Zabel (1995).

# Preferred Values

k0 = 1.3 x 10-20 [N2] s-1 at 298 K.

k0 = 4.1 x 10-5 exp(-10650/T) [N2] s-1 over the temperature range 260-300 K.

Comments on Preferred Values

The preferred values are from the study of Zabel (1995), and are in close agreement with those from Graham et al. (1978). The data from Zabel (1995) provide a consistent picture with other RO2NO2 dissociation reactions.  Falloff curves are constructed with Fc = 0.5. A revised equilibrium constant Kc = 4.76 x 1026 exp(-10900/T) cm3 molecule-1 from Burkholder et al (2015), together with the preferred value of the present evaluation for the reverse reaction would lead to k0 = 6.7 x  10-5(T/300)-3.1 exp(-10900/T) [N2] s-1 and k0 = 8.7 x 10-21 [N2] s-1 at 298 K.

# High-pressure rate coefficients

Rate coefficient data

| k/s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| >0.018 | 278 | Graham et al., 1978 | (a) |
| 5.7 x 1015 exp(-11170/T) | 261-307 | Zabel, 1995 | (b) |
| 0.30 | 298 |  |  |

# Comments

(a)	See comment (b) for k0. This is a lower limit since a linear Lindemann-Hinshelwood evaluation of the falloff curve (i.e. Fc = 1) was made for the pressure range 10-760 Torr of N2.

(b)	See comment (c) for k0.

# Preferred Values

k = 0.31 s-1 at 298 K.

k = 6.0 x 1015 exp(-11170/T) s-1 over the temperature range 260-300 K.

Comments on Preferred Values

See Comments on Preferred Values for k0. The data from Zabel (1995) were reevaluated with Fc = 0.4 such as used for the falloff curves of the reverse reaction HO2 + NO2 + M  HO2NO2 + M, because Fc is identical for the forward and backward reaction. Since the measurements from Zabel (1995) were made closer to the low pressure limit, only the extrapolition to k is noticeably influenced by the change of the used Fc. A revised equilibrium constant Kc = 4.76 x 1026 exp(-10900/T) cm3 molecule-1 from Burkholder et al (2015), together with the preferred value of the present evaluation for the reverse reaction would lead to k = 1.9 x 1015 exp(-10900/T) [N2] s-1 and k= 0.25 s-1 at 298 K.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| k0/s-1 | 1.3 x 10-20 [N2] | 298 |
| k0/s-1 | 4.1 x 10-5 exp(-10650/T) [N2] | 260-300 |
| k/s-1 | 0.31 | 298 |
| k/s-1 | 6.0 x 1015 exp(-11170/T) [N2] | 260-300 |
| k(1 bar N2)/s-1 | 6.2 x 10-2 | 298 |
| Fc | 0.4 | 260-300 |
| Reliability |  |  |
| log k0 | ± 0.3 | 298 |
| E0/R | ± 500 K | 260-300 |
| log k | ± 0.5 | 298 |
| E/R | ± 500 K | 260-300 |

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((4.1e-5*exp(-10650/T))*M*(6.0e15*exp(-11170/T)))/((4.1e-5*exp(-10650/T))*M+(6.0e15*exp(-11170/T)))*10^(log10(0.4)/(1+(log10((4.1e-5*exp(-10650/T))*M/(6.0e15*exp(-11170/T)))/(0.75-1.27*log10(0.4)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

# References

- Burkholder,J. B. Sander, S. P.,Abbatt, J., Barker,J. R.,Huie,R. E.,Kolb, C. E. Kurylo, M. J., Orkin,

- V. L.,Wilmouth, D. M., and Wine,P. H.: Chemical Kinetics and Photochemical Data for Use in

- Atmospheric Studies, NASA Panel for Data Evaluation, Evaluation Number 18, JPL Publication

- 15-10, 2015.

Cox, R. A., and Patrick, K.: Int. J. Chem. Kinet. 11, 635, 1979.

Gierczak, T., Jiménez, E., Riffault, V., Burkholder, J. B., and Ravishankara, A. R.: J. Phys. Chem. A 109, 586, 2005.

Graham, R. A., Winer, A. M., and Pitts, J. N.: Chem. Phys. Lett. 51, 215, 1977; J. Chem. Phys. 68, 4505, 1978.

Uselman, W. M., Levine, S. Z., Chan, W. H., Calvert, J. G., and Shaw, J. H.: Chem. Phys. Lett. 58, 437, 1978.

Zabel, F.: Z. Phys. Chem. 188, 119, 1995.