IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet NOx21

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

This data sheet updated: 16th July 2001.

NH2 + NO  N2 + H2O	  (1)

 N2H + HO          (2)

 N2 + H + HO	  (3)

H(1) = -520.8 kJ mol-1

H(3) = -23.8 kJ mol-1

Rate coefficient data (k = k1 + k2 + k3)

| k / cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 2.7 x 10-11 | 300 | Gordon et al., 1971 | (a) |
| (8.3 1.7) x 10-12 | 298 | Gehring et al., 1973 | DF-MS (b) |
| 2.1 x 10-8 T –1.25 | 300-500 | Lesclaux et al., 1975 | FP (c) |
| (1.8  0.3) x 10-11 | 300 |  |  |
| (2.1  0.2) x 10-11 | 298 | Hancock et al., 1979 | FP-LIF |
| (1.7  0.4) x 10-11 | 298 | Sarkisov et al., 1978 | FP (d) |
| 4.5 x 10-7 T –1.85 | 210-500 | Hack et al., 1979 | DF-LIF |
| 9.7 x 10-12 | 298 |  |  |
| 2.77 x 10-7 T –1.67 | 216-480 | Stief et al., 1982 | FP-LIF (e) |
| (2.10  0.31) x 10-11 | 298 |  |  |
| 4.4 x 10-5 T –2.3 exp(-684/T) | 294-1215 | Silver and Kolb, 1982 | DF-LIF (f) |
| (9.59  2.4) x 10-11 | 298 |  |  |
| (1.7  0.5) x 10-11 | 295 | Andresen et al., 1982 | PLP (g) |
| (1.81  0.12) x 10-11 | 297 | Whyte and Phillips, 1983 | PLP-LIF |
| 1.7 x 10-11 | 298 | Dreier and Wolfrum ,1985 | PLP (h) |
| (1.3  0.4) x 10-11 | 298 |  |  |
| 1.3·10-8 T –(1.170.25) | 294-1027 | Atakan et al., 1989, 1990 | PLP-LIF (i) |
| (1.67  0.25) x 10-11 | 298 |  |  |
| 5.6 x 10-6 T -2.2 | 295-620 | Bulatov et al., 1989 | FP (d) |
| 2.2 x 10-11 | 298 | Pagsberg et al., 1991 | (j) |
| 5.43 T -4.02 exp(-1034/T) | 293-612 | Wolf et al., 1994 | PLP-LIF |
| (1.9  0.1) x 10-11 | 295 |  |  |
| 2.2 x 10-12 exp[(525  80)/T)] | 297-673 | Diau et al., 1994 | PLP (k) |
| (1.45  0.08) x 10-11 | 297 |  |  |
| 1.4 x 10-11 | 298 | Yu and Lin, 1994 | PLP (d) |
| (1.9  0.3) x 10-11 | 299 | Imamura and Washida, 1995 | PLP (l) |
| 1.38 x 10-10 T -0.57 exp(300/T) | 305-1037 | Park and Lin, 1997 | PLP-MS (m) |
| (8.59  0.40) x 10-12 | 305 |  |  |
| (k2 + k3) = 1.4 x 10-14 T 0.53 exp(502/T) | 300-1000 |  |  |
| k1 = 1.37 x 10-9 T -0.93 exp(192/T) | 300-1000 |  |  |
| 1.65 x 10-7 T -1.54 exp(-93/T) | 203-813 | Wolf et al., 1997 | PLP-LIF (n) |
| (1.87  0.02) x 10-11 | 295 |  |  |
| Branching Ratios |  |  |  |
| (k2 + k3)/k = 0.10  0.02 | 295 | Bulatov et al., 1989 | FP-AS (d) |
| (k2 + k3)/k = 0.10 ± 0.025 | 300 | Atakan et al., 1989, 1990 | PLP-LIF (i) |
| k1/k = 0.85 | 295 | Stephens et al., 1993 | PLP-AS (o) |
| (k2 + k3)/k = 0.10 | 295 |  |  |
| k1/k = 0.7  0.2 | 298 | Quandt and Hershberger, 1996 | PLP (p) |
| k1/k = 0.90 | 300 | Park and Lin, 1996, 1997 | PLP-MS (q) |
| (k3 + k4)/k = 0.10 | 300 |  |  |
| (k2 + k3)/k = 0.090 ± 0.002 | 298 | Wolf, Yang, and Durant, 1997 | DF-MS (r) |

##### Comments

(a)	Pulse radiolysis of NH3-NO mixtures at 670 mbar (500 Torr) total pressure. [NH2] monitored by time-resolved absorption spectroscopy.

(b)	NO2 was added to an excess of H atoms followed by addition of NH3. Analysis by time-of-flight mass-spectrometry. Vibrationally excited H2O was observed as a product. The addition product NH2NO was also observed to the extent of 5% of the N2 formed.

(c)	[NH2] was monitored by absorption spectroscopy. No pressure dependence of k was observed over the range 2.7-930 mbar (2-700 Torr) of N2.

(d)	[NH2] was monitored by intracavity laser absorption.

(e)	[NH2] was monitored by LIF. Production of HO was looked for by resonance fluorescence and found under static conditions but not under flowing conditions. An upper limit of (k2 + k3)/k  0.22 was obtained.

(f)	[NH2] was monitored by LIF. HO production was detected by RF or by LIF. A rate coefficient ratio (k2 + k3)/k = 0.4  0.1 was obtained but the data were later reanalysed by the authors to give a value of 0.12. H-atom production was looked for using RF; an upper limit of 0.05 was found for the branching ratio of channels leading to H atoms.

(g)	The rate coefficient was obtained by monitoring the production of vibrationally excited H2O by observation of infrared and visible emissions. RA and LIF were used to monitor [HO].  k2/k  0.65 was obtained with the H-atom yield  being  0.05.

(h)	[NH2] and [N2] were monitored by coherent anti-Stokes Raman spectroscopy (CARS). Another independent value of the rate constant was obtained by monitoring the IR fluorescence of vibrationally excited H2O.

(i)	[HO] was monitored by LIF. The HO yield was determined by using HO production from H2O2 photolysis to calibrate for [HO].

(j)	Pulse radiolysis, of Ar-SF6-NH3-NO mixtures at a total pressure of ~ 50 mbar. [NH2] and [HO] were monitored by time-resolved UV absorption spectroscopy. The observed yield of HO was small suggesting a value of (k2+k3)/k  0.07.

(k)	[NH2] was monitored by cavity ring down absorption spectroscopy at 537.6 nm.

(l)	[NH2] was monitored by photoionization mass spectrometry.

(m)	Pulsed laser photolysis of NH3-NO mixtures. [H2O] and [NO] were monitored by time-resolved mass-spectrometry and values of k were derived from detailed modelling of the [H2O] and [NO] profiles. In a subsequent publication24 the data are reanalysed and expressions derived giving k1 and (k2+k3) up to temperatures above 2000 K but these expressions agree very closely with those cited here for T  1000 K.

(n)	The expression k = 2.66 x 10-8 T –1.27 cm3 molecule-1 s-1 also provides a good fit to the data.

(o)	Pulsed laser photolysis of NH3-NO mixtures. [H2O], [HO], [NH3], and [NH2] were monitored by infrared absorption spectroscopy.

(p)	Pulsed laser photolysis of NH3-NO mixtures. [H2O] and [NH2] were monitored by infrared absorption spectroscopy. This was a preliminary study to an investigation of the branching in the NH2+NO2 reaction.

(q)	Pulsed laser photolysis of NH3-NO-CO mixtures. Time-resolved mass-spectrometric measurements of [H2O], [NO] and of [CO2] produced by scavenging of HO by the CO.

(r)	NH2 radicals were generated by the F+NH3 reaction in a flow He carrier gas to which an NO-CO-He mixture was added downstream of the NH2 generation point. [N2] and [CO2] were determined by mass-spectrometry.  The ND2+NO reaction was also studied.

## Preferred Values

k = 1.6 x 10-11 cm3 molecule-1 s-1 at 298 K.

k = 1.6 x 10-11 (T/298)-1.4 cm3 molecule-1 s-1 over the range 210-500 K.

k1/k = 0.9 at 298 K.

(k2 + k3)/k = 0.1 at 298 K.

### Reliability

log k =  0.15 at 298 K

n =  0.5.

k1/k =  0.05 at 298 K.

(k2 + k3)/k =  0.03 at 298 K.

#### Comments on Preferred Value

The values of the rate coefficients obtained in the pulsed photolysis studies are significantly higher than those obtained using the discharge flow technique. The reason for this discrepancy is not known. The preferred value at 298 K is therefore taken as the mean of the values reported in the below references. The temperature dependence is based on the data below 500 K in the temperature dependence studies of Lesclaux et al. (1975), Hack et al. (1979), Stief et al. (1982), Silver and Kolb (1982), Atakan et al. (1989; 1990), Bulatov et al. (1989), Wolf et al. (1994; 1997), Diau et al. (1994) and Park and Lin (1997).

The preferred values of the branching ratios are based on the direct measurements of Atakan et al. (1989; 1990), Stephens et al. (1993), Park and Lin (1996; 1997) and Wolf et al. (1997). The less direct study of Bulatov et al. (1989) and the preliminary study of Quandt and Hershberger (1996) are in satisfactory agreement with the preferred values.

There are now reasonably consistent measurements of the branching ratios up to ~1700 K. The value of (k2+k3)/k remains virtually independent of temperature over the range covered by our recommendations but begins to rise steadily at temperatures in excess of 600K reaching a value of ~0.53 at 1700 K (Park and Lin, 1999).

##### References

Andresen, P., Jacobs, A., Kleinermanns, C. and Wolfrum, J.: 19th Symp. (Int.) Combust., 11, 1982.

Atakan, B., Jacobs, A., Wahl, W., Weller, R. and Wolfrum, J.: Chem. Phys. Lett. 155, 609, 1989.

Atakan, B., Wolfrum, J. and Weller, R.: Ber. Bunsenges. Phys. Chem., 94, 1372, 1990.

Bulatov, V. P., Ioffe, A. A., Lozovsky, V. A. and Sarkisov, O. M.: Chem. Phys. Lett., 162, 141, 1989.

Diau, E. W., Yu, T., Wagner, M. A. G. and Lin, M. C.: J. Phys. Chem., 98, 4034, 1994.

Dreier, T. and Wolfrum, J.: 20th Symp. (Int.) Combust., 695, 1985.

Gehring, M., Hoyermann, K., Schacke, H. and Wolfrum, J.: 14th Symp. (Int.) Combust., 99, 1973.

Gordon, S., Mulac, W. and Nangia, P.: J. Phys. Chem., 75, 2087, 1971.

Hack, W., Schacke, H., Schroter, M. and Wagner, H. Gg.: 17th Symp. (Int.) Combust., 505, 1979.

Hancock, G., Lange, W., Lenzi, M. and Welge, K. H.: Chem. Phys. Lett., 33, 168, 1975.

Imamura, T. and Washida, N.: Laser Chem., 16, 43, 1995.

Lesclaux, R., Khe, P. V., Dezauzier, P. and Soulignac, J. C.: Chem. Phys. Lett., 35, 493, 1975.

Pagsberg, P., Sztuba, B., Ratajczak, E. and Sillesen, A.: Acta Chem. Scand., 45, 329, 1991.

Park, J. and Lin, M. C.: J. Phys. Chem., 100, 3317, 1996.

Park, J. and Lin, M. C.: J. Phys. Chem., 101, 5, 1997.

Park, J. and Lin, M. C.: J. Phys. Chem. A, 103, 8906, 1999.

Quandt, R. W. and Hershberger, J. F.: J. Phys. Chem., 100, 9407, 1996.

Sarkisov, O. M., Cheskis, S. G. and Sviridenkov, E. A.: Bull. Acad. Sci. USSR, Chem. Ser., 27, 2336, Eng. trans., 1978.

Silver, J. A. and Kolb, C. E.: J. Phys. Chem., 86, 3240, 1982.

Stephens, J. W., Morter, C. L., Farhat, S. K., Glass, G. P. and Curl, R. F.: J. Phys. Chem., 97, 8944, 1993.

Stief, L. J., Brobst, W. D., Nava, D. F., Barkowski, R. P. and Michael, J. V.: J. Chem. Soc. Faraday Trans., 2, 78, 1391, 1982.

Whyte, A. R. and Phillips, L. F.: Chem. Phys. Lett., 102, 451, 1983.

Wolf, M., Yang, D. L. and Durant, J. L.: J. Photochem. Photobiol., 80, 85, 1994.

Wolf, M., Yang, D. L. and Durant, J. L.: J. Phys. Chem. A, 101, 6243, 1997.

Yu, T. and Lin, M. C.: J. Phys. Chem., 98, 2105, 1994.