IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet I.A3.56 NOx26

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this datasheet is: Atkinson, R., Baulch, D. L., Cox, R. A., Crowley, J. N., Hampson, R. F., Hynes, R. G., Jenkin, M. E., Rossi, M. J., and Troe, J.: Atmos. Chem. Phys. 4, 1461, 2004; IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This data sheet last evaluated: November 2017; last change in preferred values: June 2012.

N2O3 + M  NO + NO2 + M

H = 40.6 kJ·mol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 5.0 x 1014 T -(8.7 ± 0.9) exp(-4880/T)[Ar] | 225-260 | Markwalder et al., 1993 | (a) |

# Comments

(a)	CO2 laser-induced temperature jump measurements with NO2-N2O4-N2O3-NO-SiF4-Ar equilibrium mixtures.  The subsequent relaxation toward equilibrium was monitored by UV absorption of N2O3 at 253 nm.  Dissociation rate coefficients were derived from the measured recombination rate coefficients and the equilibrium constant from Chao et al. (1974) of Kc = 1.8 x 1029 T -1 exp(-4880/T) molecule cm-3.  Falloff curves with M=Ar were obtained over the pressure range 0.5-200 bar and extrapolated to k0 and k with Fc = 0.6.  k0(N2)/k0 (Ar) = 1.36 was taken from Smith and Yarwood (1987) (see reaction NO + NO2 + M  N2O3 + M).

# Preferred Values

k0 = 1.6 x 10-14 [N2] s-1 at 298 K.

k0 = 1.9 x 10-7 (T/300)-8.7 exp(-4880/T) [N2] s-1 over the temperature range 225-300 K.

Comments on Preferred Values

The preferred values are based on the data of Markwalder et al. (1993), which are consistent with a theoretical analysis of the results (leading to collision efficiencies c(Ar) = 0.3).  The preferred values correspond to an analysis of the falloff curve with Fc = 0.6 and the value of k given below.

High-pressure rate coefficients

Rate coefficient data

| k/s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 4.8 x 1014 T (0.4 ± 0.1) exp(-4880/T) | 225-260 | Markwalder et al., 1993 | (a) |

# Comments

(a)	See comment (a) for k0.

# Preferred Values

k = 3.6 x 108 s-1 at 298 K.

k = 4.7 x 1015 (T/300)0.4 exp(-4880/T) s-1 over the temperature range 225-300 K.

Comments on Preferred Values

The preferred values are based on the values of Markwalder et al. (1993) converted to dissociation data with the equilibrium constant from Chao et al. (1974).

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| k0/s-1 | 1.6 x 10-14 [N2] | 298 |
| k0/s-1 | 1.9 x 10-7 (T/300)-8.7 exp(-4880/T) [N2] | 225-300 |
| k/s-1 | 3.6 x 108 | 298 |
| k/s-1 | 4.7 x 1015 (T/300)0.4 exp(-4880/T) | 225-300 |
| k(1 bar N2)/s-1 | 3.6 x 105 | 298 |
| Fc | 0.6 | 225-300 |
| Reliability |  |  |
| log k0 | ± 0.4 | 225-300 |
| E0/R | ± 500 K | 298 |
| log k | ± 0.3 | 225-300 |
| E/R | ± 400 K | 298 |

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((1.9e-7*(T/300)^-8.7*exp(-4880/T))*M*(4.7e15*(T/300)^0.4*exp(-4880/T)))/((1.9e-7*(T/300)^-8.7*exp(-4880/T))*M+(4.7e15*(T/300)^0.4*exp(-4880/T)))*10^(log10(0.6)/(1+(log10((1.9e-7*(T/300)^-8.7*exp(-4880/T))*M/(4.7e15*(T/300)^0.4*exp(-4880/T)))/(0.75-1.27*log10(0.6)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

# References

Chao, J., Wilhoit, R. C., and Zwolinski, B. J.: Thermochim. Acta 10, 359, 1974.

Markwalder, B., Gozel, P., and van den Bergh, H.: J. Phys. Chem. 97, 5260, 1993.

Smith, I. W. M., and Yarwood, G.: Faraday Disc. Chem. Soc. 84, 205, 1987.