### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.2 HI2

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Gas Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: December 2007; last change to preferred values: June 2006.

O3  + ice

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients:  |  |  |  |
|  < 1 x 10-4 | 195 | Leu, 1988 | CWFT-MS (a) |  |
|  < 1 x 10-6 | 195-262 | Dlugokencky and Ravishankara, 1992 | CWFT-CL (b) |  |
|  < 6 x 10-5 | 183 | Kenner et al., 1993 | CWFT-MS (c) |  |
|  = 2 x 10-8 - 4 x 10-10 | 223, 258 | Langenberg and Schurath, 1999 | (d) |  |

# Comments

(a)	Ice film made by vapour deposition. No uptake of O3 on pure ice detected

(b)	Low pressure flow tube (1.33 mbar He). 2 mm thick ice film formed by freezing liquid water. O3 was varied between 108 and 1012 molecule cm-3. No detectable O3 loss on pure ice surfaces. Addition of e.g. sulphite or nitric acid prior to freezing induced temporary uptake.

- 4-7 m thick ice film made by vapour deposition. No uptake of O3 on pure ice detected.

- Fused silica gas chromatographic column used as flow tube. Ice films were prepared by vapour deposition and were 6.8 – 8.1 m thick. O3 (20-1000nbar) was detected using chemiluminescence. The O3 uptake coefficient was found to be dependent on [O3], with higher values obtained at lower [O3]. Data at 223 K could be parameterised using  = A/{(1+B)C}, whereby A = 5.5 x 10-8, B = 0.08  and C = the O3 concentration in mbar.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  | < 1  10-8 | 220 - 260 |

Reliability

|  log () | 0.7 |  |
| --- | --- | --- |

##### Comments on Preferred Values

The four studies of the uptake on ozone to ice surfaces show that this process is very inefficient. Only the experiments of Langenberg and Schurath (1999), designed to measure weak interactions, were able to detect uptake of ozone and their data provide the basis of the recommendation. Langenberg and Schurath provided a parameterisation of the [O3] dependent uptake coefficient at 223 K (see note (d) above), but were unable to treat data at 258 K in a similar fashion. For this reason, and also because the true surface area of the ice film could not be determined, an upper limit of 1 x 10-8 is preferred.

# References

Dlugokencky, E. J., and Ravishankara, A. R.: Geophys. Res. Lett. 19, 41-44, 1992.

Langenberg, S., and Schurath, U.: Geophys. Res. Lett. 26, 1695-1698, 1999.

Leu, M. T.: Geophys. Res. Lett. 15, 851-854, 1988.

Kenner, R. D., Plumb, I. C., Ryan, K. R.: Geophys. Res. Lett. 20, 193-196, 1993.