# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet P15

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet updated: 16th May 2002.

C2H5ONO2 + h  products

Primary photochemical transitions

| Reaction | H298/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| C2H5ONO2 + h  C2H5O + NO2 (1) | 171.7 | 697 |
|  CH3CHO + HONO (2) | -91.3 |  |
|  C2H5ONO + O(3P) (3) | 299.4 | 400 |

Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 270-315 | Roberts and Fajer, 19891 | (a) |
| 185-330 | Turberg et al., 19902 | (b) |
| 265-340 | Zhu and Ding, 19973 | (c) |
| 265-340 | Clemitshaw et al., 19974 | (d) |
| 265-340 | Talukdar et al., 19975 | (e) |

Quantum yield data ( = 1 + 2 + 3)

| Measurement | Wavelength range/nm | Reference | Comments |
| --- | --- | --- | --- |
| 1 = 1.0 ± 0.1 | 308 | Zhu and Ding, 19973 | (f) |

Comments

(a)	Absorption cross-sections were measured in a 10.2 cm pathlength cell, using a single-beam spectrometer with a photometric accuracy of ±0.5%.  Numerical data for cross-sections are available from ref. 6.

(b)	Absorption cross-sections were measured in cells of 2 cm and 10 cm pathlengths with a range of pressures of C2H5ONO2.  The spectral resolution was not specified.

(c)	Cross-sections measured at 10 nm intervals, between 238 K and 298 K, using cavity ring- down spectroscopy.  Absorption cross-sections were obtained by measuring optical loss as a function of sample gas pressure (0.013 mbar to 18 mbar).  The purity of ethyl nitrate was checked by FTIR and cavity ring-down spectroscopy.

(d)	Absorption cross-sections were measured with a dual-beam diode array spectrometer, with a spectral resolution of approximately 0.6 nm, over the temperature range 233 K to 298 K.  The purity of the ethyl nitrate was checked by NMR and FTIR.

(e)	Absorption cross-sections were measured with a diode-array spectrometer at 298 K and six other temperatures in the range 240 K to 360 K.  Absorbances were measured in 80 nm blocks which were assembled to construct the spectrum.  Corrections were made for contributions to the spectrum from NO2 present in the ethyl nitrate.

(f)	Excimer laser used to photodissociate ethyl nitrate in a cavity ring-down spectrometer.  Time-resolved spectra of products observed.  Only NO2 found as product, with undetectable yields of HONO and C2H5ONO.  Quantum yield measurements were made at 278 K, 283 K, 288 K, 293 K and 298 K with ethyl nitrate pressures of 1.3 mbar to 13 mbar in a buffer gas of N2 at total pressures of 16 mbar to 1 bar.  1 was found to be pressure and temperature independent.

Preferred Values

Absorption cross-sections at 298 K and their temperature dependence

over the ranges 233 K to 360 K and 235 nm to 340 nm

| /nm | 1020 /cm2 | 103B/K-1 | /nm | 1020 /cm2 | 103 B/K-1 |
| --- | --- | --- | --- | --- | --- |
| 185 | 1710 |  | 265 | 3.6 | 2.9 |
| 190 | 1710 |  | 270 | 3.1 | 3.1 |
| 195 | 1490 |  | 275 | 2.7 | 3.3 |
| 200 | 1140 |  | 280 | 2.2 | 3.6 |
| 205 | 738 |  | 285 | 1.7 | 3.8 |
| 210 | 400 |  | 290 | 1.2 | 4.2 |
| 215 | 195 |  | 295 | 0.85 | 4.7 |
| 220 | 91 |  | 300 | 0.55 | 5.1 |
| 225 | 45 |  | 305 | 0.33 | 5.8 |
| 230 | 24 |  | 310 | 0.19 | 6.7 |
| 235 | 11.9 | 1.4 | 315 | 0.10 | 7.9 |
| 240 | 7.7 | 2.8 | 320 | 0.051 | 8.6 |
| 245 | 5.4 | 2.9 | 325 | 0.026 | 10.4 |
| 250 | 4.5 | 2.8 | 330 | 0.012 | 12.9 |
| 255 | 4.1 | 2.6 | 335 | 0.0049 | 14.1 |
| 260 | 3.9 | 2.6 | 340 | 0.0025 | 15.6 |

The temperature variation of the absorption cross-section at a particular wavelength in the range 240 nm to 340 nm is expressed as ln (T) - ln (298 K) = B(T-298).

Quantum Yields

1 = 1.0 ± 0.1 at 308 nm, independent of pressure over the temperature range 278 K to 298 K.

Comments on Preferred Values

The preferred values of the cross-sections at 298 K are those obtained by Turberg et al.2 over the range 185 nm to 230 nm, where this is the only study, and for the range 235 nm to 340 nm averages are taken of the values from all of the five studies1-5 at the wavelengths where they overlap.

The temperature variation of the cross-sections has been studied by Zhu and Ding,3 Clemitshaw et al.4 and Talukdar et al.5  These studies together cover the temperature range 233 K to 360 K and the wavelength range 235 nm to 340 nm.  It is found in all of the studies that the temperature variation of  can be expressed as ln (,T) - ln (, 298 K) = B()(T-298).  The results from the three studies3-5 are in good agreement and the preferred values of B have been obtained by averaging values from the three studies.3-5

The only direct measurement of the quantum yield is that of Zhu and Ding.3  Their finding that at 308 nm the sole photodissociation channel was that leading to NO2 production with a quantum yield of unity is accepted for our preferred value of the quantum yield.  It is in accord with the studies of Luke et al.7,8 who concluded that the measured rates of NO2 production from ethyl nitrate photolysis in sunlight could be accounted for by assuming that 1 = 1 throughout the region 290 nm to 340 nm.  This is also supported by the measured value of unity for the same channel in the 248 nm photolysis of methyl nitrate.5

References

- J. M. Roberts and R. W. Fajer, Environ. Sci. Technol. 23, 945 (1989).

- M. P. Turberg, D. M. Giolando, C. Tilt, T. Soper, S. Mason, M. Davies, P. Klingensmith, and G. A. Takacs, J. Photochem. Photobiol. A51, 281 (1990).

- L. Zhu and C.-F. Ding, Chem. Phys. Lett. 265, 177 (1997).

- K. C. Clemitshaw, J. Williams, O. V. Rattigan, D. E. Shallcross, K. S. Law, and R. A. Cox, J. Photochem. Photobiol. A: Chemistry 102, 117 (1997).

- R. K. Talukdar, J. B. Burkholder, M. Hunter, M. K. Giles, J. M. Roberts, and A. R. Ravishankara, J. Chem. Soc. Faraday Trans. 93, 2797 (1997).

- J. M. Roberts, Atmos. Environ. 24A, 243 (1990).

- W. T. Luke and R. R. Dickerson, Geophys. Res. Lett. 15, 1181 (1988).

- W. T. Luke, R. R. Dickerson, and L. J. Nunnermacker, J. Geophys. Res. 94, 14905 (1989).