# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet P23

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: June 2011; last change in preferred values: June 2011.

CH3C(O)C(O)CH3 + h  products

## Primary photochemical transitions

| Reaction | H298/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| CH3C(O)C(O)CH3  CH3C(O) + CH3C(O) (1) |  | 390 |
|  CH3C(O) + CH3 + CO (2) |  | 338 |
|   2CH3 + 2CO (3) |  | 300 |

Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 208-476 | McMillan, 1966 | (a) |
| 230-470 | Plum et al., 1983 | (b) |
| 206-493 | Horowitz et al., 2001 | (c) |
| 184.9 | Rajakumar et al., 2008 | (d) |

Quantum yield data ( = 1 + 2 + 3)

| Measurement | Wavelength range/nm | Reference | Comments |
| --- | --- | --- | --- |
|  = 0.16 | 290-390 | Plum et al., 1983 | (e) |
| CH3CO) = 0.76(61 Torr) | 248 | Rajakumar et al., 2008 | (f) |
| = 0.79(101 Torr) |  |  |  |
| = 0.79(207 Torr) |  |  |  |
| = 0.86(302 Torr) |  |  |  |
| = 0.92(419 Torr) |  |  |  |
| = 0.90(509 Torr) |  |  |  |
| = 0.96(643 Torr) |  |  |  |

## Comments

(a)	Conventional spectrophotometric study of biacetyl absorption spectrum.

- Conventional spectrophotometric study (Cary 17-D) using biacetyl pressures of ~4 mbar to 17 mbar.  Data taken from Spectral Atlas: (http://www.atmosphere.mpg.de/enid/2295) which gives absorption cross sections read at 1- and 2-nm intervals from Fig. 1 of Plum et al (1983).

- Absorption measurements as a function of biacetyl pressure using a diode array spectrometer.  Biacetyl pressure range of 0.5–10 Torr in which no deviations from Beer–Lambert law were observed. Cross sections averaged over 1 nm intervals are listed. Reported accuracy of the biacetyl data in this work was ±4% or not less than ±1 × 10−21 cm2molecule-1, whichever was the larger.

- UV absorption measurements were made using a Hg pen-ray lamp light source at 184.9 combined with narrow bandpass filters and a photodiode detector.  The cross section determined for this wavelength was 1.46 x 10-18 cm2molecule-1. The concentration of biacetyl was determined by UV absorption at 248 nm, using the cross section of Horowitz et al. (2001).

- Rate of photolysis of biacetyl in air mixtures at atmospheric pressure measured in an environmental chamber.  The quantum yield for the photodissociation of biacetyl was obtained by comparison of the measured rate of removal of glyoxal with the rate of photolysis of NO2 under similar experimental conditions.

- Quantum yields determined from CH3CO production measured in its visible absorption band (490 - 660 nm) by CRDS following photolysis of biacetyl at 248 nm in a crossed beam pulsed laser photolysis cell. CH3CO yields were determined relative to amounts from reference reaction: HO + CH3CHO, with HO produced by co-photolysis of H2O2. Cited data for f(CH3CO) were for N2 bath gas; a rather weaker pressure dependence was found for He.

Preferred Values

## Absorption cross-sections at 298 K

| /nm | 1020 /cm2 | /nm | 1020 /cm2 | /nm | 1020 /cm2 |
| --- | --- | --- | --- | --- | --- |
| 206 | 10.30 | 303 | 1.46 | 400 | 5.12 |
| 207 | 9.86 | 304 | 1.38 | 401 | 5.19 |
| 208 | 9.14 | 305 | 1.32 | 402 | 5.26 |
| 209 | 7.97 | 306 | 1.27 | 403 | 5.38 |
| 210 | 6.74 | 307 | 1.21 | 404 | 5.54 |
| 211 | 5.82 | 308 | 1.10 | 405 | 5.75 |
| 212 | 5.18 | 309 | 0.95 | 406 | 6.00 |
| 213 | 4.70 | 310 | 0.82 | 407 | 6.26 |
| 214 | 4.29 | 311 | 0.71 | 408 | 6.47 |
| 215 | 3.90 | 312 | 0.62 | 409 | 6.59 |
| 216 | 3.55 | 313 | 0.54 | 410 | 6.69 |
| 217 | 3.21 | 314 | 0.48 | 411 | 6.82 |
| 218 | 2.90 | 315 | 0.44 | 412 | 6.97 |
| 219 | 2.58 | 316 | 0.41 | 413 | 7.11 |
| 220 | 2.26 | 317 | 0.38 | 414 | 7.31 |
| 221 | 1.96 | 318 | 0.36 | 415 | 7.47 |
| 222 | 1.70 | 319 | 0.34 | 416 | 7.57 |
| 223 | 1.50 | 320 | 0.33 | 417 | 7.62 |
| 224 | 1.35 | 321 | 0.33 | 418 | 7.51 |
| 225 | 1.27 | 322 | 0.32 | 419 | 7.39 |
| 226 | 1.23 | 323 | 0.30 | 420 | 7.37 |
| 227 | 1.24 | 324 | 0.26 | 421 | 7.32 |
| 228 | 1.28 | 325 | 0.23 | 422 | 7.25 |
| 229 | 1.34 | 326 | 0.21 | 423 | 7.24 |
| 230 | 1.41 | 327 | 0.20 | 424 | 7.13 |
| 231 | 1.47 | 328 | 0.19 | 425 | 6.98 |
| 232 | 1.53 | 329 | 0.19 | 426 | 6.81 |
| 233 | 1.59 | 330 | 0.20 | 427 | 6.57 |
| 234 | 1.68 | 331 | 0.20 | 428 | 6.43 |
| 235 | 1.80 | 332 | 0.21 | 429 | 6.34 |
| 236 | 1.92 | 333 | 0.20 | 430 | 6.31 |
| 237 | 2.09 | 334 | 0.22 | 431 | 6.40 |
| 238 | 2.15 | 335 | 0.23 | 432 | 6.63 |
| 239 | 2.21 | 336 | 0.25 | 433 | 6.78 |
| 240 | 2.29 | 337 | 0.26 | 434 | 6.78 |
| 241 | 2.39 | 338 | 0.28 | 435 | 6.72 |
| 242 | 2.54 | 339 | 0.30 | 436 | 6.56 |
| 243 | 2.69 | 340 | 0.30 | 437 | 6.40 |
| 244 | 2.80 | 341 | 0.32 | 438 | 6.42 |
| 245 | 2.89 | 342 | 0.35 | 439 | 6.28 |
| 246 | 2.94 | 343 | 0.37 | 440 | 6.51 |
| 247 | 2.99 | 344 | 0.39 | 441 | 6.67 |
| 248 | 3.05 | 345 | 0.41 | 442 | 6.99 |
| 249 | 3.15 | 346 | 0.44 | 443 | 7.23 |
| 250 | 3.31 | 347 | 0.47 | 444 | 6.85 |
| 251 | 3.48 | 348 | 0.50 | 445 | 6.49 |
| 252 | 3.60 | 349 | 0.53 | 446 | 5.90 |
| 253 | 3.68 | 350 | 0.57 | 447 | 5.43 |
| 254 | 3.73 | 351 | 0.61 | 448 | 5.01 |
| 255 | 3.75 | 352 | 0.65 | 449 | 4.33 |
| 256 | 3.78 | 353 | 0.68 | 450 | 4.06 |
| 257 | 3.84 | 354 | 0.73 | 451 | 3.44 |
| 258 | 3.94 | 355 | 0.77 | 452 | 3.20 |
| 259 | 4.09 | 356 | 0.82 | 453 | 2.65 |
| 260 | 4.27 | 357 | 0.86 | 454 | 2.16 |
| 261 | 4.41 | 358 | 0.92 | 455 | 1.72 |
| 262 | 4.46 | 359 | 0.97 | 456 | 1.39 |
| 263 | 4.49 | 360 | 1.02 | 457 | 1.14 |
| 264 | 4.49 | 361 | 1.08 | 458 | 0.85 |
| 265 | 4.48 | 362 | 1.19 | 459 | 0.73 |
| 266 | 4.49 | 363 | 1.26 | 460 | 0.55 |
| 267 | 4.54 | 364 | 1.33 | 461 | 0.45 |
| 268 | 4.63 | 365 | 1.41 | 462 | 0.36 |
| 269 | 4.81 | 366 | 1.49 | 463 | 0.28 |
| 270 | 4.95 | 367 | 1.57 | 464 | 0.22 |
| 271 | 5.00 | 368 | 1.66 | 465 | 0.18 |
| 272 | 4.98 | 369 | 1.76 | 466 | 0.14 |
| 273 | 4.92 | 370 | 1.85 | 467 | 0.12 |
| 274 | 4.85 | 371 | 1.94 | 468 | 0.10 |
| 275 | 4.76 | 372 | 2.02 | 469 | 0.08 |
| 276 | 4.70 | 373 | 2.10 | 470 | 0.07 |
| 277 | 4.68 | 374 | 2.17 | 471 | 0.06 |
| 278 | 4.67 | 375 | 2.25 | 472 | 0.05 |
| 279 | 4.68 | 376 | 2.33 | 473 | 0.04 |
| 280 | 4.71 | 377 | 2.41 | 474 | 0.04 |
| 281 | 4.73 | 378 | 2.50 | 475 | 0.03 |
| 282 | 4.65 | 379 | 2.58 | 476 | 0.03 |
| 283 | 4.50 | 380 | 2.68 | 477 | 0.03 |
| 284 | 4.32 | 381 | 2.79 | 478 | 0.02 |
| 285 | 4.14 | 382 | 2.92 | 479 | 0.02 |
| 286 | 3.94 | 383 | 3.07 | 480 | 0.02 |
| 287 | 3.77 | 384 | 3.22 | 481 | 0.02 |
| 288 | 3.62 | 385 | 3.39 | 482 | 0.02 |
| 289 | 3.50 | 386 | 3.53 | 483 | 0.02 |
| 290 | 3.38 | 387 | 3.67 | 484 | 0.02 |
| 291 | 3.28 | 388 | 3.82 | 485 | 0.02 |
| 292 | 3.20 | 389 | 4.00 | 486 | 0.01 |
| 293 | 3.11 | 390 | 4.17 | 487 | 0.01 |
| 294 | 2.96 | 391 | 4.34 | 488 | 0.02 |
| 295 | 2.73 | 392 | 4.47 | 489 | 0.02 |
| 296 | 2.50 | 393 | 4.56 | 490 | 0.02 |
| 297 | 2.29 | 394 | 4.62 | 491 | 0.02 |
| 298 | 2.10 | 395 | 4.67 | 492 | 0.02 |
| 299 | 1.93 | 396 | 4.73 | 493 | 0.02 |
| 300 | 1.77 | 397 | 4.82 |  |  |
| 301 | 1.64 | 398 | 4.92 |  |  |
| 302 | 1.54 | 399 | 5.02 |  |  |

## Quantum Yields

t 248 nm:	 1 + 2 = 0.76 for p < 80 mbar;

1 = 2; 2 = 0  for p = ∞;

290 – 380 nm:		   1 + 2+ 2 = 0.16 (average for atmospheric photolysis at surface).

Comments on Preferred Values

Biacetyl exhibits two distinct absorption regions relevant for atmospheric photolysis.  The first region consists of a broad band between 340 – 480 nm, superimposed by three distinct peaks at 417.2, 433.0 and 442.8. The second region shows a broad band with some structure with a maximum absorption near 272 nm.  The preferred values for the absorption cross-sections are based on those determined by Horowitz et al. (2001), which, are in satisfactory agreement with the earlier data of Plum et al. (1983) and McMillan et al, 1966 (e.g. smax = 4.65 x 10-20 cm2molecule-1 at 270 nm for the second band). The values given above are averaged over 1 nm and are taken from the compilation in http://www.atmosphere.mpg.de/enid/, which also contains data at other resolution.  The overall accuracy for both bands is estimated at ±5%.  The single wavelength determination of Rajakumar et al. (2008) at 184.9 nm is consistent with a third strong absorption band below 200 nm indicated by the data of Horowitz, (2001).

The recommended quantum yields for 1 + 2 are based on the data of Rajakumar et al. (2008), which are the only wavelength-resolved quantum yield data that have appeared. The observed pressure dependence of f(CH3CO) is due to dissociation of initially formed excited CH3CO* and is reproduced reasonably well, over the range of pressures covered in this study, by a Stern–Volmer relationship for the quenching of CH3CO*.  This analysis using an assumed high pressure limiting yield of f∞(CH3CO) = 2, gave a zero pressure quantum yield of fo(CH3CO) = 0.76±0.05.  The authors estimate the overall uncertainty in experimental values of CH3CO) from biacetyl photolysis at 248 nm to be 15% at the 2s (95% confidence) level.  For calculation of atmospheric photolysis rate of biacetyl in the lower troposphere, the average values reported by Plum et al (1983) can be used.

#### References

Horowitz, A., Meller, R. and Moortgat, G. K., J Photochem.Photobiol., A: Chem. 146, 19, 2001.

Klotz, B. , Graedler, F., Sorensen, S., Barnes, I, and Becker, K.H., Int. J. Chem. Kinet. 33

9–20, 2001.

McMillan, V. personal communication to J.G. Calvert, J.N.Pitts, Jr., Photochemistry, London, 1966, p. 422.

Plum, C. N., Sanhueza, E., Atkinson, R., Carter, W. P. L. and Pitts, Jr., J. N., Environ. Sci. Technol. 17, 479, 1983.

Rajakumar, B., Gierczak, T., Flad, J., Ravishankara, A.R., and Burkholder, J.B., J. Photochem Photobiol. A: Chem. 199, 336-344, 2008.