# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet P30

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: June 2012; last change in preferred values: June 2012.

C6H5C(O)H + h  products

## Primary photochemical transitions

| Reaction | H298/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| C6H5C(O)H  C6H5 + HC(O) (1) | 408.6 | 292 |
|  C6H5CO + H (2) | 363.9 | 328 |
|  C6H6 + CO (3) | 9.1 | 13.1 (mm) |

Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 220 - 300 | Nozière et al.,1994 | (a) |
| 245 - 300 | Caralp et al.,1999 | (b) |
| 255 - 296 | Etzkorn et al.,1999 | (c) |
| 280 - 308 | Zhu and Cronin, 2000 | (d) |
| 252 - 368 | Thiault et al.,2004 | (e) |
| 220 - 280 | El Dib et al.,2006 | (f) |
| 280 - 400 | Xiang et al., 2009 | (g) |
| 320 - 450 | Chen et al., 2011 | (h) |

Quantum yield data ( = 1 + 2 + 3)

| Measurement | Wavelength range/nm | Reference | Comments |
| --- | --- | --- | --- |
| f1(HCO) = 0.32±0.05 | 280 | Zhu and Cronin, 2000 | (d) |
| f1 (HCO) = 0.45±0.05 | 285 |  |  |
| f1 (HCO) = 0.29±0.05 | 308 |  |  |

## Comments

(a)	The absorption cross sections were determined by flowing nitrogen containing a calibrated concentration of benzaldehyde through a 70 cm reaction cell. UV light from a D2 lamp passed twice through the cell into a monochromator/photomultiplier unit for conventional absorption measurements. Resolution not given.

- Same set up as (a); no experimental details given.

- UV absorption cross sections were determined using a 1080 l quartz cell with a 0.5 m Czerny-Turner spectrometer coupled with a photodiode array detector (spectral resolution 0.15 nm). The maximum absolute absorption cross section for benzaldehyde at the 284.1 nm peak was s = (4.40 ± 1.82) × 10−18)cm2molecule-1.

- The UV photodissociation of benzaldehyde was investigated wavelengths of 280, 285 and 308 nm by employing excimer or dye laser photolysis in combination with CRDS. Absorption cross-sections of benzaldehyde were obtained from attenuation of the photolysis light. The HCO radical photofragmentation product was detected by CRDS at 614 nm and amounts formed after 10 ms were determined using the absorption cross-section of HCO at the probe laser wavelength, determined relative to the photolysis reaction: H2CO + hn  HCO + H, for which the HCO quantum yield is known. The uncertainty on the quantum yields reflects experimental scatter.

- Absorption cross-sections for benzaldehyde were measured in the wavelength region 252–368 nm using two different systems (D2 lamp-diode array and D2 lamp-monochromator). In addition, cross sections at 253.7 ((8.5 ± 1.3) × 10−19), 312.2 ((6.6 ± 0.1) × 10−20) and 365 nm ((2.2 ± 0.4)× 1020) were measured using a Hg pen ray lamp and were found in good agreement with those obtained using the D2 lamp-diode array system. The absorption spectra of aromatic aldehydes have been found to exhibit fine structures similarly to aromatic hydrocarbons.

- Photolysis of a slow flowing mixture of Cl2, N2, O2, and C6H5CH3. Absorption cross sections were determined by the "factor analysis method". Using factor analysis, the spectrum obtained is refined and the concentrations of the main absorbing species in a omplex mixture are extracted.

- Absorption measurements by CRDS. Cross sections and error limits (standard deviations in the precision of the measurements) given at 5 nm intervals in the range.

- Absorption cross sections of benzaldehyde were measured using incoherent broad-band cavity-enhanced absorption spectroscopy (IBBCEAS) with a Xe arc light source, giving a spectral range from 320 to 450 nm. The optical cavity was coupled into a 3.9 m3 FEP chamber which contained the benzaldehyde (>99% purity) diluted to < 100 ppbv in purified air. The optical system was calibrated using methyl vinyl ketone absorption at 360 nm. Cross sections given at 1 nm intervals; overall error limits were estimated from standard deviations in the precision of the measurements, and other sources, to be 14% (1s).

Preferred Values

## Absorption cross-sections at 298 K

| /nm | 1020/cm2 | /nm | 1020/cm2 |
| --- | --- | --- | --- |
| 220 | 21.000 | 310 | 0.0480 |
| 225 | 32.000 | 315 | 0.0658 |
| 230 | 39.000 | 320 | 0.0576 |
| 235 | 32.000 | 325 | 0.0649 |
| 240 | 24.000 | 330 | 0.0667 |
| 245 | 2.080 | 335 | 0.0677 |
| 250 | 1.300 | 340 | 0.0627 |
| 255 | 0.920 | 345 | 0.0471 |
| 260 | 1.300 | 350 | 0.0508 |
| 265 | 1.640 | 355 | 0.0385 |
| 270 | 1.990 | 360 | 0.0468 |
| 275 | 2.270 | 365 | 0.0418 |
| 280 | 1.720 | 370 | 0.0130 |
| 285 | 1.830 | 375 | 0.0043 |
| 290 | 0.120 | 380 | 0.0007 |
| 295 | 0.053 | 385 | 0.0002 |
| 300 | 0.043 | 390 | 0.0001 |
| 305 | 0.056 | 395 | 0.0002 |

## Quantum Yields

| Wavelength /nm | f1(HCO) |
| --- | --- |
| 308 | 0.29±0.05 |

Comments on Preferred Values

The absorption spectrum of benzaldehyde consists of three distinct regions; an intense band between 200 - 250 nm (smax = 3.9 x 10-17 cm2 at 230 nm); a second band between approx. 250 - 290 nm (smax = 3.9 x 10-17 cm2 at 230 nm); and a weaker absorbing plateau region with superimposed structure between 300 - 370 nm. The cross-section data of most of the studies are in reasonable agreement except for those of Noziere et al. (1999) which are systematically higher over the range studied by them, and those of Zhu and Cronin which were significantly lower, except ar 318 nm where they were slightly higher than other measurements. Part of the differences arise from different resolution of the measurements using narrow band (laser) and broad-band techniques, especially in  regions with discrete absorption features.  The most recent CEAS measurements of Chen at al.(2011) confirm the detailed structure in the near UV observed by Thiault et al.(2004), but the authors note a blue-shift in the wavelength calibration in the Thiault et al. results at l >335 nm, and an offset in their absorption at l>380 nm resulting from a baseline shift.

The preferred absorption cross-sections at l > 295 nm are averaged values from the measurements of Thiault et al.(2004) (blue shifted by 4nm between 335 – 375 nm), Xiang et al (2009) and Chen at al.(2011) in the regions of data overlap.  Between 255 nm < l < 295 nm the preferred values are average values of the data from Etzkorn et al (1999), Thiault et al (2004) , and El Dib et al. (2006).  The data of El Dib et al. (2006) are recommended for l < 255 nm.

The recommended quantum yield f(HCO) at 308 nm is the wavelength resolved value reported by Zhu and Cronin (2000). This gives a lower limit to the overall f.  The values at at shorter wavelength may be in unrepresentative due to fine structure effects in this structured part of the spectrum. Nevertheless these results indicate that photolysis is a potentially important removal process for aromatic aldehydes in the troposphere.

#### References

Chen, J., Wenger, J.C., and Venables, D.S., J. Phys. Chem. A, 2011, 115 12235-12242.

Caralp, F., Focher, V., Lesclaux, R., Wallington, T.J., and Hurley, M.D., Phys. Chem. Chem. Phys. 1, 3509-3517 (1999).

El Dib, G., Chakir, A., Roth, E., Brion, J. and Daumont, D.:  J. Phys. Chem. A: 110, 7848-7857 (2006).

Etzkorn, T., Klotz, B., Sørensen S., Patroescu, I.V., Barnes, I., Becker, K.H., and Platt, U. Atmos. Environ.: 33, 525-540 (1999).

B. Nozière, R. Lesclaux, M.D. Hurley, M.A. Dearth, and T.J. Wallington, J. Phys. Chem.: 98, 2864-2873, 1994.

Thiault, G., Mellouki, A., Le Bras, G., Chakir, A., Sokolowski-Gomez, N. and Daumont, D., J. Photochem. Photobiol. A: Chem.: 162, 273-281 (2004).

Xiang, B., Zhu, C. and Zhu, L., Chem. Phys. Lett.: 474, 74-78 (2009)

Zhu, L. and Cronin, T.J., Chem. Phys. Lett.: 317, 227-231, 2000

Figure 1:  Absorption Spectrum of Benzaldehyde