### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, Data Sheet P35

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr)

This datasheet last evaluated: May 2020; last change in preferred values: June 2017.

(CH3)2COO + h( ( products

Primary photochemical transitions

Reaction

(CH3)2COO + h  (CH3)2CO + O(3P) (1)

 (CH3)2CO + O(1D) (2)

Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 280 – 410 | Liu et al., 2014 | (a) |
| 280 – 420 | Huang et al., 2015 | (b) |
| 308 – 352 | Chang et al., 2016 | (c) |
| 355 | Chhantyal-Pun et al., 2017 | (d) |

Comments

- (CH3)2COO was prepared by PLP (248 nm) of 2,2-diiodopropane, (CH3)2CI2 in O2/Ar mixtures in a capillary tube.  The photoproducts were cooled in a supersonic expansion and passed to a TOF mass spectrometer where they were ionised with VUV radiation at 118 nm. The UV absorption spectrum was determined from depletion of the m/z =74 photo-ionisation signal resulting from excitation of the B ( X transition in ground state (CH3)2COO molecules by tunable UV radiation (280 – 420 nm) from a Nd-YAG laser. The UV-induced depletion approaches 100% near the peak of the simple Gaussian profile at 320 nm, indicating rapid dynamics in the B state, and corresponds to a peak absorption cross section of ~4 × 10−17 cm2 molecule−1; the absolute cross section measurements have an uncertainty on the order of a factor of 2.

- (CH3)2COO was generated from pulsed photolysis of a flowing gaseous mixture consisting of (CH3)2CI2, O2, and buffer gas (N2) at 248 nm via the reactions: (CH3)2CI2 + hν → (CH3)2CI + I; (CH3)2CI +O2 → (CH3)2COO + IO. Time-resolved difference absorption spectra were recorded and corrected for absorption changes due to precursor and other products (e.g. IO) molecules, leaving a residual absorption attributable to (CH3)2COO.

- The absolute absorption cross sections of (CH3)2COO under a jet-cooled condition were measured via laser depletion to be (1.32 ± 0.10) × 10-17 cm2 molecule-1 at 308 nm and (9.6 ± 0.8) × 10-18 cm2 molecule-1 at 352 nm. Absolute calibration was achieved using laser beam profiling measurements.  Control experiments using CH2I2 gave an absorption cross section at 308 nm in good agreement with the well-established literature value. The peak UV cross section of (CH3)2COO is estimated to be (1.75 ± 0.14) × 10-17 cm2 molecule-1 at 330 nm by scaling the UV spectrum of (CH3)2COO (Huang et al., 2015; note b) to the absolute cross section at 308 nm.

- (CH3)2COO was formed by laser photolysis of 2,2-diiodopropane in the presence of O2 and characterized by synchrotron photoionization mass spectrometry and also by cavity ringdown ultraviolet absorption spectroscopy. Cavity ringdown measurements of the acetone oxide removal without added reagents display a combination of first- and second-order decay kinetics, which were deconvolved to derive rate coefficients for both unimolecular thermal decay, kdec.(see CGI_14), and  the self-reaction of (CH3)2COO.  The loss of (CH3)2CI2 following photodissociation was used to calibrate the initial (CH3)2COO concentration and determine σ (355nm) = (1.45 ± 0.24) × 10−17 cm2 molecule−1 and the (CH3)2COO self-reaction rate coefficient, k = (6.0 ± 1.1) × 10−10 cm3 molecule−1 s−1.

Preferred Values

Absorption cross-sections at 298 K

| (/nm | 1020 /(cm2 molecule-1) | (/nm | 1020 /(cm2 molecule-1) |
| --- | --- | --- | --- |
| 280 | 279 | 345 | 1355 |
| 285 | 403 | 350 | 1146 |
| 290 | 560 | 355 | 929 |
| 295 | 747 | 360 | 723 |
| 300 | 955 | 365 | 540 |
| 305 | 1171 | 370 | 387 |
| 310 | 1379 | 375 | 266 |
| 315 | 1557 | 380 | 175 |
| 320 | 1687 | 385 | 111 |
| 325 | 1754 | 390 | 67 |
| 330 | 1750 | 395 | 39 |
| 335 | 1675 | 400 | 22 |
| 340 | 1538 | 405 | 12 |

 = (1.75 ± 0.53) × 10-17 cm2 molecule-1 at max (330 nm);

Gaussian fit parameters to extracted data from the absorption spectrum for the range 280 - 390 nm reported by Chang et al. (2016):  = 1747 × 10-20 exp(-0.5 × ((-327.2)/24.58)2)

Quantum Yields

1 = 1.0 for 280 <  < 380 nm.

Comments on Preferred Values

The first UV absorption spectrum of (CH3)2COO was reported by Liu et al. (2014), using UV photo-dissociation action technique. The results show a Gaussian band peaking at 330 nm with no resolved structure, which is attributed to the B̃ (1A′) ← X̃(1A′) electronic transition. Huang et al. (2015) used conventional absorption spectroscopy and reported a spectrum for (CH3)2COO slightly broader than the jet-cooled spectrum reported by Liu et al. (2014). The contribution of hot bands in the room-temperature spectrum would cause broadening in comparison with the low-temperature spectrum of Liu et al. (2014).   The results from the UV action spectra of several Criegee intermediates reported by the University of Pennsylvania group (e.g. CH2OO and CH3CHOO, Beames et al., 2012; 2013) differ substantially from spectra recorded subsequently using conventional absorption spectroscopy (e.g. Sheps, 2013; Ting et al, 2014; Smith et al., 2014).  The absorption bands determined using photo-dissociation action spectroscopy by the University of Pennsylvania group are narrower, peak at a shorter wavelength, and the cross sections are up to a factor of 4 higher than those measured using absorption spectroscopy (Sheps et al., 2013; Smith et al., 2014).

Causes for this discrepancy remain unclear, as discussed in Ting et al. (2014) and Chang et al. (2016). The latter study included control experiments which reproduced the well-established absorption cross section for CH2I2 at 308 nm. The weight of evidence favours the spectral shape and cross-sections determined by UV absorption and the recommended (CH3)2COO spectrum is based upon the work of Huang et al. (2015) and Chang et al. (2016). The figure below shows the experimental values reported by Chang et al. (2014) and a Gaussian fit to those data. The cross-sections listed in the table of preferred values are obtained from the Gaussian fit to the experimental data and are estimated to have an uncertainty of ± 30 %. The photodissociation quantum yields are likely to be close to unity.  Hydroxyl radicals produced concurrently with the generation of the Criegee intermediates were measured in the experiments of Liu et al. (2013), where they were detected by 1+1′ resonance enhanced multiphoton ionization. The HO yield observed with CH3CHOO is 6-fold larger than that from CH2OO, consistent with prior studies of HO generation from alkene ozonolysis (Kroll et al., 2002).

References

Beames, J. M., Liu, Fang Lu, Lu Lu, and Lester, M. I.: J. Amer. Chem. Soc., 134, 20045, 2012.

Beames, J. M., Liu, Fang Lu, Lu Lu, and Lester, M. I.: J. Chem. Phys. 138, 244307, 2013.

Chang, Y; Chang, C-H., Takahashi, K, Lin, J. J-M.: Chem. Phys. Lett., 653, 155, 2016.

Chhantyal-Pun, R., Welz, O., Savee J. D., Eskola, A. J., Lee, E. P. F., Blacker, L., Hill, H. R., Ashcroft, M., Khan, M. A. H., Lloyd-Jones, G. C., Evans, L., Rotavera, B., Rotavera H., Osborn, D. L., Mok, D. K. W., Dyke, J. M., Shallcross, D. E., Percival, C. J., Orr-Ewing, A. J., and Taatjes, C. A.: J. Phys. Chem. A, 121, 4, 2017.

Huang, H.-L., Chao, W., and Lin, J. J.-M.: Proc. Nat. Acad. Sci., 112, 10857, 2015.

Kroll, J. H., Donahue, N.M., Cee, V.J., Demerjian, K.L., and Anderson, J.G.: J. Am. Chem. Soc., 124, 8518, 2002.

Lehman, J. H., Li, H., Beames, J. M., and Lester, M. I.: J. Chem. Phys., 139, 141103, 2013

Liu, F., Beames, J. M., Green, A. M. and Lester, M. I.: J. Phys. Chem. A, 118, 2298, 2014.

Sheps, L.: J. Phys. Chem. Lett., 4, 4201, 2013.

Sheps, L., Scully, A.M. and Au, K.: Phys. Chem. Chem. Phys., 16, 26701, 2014.

Smith, M.C., Ting, W-L, Chang, C-H., Takahashi, K., Boering, K.A., and Lin, J. Jr -M.: J. Chem. Phys., 141, 074302, 2014.

Absorption spectrum of (CH3)2COO; full line is Gaussian fit to experimental data (filled circles) from Chang et al. (2016). Gaussian fit parameters to data for (CH3)2COO:  = 1747 × 10-20 exp(-0.5 × ((-327.2)/24.58)2)