### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet P36

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for the preferred values in this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This datasheet last evaluated: June 2015; last change in preferred values: June 2015.

CH3CH2CHOO + h  products

Primary photochemical transitions

| Reaction | H298/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| CH3CH2COO + h  CH3CH2CO + O(3P) (1) | 185 | 645 |
|  CH3CH2CO + O(1D) (2) | 292 | 410 |

Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 280-410 | Liu et al., 2014 | (a) |

Comments

(a)	Propionaldehyde oxide CH3CH2COO, was prepared by PLP (248 nm) of (CH3)2CI2 in O2/Ar mixtures in a capillary tube.  The photoproducts were cooled in a supersonic expansion and passed to a TOF mass spectrometer where they were ionised with VUV radiation at 118nm. The UV absorption spectrum was determined from depletion of the m/z =74 photo-ionisation signal resulting from excitation of the B ( X transition in ground state CH3CH2COO molecules by tunable UV radiation (280 – 420 nm) from a Nd-YAG laser. The UV-induced depletion approaches 100% near the peak of the simple Gaussian profile at 325 nm, indicating rapid dynamics in the B state, and corresponds to a peak absorption cross section of ~3.5 × 10−17 cm2 molecule−1; the absolute cross section measurements have an uncertainty on the order of a factor of 2. The electronic spectrum for CH3CH2COO is similar to that reported recently for CH3CHOO.

Preferred Values

Absorption cross-sections at 298 K

| (/nm | /cm-2 x 10-20 | (/nm | /cm-2 x 10-20 |
| --- | --- | --- | --- |
| 280 | 341.7 | 350 | 1549 |
| 285 | 562.8 | 355 | 1099 |
| 290 | 872.9 | 360 | 734.1 |
| 295 | 1275 | 365 | 461.8 |
| 300 | 1753 | 370 | 273.5 |
| 305 | 2270 | 375 | 152.5 |
| 310 | 2767 | 380 | 80.11 |
| 315 | 3177 | 385 | 39.61 |
| 320 | 3434 | 390 | 18.44 |
| 325 | 3496 | 395 | 8.086 |
| 330 | 3350 | 400 | 3.338 |
| 335 | 3024 | 405 | 1.298 |
| 340 | 2569 | 410 | 0.4750 |
| 345 | 2094 | 415 | 0.1637 |

 = (3.5 ± 2) x 10-17 cm2  at max (324 nm) ;

Gaussian fit parameters to data of Liu et al. (2014):  = 3.5 x 10-17 exp(-0.00120325 x (324.0 - )2)

Quantum Yields

1 = 1.0 for 280 <  <420 nm.

Comments on Preferred Values

The only reported study of UV absorption spectrum of the propionaldehyde oxide Creigee diradical was obtained by Liu et al (2014), using the UV photo-dissociation action spectrum technique. CH3CH2CHOO can exist in two (stable) conformers: syn- and anti- , but the syn- form is lower in energy and is expected to be prevalent from the source chemistry employed.

The results show a Gaussian band peaking at 324 nm with no resolved structure, which is attributed to the in the B̃ (1A′) ← X̃(1A′) electronic transition in CH3CH2CHOO.  No results have been reported to date for the CH3CH2CHOO molecule using conventional absorption spectroscopy. However the results from the UV action spectra of several Criegee intermediates reported by the University of Pennsylvania group (e.g. CH2OO and CH3CHOO, Beames et al, (2012) and 2013), differs substantially from spectra recorded subsequently using conventional absorption spectroscopy (e.g. Sheps ,2013; Sheps et al.,2013; Ting et al, 2014; Smith et al., 2014).  Causes for this discrepancy remain unclear, as discussed in Ting et al., 2014 and Smith et al, 2014.  The weight of evidence favours the spectral shape and cross-sections determined by UV absorption, and in view of the implied uncertainty in the spectral parameters obtained by the UV photo-dissociation action technique we make no recommendation for the absorption cross sections for CH3CH2CHOO at this time.  Fig.1 shows the experimental values extracted from Fig.3 of the paper by Liu et al., (2014) and a Gaussian fit to these data. The listed cross-sections in the above table are obtained from the Gaussian fit to the experimental data.  The best estimate for absolute values of cross-sections near the peak are about a factor 3 lower than these listed values , but the uncertainty is large over the whole range.

The photodissociation quantum yields are likely to be close to unity.  Hydroxyl radicals, produced concurrently with the generation of the Criegee intermediates, were measured in the experiments of Liu et al, (2014), where they were detected by 1+1′ resonance enhanced multiphoton ionization. The OH yield observed with CH3CH2CHOO is 10-fold larger than that from CH2OO, and is greater than from prior studies of OH generation from ozonolysis. of E-3-hexene(Kroll et al, 2002).

References

Beames, J. M., Liu, Fang Lu, Lu Lu, and Lester, M. I.: J. Chem. Phys. 138, 244307, 2013.

Sheps, L., J. Phys.Chem.Lett., 4, 4201, 2013.

Sheps, L., Scully, A.M. and Au, K., Phys.Chem.Chem.Phys.: 16, 26701, 2014.

Smith, M.C., Ting,W-L, Chang, C-H., Takahashi, K., Boering, K.A., and Lin, J. Jr -M.: J. Chem. Phys., 141, 074302, 2014.

Lehman, J.H., Li, H., Beames, J. M., and Lester, M. I.: J. Chem. Phys., 139, 141103, 2013.

Liu, F., Beames, J. M., Green, A. M. and Lester, M.I., J. Phys. Chem. A  118, 2298, 2014.

Figure 1:     Absorption spectrum of CH3CH2CHOO, syn- and anti- conformers not resolved; Gaussian fit to experimental data from Liu et al., 2014 shown as full line.

lines.