# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet P8

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet updated: 5th December 2005.

CH3C(O)C2H5 + h  products

## Primary photochemical transitions

| Reaction | H298/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| CH3C(O)C2H5 + h  CH3 + C2H5CO (1) | 352.6 | 339 |
|  C2H5 + CH3CO (2) | 349.4 | 342 |
|  CH3 + C2H5 + CO (3) | 395.3 |  |

## Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 202-355 | Martinez et al., 1992 | (a) |
| 240-350 | Yujing and Mellouki, 2000 | (b) |

Quantum yield data ( = 1 + 2 + 3)

| Measurement | Wavelength range/nm | Reference | Comments |
| --- | --- | --- | --- |
|  |  |  |  |
| 0.34 (1000 mbar) | 275 - 380 | Raber and Moortgat., 1987 | (c) |
| 0.89 (68 mbar) |  |  |  |

## Comments

- Conventional double-beam spectrophotometric measurements on mixtures of the 2-butanone and argon at a resolution of 0.5 nm.  The cross-sections are given as averages over a 1 nm ( > 280 nm) or 4 nm ( < 280 nm) region centered on the corresponding wavelength. max = 5.77 x 10-20 cm2molecule-1 at 278 nm.

(b) Diode array spectrometer measurements on pure 2-butanone at a resolution of 0.04 nm. The cross-sections are given over 1 nm intervals.  Precision based on observed standard deviation was within 5%.  max = 5.65 x 10-20 cm2molecule-1 at 278 nm.

(c) 2-butanone was photolyzed in synthetic air at several pressures in the range 68 mbar to 1 bar using a broad-band radiation source (275 nm to 380 nm) and the product yields were monitored by FTIR.  The quantum yield for photolysis of 2-butanone was found to be pressure dependent decreasing from 0.89 at 68 mbar to 0.34 at 1 bar.  They also conclude that photolysis over the wavelength region used occurs to the extent of 80 - 90% by channel 2.  These results were derived by modelling the secondary chemistry in the system.

Preferred Values

## Absorption cross-sections at 298 K

| /nm | 1020 /cm2 | /nm | 1020 /cm2 | /nm | 1020 /cm2 |
| --- | --- | --- | --- | --- | --- |
| 202 | 1.412 | 292 | 4.60 | 324 | 0.229 |
| 206 | 0.192 | 293 | 4.42 | 325 | 0.189 |
| 210 | 0.160 | 294 | 4.24 | 326 | 0.156 |
| 214 | 0.183 | 295 | 4.08 | 327 | 0.129 |
| 218 | 0.225 | 296 | 3.93 | 328 | 0.105 |
| 222 | 0.290 | 297 | 3.79 | 329 | 0.085 |
| 226 | 0.391 | 298 | 3.65 | 330 | 0.067 |
| 230 | 0.534 | 299 | 3.48 | 331 | 0.054 |
| 234 | 0.742 | 300 | 3.30 | 332 | 0.042 |
| 238 | 1.029 | 301 | 3.10 | 333 | 0.033 |
| 242 | 1.410 | 302 | 2.89 | 334 | 0.025 |
| 246 | 1.886 | 303 | 2.69 | 335 | 0.020 |
| 250 | 2.45 | 304 | 2.50 | 336 | 0.014 |
| 254 | 3.09 | 305 | 2.33 | 337 | 0.011 |
| 258 | 3.74 | 306 | 2.17 | 338 | 0.008 |
| 262 | 4.39 | 307 | 2.02 | 339 | 0.007 |
| 266 | 4.96 | 308 | 1.876 | 340 | 0.005 |
| 270 | 5.40 | 309 | 1.727 | 341 | 0.005 |
| 274 | 5.68 | 310 | 1.575 | 342 | 0.003 |
| 278 | 5.77 | 311 | 1.423 | 343 | 0.003 |
| 280 | 5.74 | 312 | 1.276 | 344 | 0.002 |
| 281 | 5.72 | 313 | 1.136 | 345 | 0.001 |
| 282 | 5.68 | 314 | 1.009 | 346 | 0.001 |
| 283 | 5.62 | 315 | 0.896 | 347 | 0.000 |
| 284 | 5.54 | 316 | 0.794 | 348 | 0.001 |
| 285 | 5.44 | 317 | 0.697 | 349 | 0.000 |
| 286 | 5.35 | 318 | 0.611 | 350 | 0.000 |
| 287 | 5.26 | 319 | 0.531 | 351 | 0.000 |
| 288 | 5.17 | 320 | 0.457 | 352 | 0.001 |
| 289 | 5.06 | 321 | 0.389 | 353 | 0.000 |
| 290 | 4.94 | 322 | 0.328 | 354 | 0.000 |
| 291 | 4.78 | 323 | 0.276 | 355 | 0.000 |

Quantum Yields

 = 0.34 for  = 275 - 380 nm at 1000 mbar.

Comments on Preferred Values

The preferred absorption cross-sections are taken from the measurements of Martinez et al. (1992) over the wavelength region 220 nm to 350 nm.  The values at the band maximim are 5% higher than the recent data of Yujing and Mellouki (2000), but 5% lower than those of McMillan, reported by Calvert and Pitts (1966).  Raber and Moortgat (1987) have also given a spectrum which is in good agreement with these cross-sections.

The only quantum yield measurements are those of Raber and Moortgat (1987), which forms the basis for the preferred quantum yield at 1000 mbar. This data needs further experimental support.

References

Calvert, J. G. and Pitts, Jr., J. N.: Photochemistry, Wiley, New York, 1966.

Martinez, R. D., Buitrago, A.A., Howell, N. W., Hearn, C. H. and Joens, J. A.: Atmos. Environ. 26A, 785, 1992.

Raber, W. H. and Moortgat, G. K.: "Photooxidation of Selected Carbonyl Compounds in Air:  Methyl Ethyl Ketone, Methyl Vinyl Ketone, Methacrolein and Methylglyoxal," Chap. 9, In: Progress and Problems in Atmospheric Chemistry," ed. J. Barker, World Scientific Publishing Singapore, 1987.

Yujing, M. and Mellouki, A.: J.Photochem and Photobiol.A: Chemistry, 134, 31, 2000.