# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet PBr10

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

This data sheet updated: 15th December 2000.

CH3Br + h  products

# Primary photochemical processes

| Reaction | H/kJ mol-1 | threshold/nm |
| --- | --- | --- |
| CH3Br + h  CH3 + Br | 296 | 404 |

# Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 180-260 | Gillotay and Simon, 1988 1 | (a) |

Quantum yield data

| Measurement | Wavelength/nm | Reference | Comments |
| --- | --- | --- | --- |
| (Br) = 1.01  0.16 | 248 | Talukdar, Vaghjiani, and Ravishankara, 19922 | (b) |
| (Br) = 1.10  0.20 | 222 |  |  |
| (Br) = 1.05  0.11 | 193 |  |  |
| (H) = 0.002  0.001 | 193 |  |  |

# Comments

(a)	Spectra were obtained using a thermostatted absorption cell with a single pass optical path of 2 m coupled to a monochromator capable of a maximum resolution of 0.015 nm.  Pressures of CH3Br used covered the range 5.3 x 10-2 – 29 mbar.  Spectra were recorded at 295 K, 270 K, 250 K, 230 K, and 210 K.  The data were fitted to a polynomial expression giving the cross sections as a function of temperature and pressure.

(b)	Pulsed laser photolysis of CH3Br-N2 or He mixtures and detection of Br(2P3/2) by resonance fluorescence.  A small amount of H2 was added to ensure rapid quenching of the Br(2P1/2) also produced.  The Br(2P3/2) measurements were calibrated by HBr photolysis at 193 nm for which a quantum yield of unity was assumed.  No H atom production could be detected in the 248 nm and 222 nm photolyses.

# Preferred Values

Absorption cross-sections of CH3Br at 295 K and 209 K.

| /nm | 1020 /cm2 | /nm | 1020 /cm2 |
| --- | --- | --- | --- |
|  | 295 K | 210 K |  | 295 K | 210 K |
| 190 | 43.9 | (a) | 226 | 23.0 | 21.6 |
| 192 | 52.9 | (a) | 228 | 18.8 | 17.7 |
| 194 | 62.0 | (a) | 230 | 15.4 | 14.4 |
| 196 | 69.1 | (a) | 232 | 12.4 | 11.4 |
| 198 | 76.0 | (a) | 234 | 9.87 | 8.86 |
| 200 | 79.1 | (a) | 236 | 7.65 | 6.58 |
| 202 | 79.7 | (a) | 238 | 5.95 | 4.97 |
| 204 | 79.3 | (a) | 240 | 4.47 | 3.79 |
| 206 | 76.7 | (a) | 242 | 3.35 | 2.76 |
| 208 | 72.7 | (a) | 244 | 2.50 | 1.94 |
| 210 | 66.6 | (a) | 246 | 1.82 | 1.42 |
| 212 | 61.4 | 61.3 | 248 | 1.31 | 0.980 |
| 214 | 55.9 | 55.6 | 250 | 0.957 | 0.675 |
| 216 | 49.3 | 49.0 | 252 | 0.686 | 0.447 |
| 218 | 44.2 | 43.3 | 254 | 0.487 | 0.315 |
| 220 | 37.7 | 36.6 | 256 | 0.336 | 0.202 |
| 222 | 32.4 | 31.2 | 258 | 0.235 | 0.129 |
| 224 | 27.6 | 25.9 | 260 | 0.164 | 0.088 |

(a) No detectable change in  over the range 209-295 K

# Quantum yields

 = 1.0 over the wavelength range 200 – 260 nm.

## Comments on Preferred Values

The preferred values of the absorption cross-section at 295 K and 210 K are those reported by Gillotay and Simon.1  Values have also been reported at 298 K by Molina et al.,3 at 5 nm intervals , and by Robbins,4 at 2 nm intervals.  The agreement among these three studies is very good.  Gillotay and Simon1 have fitted their data to a polynomial to give an expression for the cross sections as a function of temperature and pressure.

The preferred values for the quantum yield are based on the study of Talukdar et al.2 who showed that photolysis occurs with unit quantum efficiency by rupture of the C–Br bond.

# References

1	D. Gillotay and P. C. Simon, Annal. Geophys. 6, 211 (1988).

2	R. K. Talukdar, G. L. Vaghjiani, and A. R. Ravishankara, J. Chem. Phys. 96, 8194 (1992).

3	L. T. Molina, M. J. Molina, and F. S. Rowland, J. Phys. Chem. 86, 2672 (1982).

4	D. E. Robbins, Geophys. Res. Lett. 3, 213 (1976).