# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet PBr11

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

This data sheet updated: 15th December 2000.

CF3Br (Halon-1301) + h  products

# Primary photochemical processes

| Reaction | H/kJ mol-1 | threshold/nm |
| --- | --- | --- |
| CF3Br + h  CF3 + Br | 296 | 404 |

# Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 168-280 | Gillotay and Simon, 19891 | (a) |
| 190-285 | Burkholder et al., 19912 | (b) |
| 190-320 | Orkin and Kasimovskaya, 19953 | (c) |

#### Quantum yield data

| Measurement | Wavelength/nm | Reference | Comments |
| --- | --- | --- | --- |
| 1.12  0.16 | 193 | Talukdar, Vaghjiani, and Ravishankara, 19924 | (d) |
| 0.92  0.15 | 222 |  |  |

# Comments

(a) 	Spectra were obtained using a thermostatted absorption cell with a single pass optical path of 2 m coupled to a monochromator capable of a maximum resolution of 0.015 nm.  Pressures of CF3Br used covered the range 0.8 – 950 mbar.  Spectra were recorded at 295 K, 270 K, 250 K, 230 K, and 210 K.  The data were fitted to a polynomial expression giving the cross sections as a function of temperature and pressure.

(b) 	Spectra were obtained using thermostatted absorption cells with single pass optical paths of 98.1 cm and 150 cm, coupled to spectrographs having resolutions in the range 0.4-0.5 nm.  Spectra were recorded at 296 K, 270 K, 250 K, 230 K, and 210 K.  The data were fitted to a polynomial expression giving the cross sections as a function of temperature and pressure.

(c)	Spectra were obtained using a cell thermostatted at 295 K with a single path optical length of 14.0 cm and coupled to a double beam spectrophotometric system. Sample pressures in the range 0.013–1 bar were used.

(d) Pulsed laser photolysis of CF3Br-N2 mixtures and detection of Br(2P3/2) by resonance fluorescence. A small amount of H2 was added to ensure rapid quenching of the Br(2P1/2) also produced. The Br(2P3/2) measurements were calibrated by CH3Br photolysis at the same wavelength for which a quantum yield of unity was assumed.

### Preferred Values

Absorption cross-sections of CF3Br at 295 K and 210 K.

| /nm | 1020 /cm2 | /nm | 1020 /cm2 |
| --- | --- | --- | --- |
|  | 295 K | 210 K |  | 295 K | 210 K |
| 190 | 6.50 | 7.11 | 230 | 2.98 | 2.24 |
| 192 | 7.49 | 8.27 | 232 | 2.35 | 1.67 |
| 194 | 8.49 | 9.43 | 234 | 1.83 | 1.21 |
| 196 | 9.48 | 10.6 | 236 | 1.40 | 0.863 |
| 198 | 10.4 | 11.7 | 238 | 1.06 | 0.607 |
| 200 | 11.2 | 12.6 | 240 | 0.789 | 0.420 |
| 202 | 11.8 | 13.2 | 242 | 0.574 | 0.287 |
| 204 | 12.2 | 13.6 | 244 | 0.418 | 0.193 |
| 206 | 12.4 | 13.8 | 246 | 0.301 | 0.129 |
| 208 | 12.3 | 13.6 | 248 | 0.216 | 0.0848 |
| 210 | 12.0 | 12.9 | 250 | 0.153 | 0.0562 |
| 212 | 11.3 | 12.1 | 252 | 0.107 | 0.0371 |
| 214 | 10.6 | 11.1 | 254 | 0.0751 | 0.0241 |
| 216 | 9.69 | 9.86 | 256 | 0.0524 | 0.0163 |
| 218 | 8.65 | 8.54 | 258 | 0.0364 | 0.0110 |
| 220 | 7.58 | 7.25 | 260 | 0.0252 | 0.0074 |
| 222 | 6.52 | 5.97 | 262 | 0.0176 |  |
| 224 | 5.50 | 4.84 | 264 | 0.0121 |  |
| 226 | 4.56 | 3.86 | 266 | 0.0086 |  |
| 228 | 3.73 | 2.96 | 268 | 0.0061 |  |

# Quantum Yields

 = 1.0 over the range 200-270 nm.

## Comments on Preferred Values

The preferred values of the absorption cross-sections at 295 K are the mean of the values obtained in the studies of Gillotay and Simon,1 Burkholder et al.,2 and Orkin and Kasimovskaya.3  Molina et al.5 have also reported  values at 5 nm intervals.  The agreement among these four studies,1-3,5 over the wavelength range of the preferred values, is excellent.  The temperature dependence of the of the cross sections down to 210 K has been studied by Gillotay and Simon1 and by Burkholder et al.2 and in both cases polynomial expressions were derived giving the cross sections as a function of temperature and wavelength.  There are significant differences between the two studies.1,2  Thus at  > 220 nm both studies reported a decrease in absorption as the temperature was lowered, but near the absorption peak ( ~ 205 nm) Burkholder et al.2 found the cross-sections to be independent of temperature, while Gillotay and Simon1 found the absorption to increase with decreasing temperature, with a 20% increase at the lowest temperature studied.  Furthermore, at 210 K there is good agreement on the values of  at longer wavelengths (~280 nm), but the discrepancy between the two studies1,2 increases steadily in going to shorter wavelengths with the values of Gillotay and Simon1 being ~30% larger than those of Burkholder et al.2 at 190 nm.  Provisionally, the preferred values at 210 K are taken as the mean of the values of Gillotay and Simon1 and of Burkholder et al.2

The preferred quantum yields are based on the study of Talukdar et al.4 in which it was shown that photolysis occurs with unit quantum efficiency by rupture of the C-Br bond to give CF3 + Br.  CF3Br has no apparent tropospheric chemistry loss mechanism2 and is estimated to have a tropospheric lifetime against direct solar photoexcitation of greater than 1000 years.5

# References

1	D. Gillotay and P. C. Simon, J. Atmos. Chem. 8, 41 (1989).

2	J. B. Burkholder, R. R. Wilson, T. Gierczak, R. Talukdar, S. A. McKeen, J. J. Orlando, G. L. Vaghjiani, and A. R. Ravishankara, J. Geophys. Res. 96, 5025 (1991).

3	V. L. Orkin and E. E. Kasimovskaya, J. Atmos. Chem. 21, 1 (1995).

4 	R. K. Talukdar, G. L. Vaghjiani, and A. R. Ravishankara, J. Chem. Phys. 96, 8194 (1992).

5	L. T. Molina, M. J. Molina, and F. S. Rowland, J. Phys. Chem. 86¸ 2672 (1982).