# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet PNOx1

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet updated: 16th July 2001.

# HONO + h  products

# Primary photochemical transitions

| Reaction |  | H/kJ mol-1 | threshold/nm |
| --- | --- | --- | --- |
| HONO + h  HO + NO | (1) | 207 | 578 |
|  H + NO2 | (2) | 331 | 361 |
|  HNO + O(3P) | (3) | 442 | 271 |

# Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 185-270 | Kenner, Rohrer, and Stuhl, 19861 | (a) |
| 300-400 | Bongartz et al., 1991;2 19943 | (b) |

#### Quantum yield data

| Measurement | Wavelength/nm | Reference | Comments |
| --- | --- | --- | --- |
| 1 = 0.92  0.16 | 3655 | Cox and Derwent, 19764 | (c) |
| (HO*) | 193 | Kenner, Rohrer, and Stuhl, 19861 | (d) |
| (H) | 351 | Wollenhaupt et al., 20005 | (e) |

# Comments

(a)	A relative absorption spectrum was measured in the range 185-270 nm with absolute determinations at 193 nm and 215 nm. A value of  =1.6 x 10-18 cm2 molecule-1 was obtained at 193 nm. Two different methods used to prepare HONO gave similar results.  The  values agree with those of Cox and Derwent4 in the wavelength region 220-270 nm, but the peak at 215 nm, seen in the Cox and Derwent4 study, which could have been due to NO absorption, was not observed.

(b)	Absolute absorption cross-sections were determined using conventional absorption spectroscopy, and with low, non-equilibrium concentrations of HONO determined by a combination of gas-phase and wet chemical analysis. Spectral resolution was 0.1 nm; cross sections averaged over 0.5 nm are given in a table. In their later work, improved conditions were used, specifically, higher HONO mole fractions, greater stability of HONO in the absorption chamber, and determination of the NO2 present by interference free optical absorption at 440 nm.

(c)	Rates of photon absorption and decomposition of NO2 and HONO were measured in the same photolysis cell. The value of  obtained supersedes an earlier estimate6 using the same technique but based on less reliable absorption cross-section data.

(d)	Laser photolysis of HONO at 193 nm. HO* was measured by emission spectroscopy. A small quantum yield of ~ 10-5 was determined.

(e)	Pulsed laser photolysis at 351 nm of flowing HONO - N2 (or Ar) mixtures was used to generate HO and the system was investigated using resonance absorption at 121.6 nm to discover the extent of any concommittent production of H. The system was calibrated for [H] by 248 nm photolysis of CH3SH. An upper limit of 1% was obtained for (H).

#### Preferred Values

Absorption cross-sections of HONO at 298 K

| /nm | 1020/cm2 | /nm | 1020/cm2 | /nm | 10-20/cm2 |
| --- | --- | --- | --- | --- | --- |
| 190 | 127 | 260 | 8.0 | 330 | 9.3 |
| 195 | 172 | 265 | 5.2 | 335 | 6.5 |
| 200 | 197 | 270 | 3.4 | 340 | 16.8 |
| 205 | 220 | 275 | 2.5 | 345 | 9.6 |
| 210 | 214 | 280 | - | 350 | 11.5 |
| 215 | 179 | 285 | - | 355 | 23.6 |
| 220 | 146 | 290 | - | 360 | 8.0 |
| 225 | 120 | 295 | - | 365 | 16.1 |
| 230 | 86 | 300 | 0.0 | 370 | 20.5 |
| 235 | 60 | 305 | 0.7 | 375 | 4.9 |
| 240 | 42 | 310 | 1.6 | 380 | 9.2 |
| 245 | 30 | 315 | 2.5 | 385 | 14.5 |
| 250 | 18.5 | 320 | 4.4 | 390 | 2.4 |
| 255 | 12.4 | 325 | 5.0 | 395 | 0.6 |

# Quantum Yields at 298 K

1 = 1.0 throughout the wavelength range 190-400 nm.

## Comments on Preferred Values

Since our previous evaluation, IUPAC 1997,7 Wang and Zhang8 have measured the absorption cross-sections at 352.2 nm, 354.2 nm and 357.0 nm and there have been three other new determinations by Stutz et al.,9 Pagsberg et al.,10 and Brust et al.,11 of the absorption cross-sections over a range of wavelengths in the 300-400 nm range. The results of Wang and Zhang,8 Stutz et al.9 and Pagsberg et al.10 are in good agreement but the values obtained by Brust et al.11 are much lower. The reason for this discrepancy is not clear.

The studies of Wang and Zhang,8 Stutz et al.,9 and Pagsberg et al.10 are also in agreement with the earlier studies of Stockwell and Calvert,12 Vasudev,13 and Bongartz et al.2,3 which were the basis of the preferred values for the absorption cross-section given in our previous evaluation, IUPAC, 1997,7 which are therefore unchanged. The preferred values of the cross-sections tabulated for the 300-395 nm range are obtained from the data of Bongartz et al.2,3 In their later work,3 cross-sections were measured under better controlled conditions than in their earlier study2 and it was shown that their earlier data were consistently too high by, on average, 14.5%. The preferred values have been obtained, therefore, by averaging the data from Ref. 2 over 5 nm intervals centred on the wavelength specified in the Table and reducing these values by 14.5% as directed in Ref. 3.

The HONO spectrum consists of a diffuse structured band between 300 and 390 nm and a broad structureless band from 270 nm to below 180 nm, peaking at ~210 nm. The only direct determination of the (HO) in this region is that of Cox and Derwent4 who showed that channel (1) is the dominant process between 330 nm and 380 nm and obtained a quantum yield for HO production of 0.92  0.16 at 365 nm. There is some indirect evidence for H atom production at ~ 350 nm14 but Wollenhaupt et al.5 have shown (H) to be less than 0.01. We therefore take (HO) to be unity throughout this band.

In the second absorption band, cross-sections over the range 185-275 nm are based on the data of Kenner et al.,1 which show that channel (1) is the main photodissociation channel in this region also, but minor H atom producing channels in the 193.3 nm photodissociation of a beam of jet-cooled HONO15 have also been observed.

# References

1	R. D. Kenner, F. Rohrer, and F. Stuhl, J. Phys. Chem. 90, 2635 (1986).

2	A. Bongartz, J. Kames, F. Welter, and U. Schurath, J. Phys. Chem. 95, 1076 (1991).

3	A. Bongartz, J. Kames, U. Schurath, Ch. George, Ph. Mirabel, and J. L. Ponche, J. Atmos. Chem. 18, 149 (1994).

4	R. A. Cox and R. G. Derwent, J. Photochem. 6, 23 (1976/77).

5	M. Wollenhaupt, S. A. Carl, A. Horowitz, and J. N. Crowley, J. Phys. Chem. A 104, 2695 (2000).

6	R. A. Cox, J. Photochem. 3, 175 (1974).

7	IUPAC, Supplement VI, 1997 (see references in Introduction).

8	L. Wang and J. Zhang, Env. Sci. Technol. 34, 4221 (2000).

9	J. Stutz, E. S. Kim, U. Platt, P. Bruno, C. Perrino, and A. Febo, J. Geophys. Res. 105,14585 (2000).

10 	P. E. Pagsberg, E. Bjerbakke, E. Ratajczak, and A. Sillesen, Chem. Phys. Lett. 272, 383 (1997).

11	A. S. Brust, K. H. Becker, J. E. Kleffman, and P. Wiesen, Atmos. Environ. 34, 13 (2000).

12	W. R. Stockwell and J. G. Calvert, J. Photochem. 8, 175 (1978).

13	R. Vasudev, Geophys. Res. Lett. 17, 2153 (1990).

14	J. Burkholder, A. Mellouki, R. Talukdar, and A. R. Ravishankara, Int. J. Chem. Kinet. 24, 711 (1992).

15	G. Amaral, K. Xu, and J. Zhang, J. Phys. Chem. A 105, 1465 (2001).