# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet ROO_44

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: June 2011; last change in preferred values: June 2011.

2 CH3CH(OH)CH(O2)CH3  CH3CH(OH)CH(O)CH3 + CH3CH(OH)CH(O)CH3 + O2	(1)

 CH3CH(OH)C(O)CH3 + CH3CH(OH)CH(OH)CH3 + O2	(2)

Rate coefficient data (k = k1 + k2)

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| kobs = (8.8 ± 1.0) x 10-13 | 298 | Jenkin and Hayman, 1995 | MM-UVA (a,b) |
| kobs = (7.9 ± 0.7) x 10-13 | 296 |  | PLP-UVA (a,b) |
| (6.79 ± 0.41) x 10-13 | 303 | Boyd and Lesclaux, 1997 | PLP-UVA (a,c) |
| 7.7 x 10-15 exp[(1330 ± 350)/T] | 303-421 |  |  |
| Branching Ratios |  |  |  |
| k1/k2 = 4.0 x 104 exp[(3600 ± 100)/T] | 303-421 | Boyd and Lesclaux, 1997 | PLP-UVA (a,c) |

## Comments

(a)	k is defined by –d[CH3CH(OH)CH(O2)CH3]/dt = 2k [CH3CH(OH)CH(O2)CH3]2. kobs denotes an upper limit rate coefficient derived from an experimentally observed decay without correction for probable secondary removal of CH3CH(OH)CH(O2)CH3.

(b)	CH3CH(OH)CH(O2)CH3 generated from the photolysis of H2O2-but-2-ene-O2-N2 mixtures at 1 bar (750 Torr), at 254 nm (in the MM experiments) or 248 nm (in the PLP experiments). Absorption spectrum characterised over the wavelength range 210-300 nm. kobs determined from transient decay traces recorded at 250 nm, which were found to obey second order kinetics.

(c)	CH3CH(OH)CH(O2)CH3 generated from the 248 nm photolysis of H2O2-but-2-ene-O2-N2 mixtures at 1013 mbar (760 Torr). The kinetics and branching ratios were determined from simulation of the transient decay traces recorded at 220 nm and 270 (or 280) nm. Quantification of the branching ratio was found to be sensitive to the deviation from second order kinetics and to a distortion to the trace at 220 nm, which results from an additional absorption due to HO2 formation from propagating channel (1). No detectable deviation from second order kinetics was observed at 303 K, consistent with k1/k <0.3; but increasing with temperature such that k1/k = (0.88  0.10) at 421 K. Expression for k1/k determined from higher temperature data, and extrapolated to allow analysis of the data obtained at 303 K.

#### Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| k/cm3 molecule-1 s-1 | 6.7 x 10-13 | 298 |
| k/cm3 molecule-1 s-1 | 7.7 x 10-15 exp(1330/T) | 298 - 420 |
| k1/k | 0.18 | 298 |
| k2/k | 0.82 | 298 |
| k1/k | 1/[1+ 2.5 x 10-5 exp(3600/T)] | 298 - 420 |
| k2/k | 1-(k1/k) | 298 - 420 |

Reliability

|  log k | ± 0.2 | 298 - 400 |
| --- | --- | --- |
|  E/R | ± 300 K |  |
|  k1/k | ± 0.15 | 298 |
|  k2/k | ± 0.15 | 298 |
| (E1/R – E/R) | ± 500 K |  |

Comments on Preferred Values

The preferred values of k and the branching ratios are based on the temperature dependence expressions of Boyd and Lesclaux (1997). The room temperature values of kobs reported by Jenkin and Hayman (1995) also agree well with the preferred value at 298 K, when corrected for secondary removal of CH3CH(OH)CH(O2)CH3 via reaction with HO2, using the conventional expression, kobs = (1+(k1/k))k. Additional studies are required to confirm the magnitude of the temperature dependence of the reaction.

The API-MS study of Tuazon et al. (1998) reported formation of the hydroxycarbonyl, CH3CH(OH)C(O)CH3, and the dihydroxyalkane, CH3CH(OH)CH(OH)CH3, during the HO initiated oxidation of cis-but-2-ene and trans-but-2-ene in the absence of NOx (at 297 K and 986 mbar) attributed to the operation of reaction channel (2). The formation of the hydroxyhydroperoxide, CH3CH(OH)CH(OH)CH3, was also observed and attributed to the secondary reaction of CH3CH(OH)CH(O2)CH3 with HO2, formed from the subsequent chemistry of  CH3CH(OH)CH(O)CH3 produced in reaction channel (1). Further quantitative product studies are required to confirm, and reduce the uncertainties on, the preferred branching ratios.

#### References

Boyd, A.A. and Lesclaux, R.: Int J Chem Kinet., 29, 323, 1997.

Jenkin, M. E. and Hayman, G. D.: J. Chem. Soc. Faraday Trans., 91, 1911, 1995.

Tuazon, E.C., Aschmann, S.M., Arey, J. and Atkinson, R.: Environ. Sci. Technol., 32, 2106, 1998.