# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet II.A6.128 ROO_9

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this datasheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This datasheet last evaluated: 4th June 2009. Last change in preferred values: 12th June 2003.

CH3O2 + NO2 +M  CH3O2NO2 + M

H° = -92.7 kJ·mol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (2.33 ± 0.08) x 10-30 [N2] | 298 | Sander and Watson, 19801 | FP-AS (a) |
| 2.2 x 10-30 (T/300)-2.5 [N2] | 253-353 | Ravishankara, Eisele, and Wine, 19802 | FP-AS (b) |
| (1.46  0.50) x 10-30 [SF6] | 295 | Wallington, Nielsen, and Sehested, 19993 | (c) |

## Comments

(a)	Pressure range 70 mbar to 900 mbar for the bath gases He, N2, and SF6. Analysis of the falloff curve was carried out with a theoretical Fc value of 0.39, in good agreement with the fitted value of Fc = 0.4 ± 0.10.

(b)	Pressure range 100 mbar to 950 mbar. Analyses of the falloff curves at 253 K, 298 K and 353 K were carried out with Fc = 0.4 independent of temperature.

(c)	Pulse radiolysis study in 0.5-14 bar of SF6. Evaluating of the falloff curve with Fc = 0.40.

Preferred Values

k0 = 2.5 x 10-30 (T/300)-5.5 [N2] cm3 molecule-1 s-1, over the temperature range 250 to 350 K.

Reliability

log k0 = ± 0.3 at 298 K.

n = ± 1.

Comments on Preferred Values

The preferred values are based on the results from refs. 1 and the theoretical analysis from ref. 4. These values are based on a theoretically determined value of Fc = 0.36 at 300 K.

### High-pressure rate coefficients

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (8.0 ± 1.0) x 10 -12 | 298 | Sander and Watson, 19801 | FP-AS (a) |
| 7 x 10-12 (T/298) -3.5 | 253-353 | Ravishankara, Eisele, and Wine, 19802 | FP-AS (b) |
| (1.8  0.25) x 10-11 | 295 | Wallington, Nielsen, and Sehested, 19993 | (c) |

Comments

(a)	See comment (a) for k0.

(b)	See comment (b) for k0. The large negative temperature coefficient is probably an artifact of the interpretation. If a larger negative temperature exponent for k0 and a smaller Fc value at higher temperature are used, the large negative temperature exponent of k will decrease.

(c)	See comment (c) for k0.

Preferred Values

k = 4.0 x 10-12 cm3 molecule-1 s-1 at 298 K and 1 bar of air.

k = 1.8 x 10-11 cm3 molecule-1 s-1, independent of temperature over the range 250 to 350 K.

Reliability

log k =  0.3 at 298 K.

n = ± 0.5.

Comments on Preferred Values

The preferred values are based on the high pressure study from ref. 3. An experimental value of Fc = 0.36 at 298 K appears well established. Less complete information on the falloff range is obtained from the experiments by Cox and Tyndall,5 who measured k = 1.6 x 10-12 cm3 molecule-1 s-1 at 700 mbar of N2 and 1.2 x 10-12 cm3 molecule-1 s-1 at 66 mbar of Ar at 275 K, and Bridier, Lesclaux, and Veyret6 who measured k = 4.4 ( 0.4) x 10-12 cm3 molecule-1 s-1 at 298 K in 1 bar of air. The apparent observation of a pressure independent rate coefficient k over the range 66 mbar to 760 mbar of Ar, reported by Adachi and Basco,7 is not confirmed by refs. 1 and 2. H is taken from the equilibrium measurements of ref. 6.

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((2.5e-30*(T/300)^-5.5)*M*(1.8e-11))/((2.5e-30*(T/300)^-5.5)*M+(1.8e-11))*10^(log10(0.36)/(1+(log10((2.5e-30*(T/300)^-5.5)*M/(1.8e-11))/(0.75-1.27*log10(0.36)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

References

- S. P. Sander and R. T. Watson, J. Phys. Chem. 84, 1664 (1980).

- A. R. Ravishankara, F. L. Eisele, and P. H. Wine, J. Chem. Phys. 73, 3743 (1980).

- T. J. Wallington, O. J. Nielsen, and K. Sehested, Chem. Phys. Lett. 313, 456 (1999).

- M. Destriau and J. Troe, Int. J. Chem. Kinet. 22, 915 (1990).

- R. A. Cox and G. S. Tyndall, J. Chem. Soc. Faraday Trans. 2, 76, 153 (1980).

- I. Bridier, R. Lesclaux, and B. Veyret, Chem. Phys. Lett. 119, 259 (1992).

- H. Adachi and N. Basco, Int. J. Chem. Kinet. 12, 1 (1980).