# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet II.A5.110 RO_11

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this datasheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This datasheet last evaluated: June 2009. Last change in preferred values: March 2005.

CH3O + NO + M  CH3ONO + M	(1)

CH3O + NO  HCHO + HNO	(2)

H°(1) = -172.7 kJ·mol-1

H°(2) = -103.1 kJ·mol-1

### Low-pressure rate coefficients

Rate coefficient data

| k01/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 1.35 x 10-29 (T/298)-3.8 [Ar] | 296-573 | Frost and Smith, 1990 | PLF-LIF (a) |
| 1.8 x 10-29 (T/300)-3.2 [Ar] | 220-473 | McCaulley et al., 1990 | DF-LIF (b) |
| (4.8  0.4) x 10-12 (k2) | 298 | Daële et al., 1995 | DF-LIF (c) |
| 2.65 x 10-29 (T/298)-2.8 [He,Ar] | 248-473 | Caralp et al., 1998 | DF/PLP-LIF (d) |
| 1.25 x 10-11 exp(-1015/T) + 1.92 x 10-12 (T/298)-2.56 (k2) |  |  |  |

Comments

(a)	Rate coefficients measured up to 165 mbar of Ar or CF4 diluent. Evaluation of the chemical activation system CH3O + NO  CH3ONO*, CH3ONO* + M  CH3ONO + M, and CH3ONO*  HCHO + HNO carried out using an extended Lindemann-Hinshelwood mechanism. At low pressures the disproportionation reaction CH3O + NO  HCHO + HNO dominates (k2 = 5.0 x 10-12 (T/298)-0.6 cm3 molecule-1 s-1). Assuming that reactions (1) and (2) involve the same intermediate complex, k2 is expected to decrease with increasing pressure.

(b)	Measurements over the pressure range 1-6.6 mbar in He or Ar. The disproportionation reaction CH3O + NO  HCHO + HNO was measured by molecular beam MS (k2 = 1.3 x 10-12 exp(250/T) cm3 molecule-1 s-1).

(c)	Analysis by LIF and mass spectrometry. Experiments at 298 K and 1.3 mbar of He.

(d)	Two sets of experiments, using DF over the range 0.6-7 mbar and 248-473 K, or PLP over the range 39-658 mbar and 284-364 K. Results with the bath gases He (mostly used) and Ar (some experiments) essentially agreed. Extensive RRKM modelling allowed to separate k1 and k2. Falloff curves for k1 evaluated with Fc = exp(-T/900). The overall rate constant is assumed to be of the form k = k1([M]) + k2.

Preferred Values

k01 = 2.6 x 10-29 (T/300)-2.8 [N2] cm3 molecule-1 s-1 over the temperature range 200-400 K.

k2 = 2.3 x 10-12 (T/300)-0.7 cm3 molecule-1 s-1 over the temperature range 200-300 K.

Reliability

log k01 = ± 0.1 at 298 K.

n = ± 0.5.

log k2 =  0.2 at 298 K.

Comments on Preferred Values

The preferred values are based on the extensive work by Caralp et al. (1998) which includes and supersedes the earlier results from Frost and Smith (1990), McCaulley et al., 1990, Daële et al., 1995 as well as by Ohmori et al. (1993) in the middle of the falloff curve. The results are represented in the form of k = k1([M]) + k2, where k1(M) is based on k01 such as preferred here, k1 such as given below and Fc = exp(-T/900) for M = He, Ar and N2. It remains to be investigated whether k2 decreases with increasing pressure (common intermediate of reactions (1) and (2)) or is pressure independent (direct reaction (2)).

High-pressure rate coefficients

Rate coefficient data

| k1/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 2.1 x 10-11 | 440-473 | Batt, Milne and McCulloch, 1977 | (a) |
| (2.08 ± 0.12) x 10-11 | 298 | Sanders et al., 1980 | (b) |
| 1.4 x 10-11 | 298 | Zellner, 1987 | PLP-AS (c) |
| 3.6 x 10-11 (T/298)-0.6 | 296-573 | Frost and Smith, 1990 | PLF-LIF (d) |
| (2.45 ± 0.31) x 10-11 | 300 | Dóbé et al. 1994 | DF-LIF (e) |
| 3.26 x 10-11 (T/298)-0.6 | 248-473 | Caralp et al., 1998 | PLP-LIF (f) |

Comments

(a)	Thermal decomposition of methyl nitrite in the presence of NO and (CH3)3CH. Combination of these data with the equilibrium constant gives the value indicated. For the second channel, k(CH3O + NO  CH2O + HNO)/k(CH3O + NO  CH3ONO) = 0.17 was estimated.

(b)	Photolysis of methyl nitrite at 266 nm with CH3O detection by LIF at He pressure of 13-66 mbar. HNO as a reaction product was also detected by LIF; however, no absolute estimate of its yield could be made.

(c)	Falloff curve was measured over the range 5-500 mbar. Extrapolations carried out using Fc = 0.6.

(d)	See comment (a) for k0.

(e)	CH3O radicals and HCHO from reaction (2) detected by LIF. The branching ratio for HCHO formation varied between 0.84 and 0.26 over the pressure range 1-11 mbar.

(f)	See comment (d) for k0.

Preferred Values

k1 = 3.3 x 10-11 (T/300)-0.6 cm3 molecule-1 s-1 over the temperature range 200-400 K.

Reliability

log k1 = ±0.5 at 298 K.

n = ±0.5.

Comments on Preferred Values

The recommended value is from the most extensive study by Caralp et al. (1998) which supersedes and includes earlier work. The results are in accord with an RRKM modelling of the chemical activation system. Batt (1987) cites a rate coefficient ratio of k2/k <0.05 from a study at 433-473 K, consistent with our preferred values.

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((2.6e-29*(T/300)^-2.8)*M*(3.3e-11*(T/300)^-0.6))/((2.6e-29*(T/300)^-2.8)*M+(3.3e-11*(T/300)^-0.6))*10^(log10((exp(-T/900)))/(1+(log10((2.6e-29*(T/300)^-2.8)*M/(3.3e-11*(T/300)^-0.6))/(0.75-1.27*log10((exp(-T/900)))))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

References

Batt, L., Milne, R. T. and McCulloch, R. D.: Int. J. Chem. Kinet., 9, 567, 1977.

Batt, L.: Int. Rev. Phys. Chem., 6, 53, 1987.

Caralp, F., Rayez, M.-Th., Forst, W., Gomez, N., Delcroix, B., Fittschen, C. and Devolder, P.: J. Chem. Soc. Faraday Trans., 94, 3321, 1998.

Daële, V., Laverdet, G., LeBras, G. and Poulet, G.: J. Phys. Chem., 99, 1470, 1995.

Dóbé, S., Lendvay, G., Szilagyi, I. and Bérces, T.: Int. J. Chem. Kinet., 26, 887, 1994.

Frost, M. J. and Smith, I. W. M.: J. Chem. Soc. Faraday Trans., 86, 1757, 1990.

McCaulley, J. A., Moyle, A. M., Golde, M. F., Anderson, S. M. and Kaufman, F.: J. Chem. Soc. Faraday Trans., 86, 4001, 1990.

Ohmori, K., Yamasaki, K. and Matsui, H.: Bull. Chem. Soc. Jpn., 66, 51, 1993.

Sanders, N., Butler, J. E., Pasternack, L. R. and McDonald, J. R.: Chem. Phys., 48, 203, 1980.

Zellner, R.: J. Chim. Phys., 84, 403, 1987.