IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet I.A4.86 SOx15

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this data sheet is: Atkinson, R., Baulch, D. L., Cox, R. A., Crowley, J. N., Hampson, R. F., Hynes, R. G., Jenkin, M. E., Rossi, M. J., and Troe, J.: Atmos. Chem. Phys. 4, 1461, 2004; IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This data sheet last evaluated: Nov. 2017; last change in preferred values: Nov. 2017.

HO + SO2 + M  HOSO2 + M

H = -125 kJ·mol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (2.54 ± 0.33) x 10-31 [N2] | 298 | Leu, 1982 | DF-RF (a) |
| 1.6 x 10-31 [N2] | 297 | Paraskevopoulos et al., 1983 | FP-RA (b) |
| 5.8 x 10-31 (T/300)-2.6 [N2] | 260-420 | Wine et al., 1984 | FP-RF (c) |
| (2.4 ± 0.7) x 10-31 [N2] 1.1x 10-30 (T/298)-3.62 [N2] | 298 200-600 | Lee et al., 1990 Blitz et al., 2017b | DF-RF (d) LP-LIF (e) |

Comments

(a)	Pressure range 0.9-4.0 Torr. Temperature dependence measured for M = He over the range 261-414 K and the pressure range 0.9-10 Torr, leading to k0 = (7.910.4) x 10-32 (T/298)-2.85 [He] cm3 molecule-1 s-1. Experiments with M = He, Ar, N2, O2, CO2, and SO2. Falloff representation with Fc = 1 responsible for low values of k0 and k.

(b)	Pressure range 55-760 Torr. Falloff representation with Fc = 1 responsible for too low values of k0 and k.

(c)	Pressure range 13-696 Torr, bath gases He, Ar, N2, and SF6. Falloff representation with Fc = exp(-T/388), corresponding to Fc = 0.46 at 300 K.

(d)	Pressure range 0.6-45 Torr, bath gases He, N2, and SO2. Falloff representation with Fc = 1 responsible for too low values of k0 and k.

(e)   HO produced by two-photon photolysis of SO2 at 248 nm, generating O(1D) which reacts with H2. Pressure range 25-300 Torr He. Falloff curve at 298 K fitted with Fc = 0.13. The value of k(1 bar) = 5.8 x 10-31 cm3 molecule s-1 at 298 K is lower than the preferred value by about a factor of 0.7. The discrepancy is suggested to be due to the neglect of two-photon photolysis of SO2 in earlier studies from other laboratories. The derived large value of k0 is a consequence of the use of a markedly smaller Fc than employed in earlier falloff representations. The parameters listed in the table were obtained via fitting to simulated data using k(T) = (7.8 ± 2.2) × 10−13(T/298)0.1 cm3 molecule−1 s−1 and ⟨ΔEdown⟩(N2)/cm−1 = 600 × (T/298)0.3.

Preferred Values

k0 = 2.8 x 10-31 (T/300)-2.6 [N2] cm3 molecule-1 s-1 over the temperature range 200-400 K.

Comments on Preferred Values

Work published before 1980 has been discussed in Fulle et al. (1999) and is not shown here. The preferred value at 300 K is based on the low pressure results from Leu (1982) and Lee et al. (1990); the temperature coefficient is from Wine et al. (1984). Falloff curves with Fc = 0.53 and k = 2 x 10-12 cm3 molecule-1 s-1 from Fulle et al. (1999) give k(1bar) in good agreement with data from Pavaskevopoulos et al. (1983), Wine et al. (1984), Harris et al. (1980), Izumi et al. (1984), Barnes et al. (1986), and Martin et al. (1986). The data from Blitz et al. (2017b) at 100 Torr of He within the error limits are consistent with earlier results.

High-pressure rate coefficients

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 1.2 x 10-12 | 297 | Pavaskevopoulos et al., 1983 | FP-RA (a) |
| 1.26 x 10-12 (T/300)-0.7 | 260-420 | Wine et al.,1984 | FP-RF (b) |
| 1.2 x 10-11 exp(-360/T) | 220-400 | Fulle et al., 1999 | LP-LIF(c) |
| 3.6 x 10-12 | 300 |  |  |
| (2.040.10) x 10-12 (T/300)-0.27 (7.2x 10-13 | 295-673 295-810 | Blitz et al., 2003 Blitz et al., 2017a | LP-LIF (d) LP-LIF (e) |

Comments

(a)	See comment (b) for k0.

(b)	See comment (c) for k0.

(c)	Measurements in the pressure range 1-96 bar of He. Detailed analysis of earlier work and of full falloff curves.

(d)	Studies of vibrational relaxation OH(v=1) + SO2 as well as OH + SO2 + M in the pressure range 100-200 Torr of He at 295, 373, and 473 K.

(e)  Studies of vibrational relaxation HO(v=1, 2, 3) + SO2 in He. Presence of a weakly bound complex OH-OSO* prior to adduct formation suggested. Evaluation of the composite mechanism leads to k

Preferred Values

k = 2.0 x 10-12 cm3 molecule-1 s-1 over the temperature range 200-400 K.

Comments on Preferred Values

The direct derivation of k from the high pressure falloff curves by Fulle et al. (1999) gives larger values than the vibrational relaxation results from Blitz et al. (2003, 2017a). This may be explained by the formation of an OH-OSO* pre-reaction complex with different redissociation to OH + SO2 in recombination and vibrational relaxation experiments. Inspecting the data from Fulle et al. (1999) and taking into account that asymmetric broadening of the falloff curves like for OH + NO2 + M may have been present, one may conclude that the difference to the values from Blitz et al. (2003, 2017a) is not large. Theoretical studies of the reaction and its potential by Somnitz (2004) and Glowacki et al. (2009) so far appear inconclusive with respect to the temperature dependence of k, but a very weak temperature dependence has been fitted by Blitz et al. (2017b). The preferred value is a compromise between the direct data from Fulle et al. (1999), extending to high pressures, and the less direct data from Blitz et al. (2017a) using vibrational relaxation of HO by SO2 as a proxy. Falloff curves here are represented with Fc = exp(-T/472), corresponding to Fc = 0.53 at 300 K from Fulle et al. (1999).

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| k0/cm3 molecule-1 s-1 | 2.8 x 10-31 [N2] | 298 |
| k0/cm3 molecule-1 s-1 | 2.8 x 10-31 (T/300)-2.6 [N2] | 250-300 |
| k/cm3 molecule-1 s-1 | 2.0 x 10-12 | 298 |
| k/cm3 molecule-1 s-1 | 2.0 x 10-12 | 250-300 |
| k(1 bar N2)/cm3 molecule-1 s-1 | 9.3 x 10-13 | 298 |
| Fc | exp(-T/472) 0.53 | 250-400 298 |
| Reliability |  |  |
| log k0 | ± 0.3 | 298 |
| n0 | ± 1 | 250-300 |
| log k | ± 0.3 | 298 |
| n | ± 0.3 | 250-300 |

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((2.8e-31*(T/300)^-2.6)*M*(2.0e-12))/((2.8e-31*(T/300)^-2.6)*M+(2.0e-12))*10^(log10(EXP(-T/472))/(1+(log10((2.8e-31* (T/300)^-2.6)*M/(2.0e-12))/(0.75-1.27*log10(EXP(-T/472))))^2))

The molecular density, M = 7.2431021P(bar) / T(K)

References

Barnes, I., Bastian, V., Becker, K. H., Fink, E. H., and Nelson,W.: J. Atmos. Chem. 4,445, 1986.

Blitz, M. A., Hughes, K. J., and Pilling, M. J.: J. Phys. Chem. A. 107, 1971, 2003.

Blitz, M. A., Salter, R. J., Heard, D. E., and Seakins, P. W.: J. Phys. Chem. A 121, 3175, 2017(a).

Blitz, M. A., Salter, R. J., Heard, D. E., and Seakins, P. W.: J. Phys. Chem. A 121, 3184, 2017(b).

Fulle, D., Hamann, H. F., and Hippler, H.: Phys. Chem. Chem. Phys. 1, 2695, 1999.

Glowacki, D.R., Reed, S. K., Pilling, M. J., Shalashilin, D. V., and Martinez-Núñez, E.: Phys. Chem.Chem. Phys. 11, 863, 2009.

Harris, G.W., Atkinson, P. R., and Pitts, J. N.: Chem. Phys. Lett. 69, 378, 1980.

Izumi, K., Mizuochi, M., Yoshioka, M., Murano, K., and Fukuyama, T.: Environ. Sci. Technology 18, 116, 1984.

Lee, Y.Y., Kao, W.C., and Lee, Y. P.: J. Phys. Chem. 94, 4535, 1990.

Leu, M. T.: J. Phys. Chem. 86, 4558, 1982.

Martin, D., Jourdain, J. L., and LeBras, G.: J. Phys. Chem. 90, 4143, 1986.

Paraskevopoulos, G., Singleton, D. L., and Irvin, R. S.: Chem. Phys. Lett. 100, 83, 1983

Somnitz, H.: Phys. Chem. Chem. Phys. 6, 3844, 2004.

Wine, P. H., Thompson, R. J., Ravishankara, A.R., Semmes, D. H., Gump, C. A., Tarabi, A., and

Nicovich, J. M.: J. Phys. Chem. 88, 2094, 1984.

# Text boxes

Rate coefficients for OH + SO2 in N2 at 298 K and the IUPAC preferred values (solid line)