IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet SOx59

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this data sheet is: Atkinson, R., Baulch, D. L., Cox, R. A., Crowley, J. N., Hampson, R. F., Hynes, R. G., Jenkin, M. E., Rossi, M. J., and Troe, J.: Atmos. Chem. Phys. 4, 1461, 2004; IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This data sheet last evaluated: November 2017; last change in preferred values: November 2001.

CH3S + NO + M  CH3SNO + M

Low-pressure rate coefficients

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (3.24 ± 0.36) x 10-29 [N2] | 295 | Balla et al., 1986 | (a) |
| (1.43 ± 0.36) x 10-29 [N2] | 351 |  |  |
| (1.13 ± 0.20) x 10-29 [N2] | 397 |  |  |
| (5.84 ± 0.66) x 10-30 [N2] | 453 |  |  |

## Comments

(a)	Pulsed laser photolysis of (CH3S)2-NO-N2 (or SF6) mixtures at 266 nm, with CH3S being monitored by LIF.  Lower part of the falloff curves were measured over the pressure range 2-400 mbar (1.5-300 Torr) of N2.  Falloff extrapolations were carried out with fitted values of Fc of 0.6, 0.86, 0.77, and 0.94 at 295, 351, 397, and 453 K, respectively.

## Preferred Values

k0 = 3.3 x 10-29 (T/300)-4 [N2] cm3 molecule-1 s-1 over the temperature range 290-450 K. This value was obtained by fitting to the pressure and temperature dependent data in N2 using a temperature independent values of Fc = 0.54 and  k derived from data in SF6 (see below).

Reliability

log k0 = 0.3 at 298 K.

n = ±2.

Comments on Preferred Values

The preferred values are based on the data of Balla et al.(1986).  A further determination in N2 at a single temperature and pressure (298 K and 25 Torr) by Turnipseed et al. (1986) is in good agreement. Although the falloff extrapolations of Balla et al. (1986) were made with a theoretically improbable temperature coefficient of Fc, the low-pressure rate coefficients are much less influenced by this extrapolation than the high-pressure rate coefficients.

High-pressure rate coefficients

## Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 1.81 x 10-12 exp(900/T) | 295-453 | Balla et al., 1986 | (a) |
| (3.97  0.44) x 10-11 in 300 Torr SF6 | 295 |  |  |

Comments

(a)	See comment (a) for k0.  The high-pressure limit was obtained from measurements at 267 and 400 mbar (200 and 300 Torr) of SF6.

## Preferred Values

k = 4.0 x 10-11 cm3 molecule-1 s-1, independent of temperature over the range 290-450 K.

Reliability

log k = ±0.5 over the temperature range 290-450 K.

Comments on Preferred Values

The negative temperature coefficient of k reported by Balla et al. (1986) is most probably due to an increasing underestimate of the falloff corrections with increasing temperature.  We recommend the use of the extrapolated k value at 298 K over large temperature ranges together with Fc = 0.54. Along with the values recommended for k0 above, this parameterisation accurately reproduces all the data in N2.

Intermediate Falloff Range

## Rate coefficient data

| k/cm3 molecule-1 s-1 | P/mbar | M | Temp./K | Reference | Comments |
| --- | --- | --- | --- | --- | --- |
| (1.69 ± 0.04) x 10-11 | 28 | He | 227 | Turnipseed et al., 1993 |  |
| (1.30 ± 0.09) x 10-11 | 25 | He | 242 |  | (a) |
| (1.89 ± 0.08) x 1011 | 25 | He | 242 |  |  |

## Comments

(a)	CH3S radicals were generated by either photolysis of dimethyl sulfide at 193 nm or photolysis of dimethyl disulfide at 248 nm.  The decay of CH3S radical concentrations was followed by LIF.  Experiments were performed under slow gas flow conditions.

## References

Balla, R. J., Nelson, H. H., and McDonald, J. R.:Chem. Phys. 109, 101, 1986.

Turnipseed, A. A., Barone, S. B., and Ravishankara, A. R.: J. Phys. Chem. 97, 5926, 1993.

Turnipseed, A. A., Barone, S. B., and  Ravishankara, A. R.: J. Phys. Chem. 100, 14703, 1996.