# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet iClOx30

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be re-transmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet updated: 25th September 2003.

ClO + O3  ClOO + O2	(1)

 OClO + O2	(2)

H°(1) = -146.8 kJ·mol-1

H°(2) = -149.7 kJ·mol-1

Rate coefficient data (k = k1 + k2)

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| k2 <1 x 10-18 | 298 | DeMore et al., 1975 | DF-MS |
| k2 <1 x 10-18 | 298 | Wongdontri-Stuper et al., 1979 | FP-UVA (a) |
| k1 <1.3 x 10-17 | 233 | Stevens and Anderson, 1990 | (b) |
| k1 <1.4 x 10-17 | 298 |  |  |
| k1 = (4.0 ± 2.0) x 10-16 | 413 |  |  |

# Comments

(a)	Flash photolysis of Cl2-O3 mixtures.  Upper limit to the rate coefficient obtained expected to really refer to k2 (Stevens and Anderson, 1990).

(b)	Discharge flow system.  Reaction channel (1) was followed by monitoring ClO produced from the thermal decomposition of the product ClOO in the presence of O3. The product ClO was distinguished from the reactant ClO through isotopic labelling.

# Preferred Values

k1 <1.5 x 10-17 cm3 molecule-1 s-1 at 298 K.

k2 <1 x 10-18 cm3 molecule-1 s-1 at 298 K.

Comments on Preferred Values

The preferred upper limit for k1 is based on the results of the study of Stevens and Anderson (1990). The preferred upper limit for k2 is based on the data of DeMore et al. (1975) and Wongdontri-Stuper et al. (1979). The upper limit of Stevens and Anderson (1990) at room temperature can be combined with their measured rate coefficient at 413 K to derive A1 = 2 x 10-12 cm3 molecule-1 s-1 and E1/R > 3600 K.  For k2 one can estimate A2 = 1 x 10-12 cm3 molecule-1 s-1 and derive E2/R > 4000 K.

# References

DeMore, W. B., Lin, C. L. and Jaffe, S.: presented at ACS National Meeting, Philadelphia, PA, 1975.

Stevens, P. S. and Anderson, J. G.: Geophys. Res. Lett. 17, 1287, 1990.

Wongdontri-Stuper, W., Jayanty, R. K. M., Simonaitis, R. and Heicklen, J.: J. Photochem. 10, 163, 1979.