# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet III.A4.97 iIOx19

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This datasheet last evaluated: 9th March 2005.

IO + NO2 + M  products

H° = -79 kJmol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (4.3 ± 2.0) x 10-31 [N2] | 277 | Jenkin and Cox, 1985 | MM-A (a) |
| 7.7 x 10-31 (T/300)-5.0 [N2] | 254-354 | Daykin and Wine, 1990 | PLP-A (b) |
| (3.6 ± 1.0) x 10-31 [He] | 298 | Maguin et al., 1992 | DF-MS (c) |
| (7.9 ± 2.2) x 10-31 [N2] | 298 |  |  |
| (1.80 ± 0.07) x 10-31 x (T/300)-2.6 [O2] | 290-350 | Larin et al., 1998 | FR-F (d) |
| 4.1 x 10-31 (T/298)-6.3 [N2] | 238-298 | Hölscher and Zellner, 2002 | PLP-LIF (e) |
| 1.3 x 10-30 (T/300)-4.5 [N2] | 216-474 | Allan and Plane, 2002 | PLP-LIF (f) |

Comments

(a)	Photolysis of I2 in the presence of O3 producing IO radicals monitored by absorption at 427 nm in the presence of an excess of NO2.  The total pressure was varied over the range 47-537 mbar of N2.  The falloff curve was analyzed using Fc = 0.4 by analogy to the BrO + NO2 + M reaction.  A small correction was made for a second-order component to the IO radical kinetics at higher pressures.

(b)	IO radicals generated by pulsed laser photolysis of I2-NO2-N2 mixtures at 351 nm; IO radicals monitored by absorption at 427 nm.  Pressure range 53-1000 mbar.  The data were extrapolated to the low- and high-pressure rate coefficients using Fc = 0.4.

(c)	IO radicals and IONO2 detected by MS.  IO radicals were generated by the reaction O + I2  IO + I.  The pressure range was 1.6-2.8 mbar of He.  Using a relative third-body efficiency of N2 and He for the analogous BrO + NO2 + M (ratio k0(N2)/k0(He) = 2.2) from Sander et al. (1981), the value reported above was derived.

(d)	I atoms generated by photolysis of a flow of CH3I at 254 nm; IO radicals formed by the reaction I + O3  IO + O2.  Pressure range 1.3-8 mbar of O2.  Assuming a ratio of c(N2)/c(O2) = 1.4, the expression k0 = 2.50 x 10-31 x (T/300)-2.6 [N2] cm3 molecule-1 s-1 over the temperature range 290 K to 350 K was derived.

(e)	Laser flash photolysis of mixtures of O3, CF3I and NO2 in air with pulsed LIF detection of IO. Pressure range 50-400 mbar. Evaluation of the falloff curve with Fc = 0.6. Rate coefficients about 20% below those from Daykin and Wine (1990).

(f)	Laser flash photolysis of NO2 in the presence of CF3I and N2 with LIF detection of IO. Falloff extrapolation with Fc = 0.57 obtained from RRKM theory. Rate coefficients about 20% above data from Daykin and Wine (1990). Preliminary results by Blitz et al. (2000) are cited which are close to the present results.

Preferred Values

k0 = 7.7 x 10-31 (T/300)-5 [N2] cm3 molecule-1 s-1 over the temperature range 250-360 K.

Reliability

log k0 = ± 0.3 at 298 K.

n = ± 2.

Comments on Preferred Values

The preferred values for k0 are an average of the data of Daykin and Wine (1990), the value of Maguin et al. (1992) derived with the given ratio of efficiencies for N2 and He, the data from Hölscher and Zellner (2002), extrapolated with Fc = 0.4 instead of 0.6, and the data from Allan and Plane (2002).  The measurements of Larin et al. (1998) are a factor of 4 lower than the preferred values and need to be confirmed.

High-pressure rate coefficients

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (1.6 ± 0.6) x 10-11 | 277 | Jenkin and Cox, 1985 | MM-A (a) |
| 1.55 x 10-11 | 254-354 | Daykin and Wine, 1990 | PLP-A (b) |
| 1.0 x 10-11 | 238-298 | Hölscher and Zellner, 2002 | PLP-LIF (c) |
| 6.5 x 10-12 (T/300)-1.3 | 216-474 | Allan and Plane, 2002 | PLP-LIF (d) |

Comments

(a)	See comment (a) for k0.  The rate coefficient k was obtained from a fit of the falloff curve using Fc = 0.4.

(b)	See comment (b) for k0.

(c)	See comment (e) for k0.

(d)	See comment (f) for k0.

Preferred Values

k = 1.6 x 10-11 cm3 molecule-1 s-1, independent of temperature over the range 250-360 K.

Reliability

log k = ± 0.3 over the temperature range 250-360 K.

Comments on Preferred Values

The preferred values for k are based on the data of Daykin and Wine (1990).  Falloff extrapolations are made with Fc = 0.4, independent of temperature over the range 250 to 360 K. If extrapolated with this Fc instead of Fc  0.6, the measurements by Hölscher and Zellner (2002) and Allan and Plane (2002) are consistent with the preferred k.

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((7.7e-31*(T/300)^-5)*M*(1.6e-11))/((7.7e-31*(T/300)^-5)*M+(1.6e-11))*10^(log10(0.4)/(1+(log10((7.7e-31* (T/300)^-5)*M/(1.6e-11))/(0.75-1.27*log10(0.4)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

References

Allan, B. J. and Plane, J. M. C.: J. Phys. Chem. A, 106, 8634, 2002.

Blitz, M. A., Dillon, T. J. and Heard, D. E.: 16th Int. Symp. on Gas Kinetics, Cambridge, UK, 2000.

Daykin, E. P. and Wine, P. H.: J. Phys. Chem. 94, 4528, 1990.

Hölscher, D. and Zellner, R.: Phys. Chem. Chem. Phys., 4, 1839, 2002.

Jenkin, M. E. and Cox, R. A.: J. Phys. Chem., 89, 192, 1985.

Larin, I. K., Nevozhai, D. V., Sapasskii, A. I. and Trofimova, E. M.: Kinet. Catal., 39, 666. 1998.

Maguin, F., Laverdet, G., Le Bras, G. and Poulet, G.: J. Phys. Chem., 96, 1775, 1992.

Sander, S. P., Ray, G. W. and Watson, R. T.: J. Phys. Chem., 85, 199, 1981.