# IUPAC Task Group on Atmospheric Chemical kinetic Data Evaluation – Data Sheet III.A4.85 iIOx6

Data sheets can be downloaded for personal use only and must not be re-transmitted or disseminated either electronically or in hard copy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This data sheet last evaluated: March 2005.

I + NO2 + M  INO2 + M

H° = -79.8 kJ·mol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 1.5 x 10-31 (T/300)-1 [He] | 320-450 | van den Bergh and Troe, 1976 | PLP-UVA (a) |
| 1.62 x 10-31 [He] | 330 | van den Bergh, Benoit-Guyot and Troe, 1977 | PLP-UVA (b) |
| 2.6 x 10-31 [N2] | 330 |  |  |
| (9.5 ± 3.5) x 10-32 [He] | 298 | Mellouki et al., 1989 | DF-EPR (c) |
| 3.1 x 10-31 [N2] | 298 | Buben et al., 1990 | FP-RF (d) |

Comments

(a)	Derived from the NO2 catalyzed recombination of I atoms, with I atoms being produced by photolysis of I2 at 694 nm.  The falloff curve was measured from 1 200 bar of He, and only a short extrapolation to k0 was required.

(b)	As in comment (a).  The efficiencies of 26 bath gases were studied.

(c)	Measurements performed over the pressure range 0.8 to 2.9 mbar.

(d)	I atoms generated by photolysis of CH3I in a flow system with NO2-N2 mixtures.  The bath gases N2, O2, Ar and He were studied at total pressures between 0.7 and 13 mbar.

Preferred Values

k0 = 3.0 x 10-31 (T/300)-1 [N2] cm3 molecule-1 s-1 over the temperature range 290-450 K.

Reliability

log k0 = ± 0.2 at 298 K.

n = ± 1.

Comments on Preferred Values

The preferred values are based on the results of the studies of van den Bergh and Troe (1976), van den Bergh et al. (1977) and Buben et al. (1990).  The data of Mellouki et al. (1989) for M = He are also consistent with these data  Falloff extrapolations are made with a fitted value of Fc = 0.63 from van den Bergh and Troe (1976).

High-pressure rate coefficients

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 6.6 x 10-11 | 320-350 | van den Bergh and Troe, 1976 | PLP-UVA (a) |

Comments

(a)	See comment (a) for k0.  Extrapolation of the falloff curve towards the high pressure limit uses a fitted value of Fc = 0.63.

Preferred Values

k = 6.6 x 10-11 cm3 molecule-1 s-1, independent of temperature over the range 290-450 K.

Reliability

log k = ± 0.3 over the temperature range 300-400 K.

Comments on Preferred Values

The preferred values are based on the results of the study of van den Bergh and Troe (1976). Falloff curves are represented with Fc = 0.63.

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((3.0e-31*(T/300)^-1)*M*(6.6e-11))/((3.0e-31*(T/300)^-1)*M+(6.6e-11))*10^(log10(0.63)/(1+(log10((3.0e-31*(T/300)^-1)*M/(6.6e-11))/(0.75-1.27*log10(0.63)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

References

Buben, S. N., Larin, I. K., Messineva, N. A. and Trofimova, E. M.: Kinet. Catal., 31, 854, 1990; original pages 973-977, 1990.

Mellouki, A., Laverdet, G., Jourdain, J. L. and Poulet, G.: Int. J. Chem. Kinet., 21, 1161, 1989.

van den Bergh, H. and Troe, J.: J. Chem. Phys., 64, 736, 1976.

van den Bergh, H., Benoit-Guyot, N. and Troe, J.: Int. J. Chem. Kinet., 9, 223, 1977.