# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet oBrOx14

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

This data sheet updated: 29th March 2005.

BrCH2CH2O2 + BrCH2CH2O2  BrCH2CH2OH + BrCH2CHO + O2	(1)

 2BrCH2CH2O + O2	(2)

Rate coefficient data (k = k1 + k2)

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| kobs = (6.2  1.2) x 10-12 | 298 | Crowley and Moortgat, 1992 | MM-UVA (a,b) |
| 6.15 x 10-14 exp[(1247  203)/T] | 275-373 | Villenave et al., 2003 | FP-UVA (c) |
| (4.49  0.22) x 10-12 | 298 |  |  |
| Branching Ratios |  |  |  |
| k1/k = 0.43 | 296 | Yarwood et al., 1992 | UV-P-FTIR(d) |
| k2/k = 0.57 |  |  |  |

Comments

(a)	kobs is based on the measured overall second-order decay of CH2BrCH2O2, defined by 
-d[CH2BrCH2O2]/dt = 2kobs[CH2BrCH2O2]2. As described in detail by Lesclaux (1997), HO2 radicals formed from the subsequent chemistry of CH2BrCH2O (formed from channel (2)) are expected to lead to secondary removal of CH2BrCH2O2. The true value of k is expected to fall in the range kobs/(1+)  k  kobs, where  = k2/k.

(b)	Molecular modulation study of the photolysis of Br2 in the presence of C2H4-O2-N2 mixtures at total pressures up to 800 mbar.  Modulated waveforms for the formation and removal of CH2BrCH2O2 radicals were monitored by absorption at 270 nm, i.e. where HO2 does not absorb.

(c)	Flash photolysis of Br2 in the presence of C2H4-O2-N2 mixtures at a pressure of 1013 mbar. Decays in transient absorption signals (with contributions from CH2BrCH2O2 and HO2) were recorded in the wavelength range 210 nm to 290 nm. k derived from simulations of the decay traces using an explicit reaction mechanism.

(d)	Steady-state photolysis of Br2 in the presence of C2H4-O2-N2 mixtures at 933 mbar total pressure, with FTIR spectroscopic determination of products.  The major products observed were BrCH2CHO, BrCH2CH2OH, and BrCH2CH2OOH.  The branching ratio, k2/k1 = 1.35  0.07, was determined from the yields of BrCH2CHO and BrCH2CH2OH relative to the loss of C2H4.

Preferred Values

k = 4.0 x 10-12 cm3 molecule-1 s-1 at 298 K.

k = 6.0 x 10-14 exp(1250/T) cm3 molecule-1 s-1 over the temperature range 270-380 K.

k2/k = 0.57 at 298 K.

Reliability

log k =  0.2 at 298 K.

(E/R) =  500 K.

(k1/k) = Δ(k2/k) =  0.1 at 298 K.

Comments on Preferred Values

The preferred values of k are based on the temperature dependence expression of Villenave et al. (2003), with which the earlier 298 K kobs determination of Crowley and Moortgat (1992) is entirely consistent. The preferred values of the branching ratios are based on the data of Yarwood et al. (1992), which require confirmation.

The above value of k is similar to that for the self-reaction of CH2ClCH2O2, both showing an enhancement of a factor of ca. 50 compared with the self-reaction rate coefficient for the unsubstituted analogue, C2H5O2.

References

## Crowley, J. N. and Moortgat, G. K.: J. Chem. Soc. Faraday Trans. 88, 2437, 1992.

Lesclaux, R.: Combination of peroxyl radicals in the gas phase. In ‘Peroxyl Radicals’, edited by Z.B. Alfassi. John Wiley and Sons, 1997.

## Villenave, E., Moisan, S. and Lesclaux, R.: J. Phys. Chem. A 107, 2470, 2003.

Yarwood, G., Peng, N. and Niki, H.: Int. J. Chem. Kinet. 24, 369, 1992.