# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet IV.A1.38 oFOx38

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This data sheet last evaluated: March 2005.

CF3 + O2 + M  CF3O2 + M

H = -148 kJ mol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (2.0  0.1) x 10-29 [He] | 295 | Ryan and Plumb, 1982 | DF-MS (a) |
| (1.9  0.2) x 10-29 (T/300)-4.7 [N2] | 233-373 | Caralp, Lesclaux,and Dognon, 1986 | PLP-MS (b) |
| (2.5  0.3) x 10-29 [N2] | 295 | Breheny, Hancock and Morrell, 2001 | PLP-CL(c) |

Comments

- Microwave discharge-flow system coupled to quadrupole MS. CF3 radicals monitored by MS. Measurements over the range 0.7-11 mbar, extrapolated with Fc  0.4 and k  8.0 x 10-12 cm3 molecule-1s-1.

- Pulsed laser photolysis–MS study over the range 0.3-16 mbar. Extrapolation with Fc  0.6 and k  9.0 x 10-12 cm3 molecule-1s-1.

- Pulsed laser photolysis-IR chemiluminescence study of CF3I in the presence of NO2 and O2, using IR emission from the reaction CF3 + NO2 for detection. Pressure range 2.7-150 mbar. Extrapolation with Fc  0.6 and k  2.55 x 10-12 cm3 molecule-1s-1, using data up to 800 mbar from relative rate measurements by Kaiser et al. (1995).

Preferred Values

k0 = 2.2 x 10-29 (T/300)-4.7 [N2] cm3 molecule-1 s-1 over the temperature range 230-380 K.

Reliability

log k0 =  0.1 at 298 K.

n =  1.5.

Comments on Preferred Values

The preferred values are an average of the low pressure results from Caralp et al. (1986), and Breheny et al. (2001) which appear well consistent with the measurements in He from Ryan and Plumb (1982). Differences in k and Fc, used in the extrapolation, only slightly influence the preferred k0 because all measurements extended to pressures close to the low pressure limit of k.

High-pressure rate coefficients
Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 1.0 x 10-11 | 298 | Cooper et al., 1980 | PR (a) |
| Relative Rate Coefficients |  |  |  |
| (3.92  0.25) x 10-12 | 271-363 | Kaiser, Wallington and Hurley, 1995 | PR (b) |

Comments

- Pulse radiolysis of CF3Cl. CF3O2 detected by UV absorption spectroscopy near 260 nm. Measurements in 920 mbar of Ar.

- UV irradiation of CF3I/CH4/Cl2/N2/O2 mixtures and observation of loss of CF3 and CH4. Measurement of the ratio k(CF3 + O2)/k(CF3 + Cl2) as a function of the pressure and calibration of this ratio at low pressures against k0(CF3 + O2) from Caralp et al., (1986). Inspection of the spectra recorded by Cooper et al. (1980) and comparison with more recently detected spectra of CF3O2 indicates that the rate of CF3 + O2 was not observed by Cooper et al. (1980).

Preferred Values

k = 4 x 10-12 cm3 molecule-1 s-1 over the temperature range 200-300 K.

Reliability

log k =  0.3 at 298 K.

n =  1.5.

Comments on Preferred Values

Since the measurements of Cooper et al. (1980) were shown not to lead to k, the results from the relative rate measurements from Kaiser et al. (1995) are preferred. They are similar to values for k for CCl3 + O2 from Luther et al. (2001) for which n = -1.4 was measured. Using an estimated Fc = 0.39 independent of the temperature, all results (except those from Cooper et al. (1980)) are consistently represented and the remaining uncertainty of k does not impact on k0.

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((2.2e-29*(T/300)^-4.7)*M*(4.0e-12))/( (2.2e-29*(T/300)^-4.7)*M+(4.0e-12))*10^(log10(0.39)/(1+(log10((2.2e-29*(T/300)^-4.7)*M/(4.0e-12))/(0.75-1.27*log10(0.39)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

References

Breheny, C., Hancock, G. and Morrell, C.: Z. Phys. Chem., 215, 305, 2001.

Caralp, F., Lesclaux, R. and Dognon, A. M.: Chem. Phys. Lett., 129, 433, 1986.

Cooper, R., Cumming, J. B., Gordon, S. and Mulac, W. A.: Rad. Phys. Chem., 16, 169, 1980.

Kaiser, E. W., Wallington, T. J. and Hurley, M. D.: Int. J. Chem. Kinet., 27, 205, 1995.

Luther, K., Oum, K. and Troe, J.: J. Phys. Chem. A, 105, 5535, 2001.

Ryan, K. R. and Plumb, I. C.: J. Phys. Chem., 86, 4678, 1982.